## Slide 1
Valuing Economic Benefits from
Transmission Planning
ERCOT System Planning
March 22, 2006

## Slide 2: Economic Terminology
P
S
D
Q
CS
PS
The economic value of a product is equal to the sum of the Consumer Surplus (CS) and Producer Surplus (PS). In other words, the total economic value of a product will be shared among consumers and producers. The economic value is also called the Societal Surplus (SS).

## Slide 3: Economic Terminology
Producer surplus is due to all producers being paid the market clearing price, although some would have been willing to be paid less.
Consumer surplus is due to all consumers paying the market clearing price although some would have been willing to pay more.
Q
P
D
S
q1
p
p2
CS
PS
q
p1

## Slide 4: Important Equalities
Changes in consumer surplus are equal and opposite to changes in producer revenue
  In a market with efficient pricing of congestion rights, where the proceeds of the sale of these rights are returned to consumers
Changes in societal surplus are equal and opposite to changes in producer costs
  For an equal quantity served
  An algebraic proof of this is available

## Slide 5: Issue for Debate
No debate on the economic theory
No debate that planning transmission projects to relieve constraints is a good idea
No debate over comparing the annual “savings” due to a project to the annual carrying cost of the project capital
The debate is over what we mean by “savings”
  Savings to the system as a whole, or savings to consumers only

## Slide 6: Options
Societal Impact Test – the increase in the societal surplus (equal to the reduction in production costs) due to a project must exceed the annual carrying cost of the project capital
Consumer Impact Test – the increase in consumer surplus (equal to the reduction in generator revenues) due to a project must exceed the annual carrying cost of the project capital

## Slide 7: For Starters
Examples can be developed that support almost any position
  It is more important to focus on how the project criteria fit into the overall market design
ERCOT Transmission Planning must have a clearly defined criteria in order to evaluate projects
  In our last study, we conducted over 1,000 model runs to evaluate potential projects

## Slide 8: Societal Impact Test
Projects that pass the Societal Impact test result in overall production cost savings. In other words, the same load is served more efficiently, at a lower system cost.
Does not consider whether consumers or producers receive the benefits of any particular decision

## Slide 9: Focus on the Long-Term View
All system costs are paid by the consumer
  Regardless of any transmission improvements, consumers will pay for generators to earn a reasonable market return on investments
  Competition will limit generator revenues
  In the long run, consumers will benefit from minimizing system production costs while minimizing transmission investment

## Slide 10: The Nodal Market
What is the objective of the nodal market?
  To minimize bid-based production cost
  To provide price signals so generators will build new plants in areas with high LMPs
Some transmission constraints should and will be solved by generation siting
How can we delineate the transmission projects that could be better solved by generation siting?
  By focusing only on those projects that make the system as a whole more efficient.

## Slide 11: Concerns About Consumer Surplus Test
Can be used to justify projects that would be solved by new generation siting
Can be used to justify projects that affect LMPs at specific generator buses
Consumer Surplus savings are highly dependent on generator bidding behavior
  Production cost savings are not highly dependent on generator bidding behavior
Consumer surplus savings may not be additive

## Slide 12: Special Considerations
The societal benefit test may be inappropriate for projects that address market power issues, or for projects that alleviate constraints into areas where new generation cannot be built due to environmental regulations or land-use restrictions.
These projects could be evaluated using a special process, in consultation with outside parties (such as an Independent Market Monitor, the PUC, and other stakeholders)
These projects should be the exception, not the rule.

## Slide 13: Conclusions
The Societal Benefit test selects projects that increase overall system efficiency and result in long-term savings to consumers
The Consumer Benefit test may lead to:
  Approval of unnecessary transmission projects
  Increased long-term costs to consumers

## Slide 14: Recommendation
Transmission Planning should continue to use the Societal Benefit criteria (increased system efficiency) for evaluating new transmission projects
Transmission Planning should work with stakeholders (PUC, CMWG, RPG) to address external issues such as market power

## Slide 15
Comments?