## Slide 1: ECONOMIC TRANSMISSION PLANNING
Wholesale Market Subcommittee
March 22, 2006
CMWG Proposal #1

## Slide 2: Coalition Position
Reject Project
We agree that projects with a net present value (NPV) of Societal Surplus (SS), which exceeds the NPV of the incremental transmission cost of service (TCOS) should be built
However, in recognition of how transmission is paid for in ERCOT (i.e. REPs/loads pay), we believe that projects whose NPV of Consumer Surplus (CS), which exceeds the NPV of TCOS should also be built
Proposed benefit metric:
NPV of SS > NPV of TCOS
NPV of CS > NPV of TCOS
Quantify SS & CS over life of project
RPG Recommend Project Approval
RPG Recommend Project Approval
Request of WMS
Vote to support the proposed metric, which appropriately identifies and recommends projects with long-term system benefit (SS), as well as, near-term benefits to loads (CS)
Yes
No
No
Yes

## Slide 3: Presentation Overview
Utilized a two area system to examine a series of individual transmission upgrade proposals both incrementally (on a project by project basis) and cumulatively (as a set of projects)
An example of a project that has negative Consumer Surplus, but positive Societal Surplus will be reviewed
An example of a worthwhile project that passes both the Societal and Consumer Surplus test will be reviewed
An example of a worthwhile project that passes only the Consumer Surplus will be reviewed

## Slide 4: Scenario1: Base Case
Generator Term Definitions
Equiv. Hourly OOMC Start Cost ($/hr) – cost to start out of merit unit ($18k in this example) divided by total run hours (10 hrs in this example)
Running Cost ($/hr) – Output MW * Production Cost
Production Cost ($/hr) – Running Cost + Equiv. Hourly OOMC Start Cost
Generator Revenue ($/hr) – Output MW * Locational Marginal Price (LMP) at the bus + reimbursement for OOMC Start Cost
Generator Profit ($/hr) – Generator Revenue minus Production Cost
Load Term Definitions
Clear Price ($/MWh) – Load Zone LMP
Initial Cost ($) – Load MW * Load Zone LMP
Out Of Merit Uplift ($) – Equivalent Hourly OOMC Start Cost allocated to each Load Zone on a load ratio share (LRS) basis
Congestion Refund ($) – [Initial Cost + Out Of Merit Uplift] minus Generator Revenue, which is allocated to each Load Zone on a LRS basis
Final Cost ($) – Initial Cost minus Congestion Refund
Net Load Cost ($/MWh) – Final Cost by Load Zone divided by Load Zone MWs
Generation Pocket
Load Pocket

## Slide 5: Scenario 7: Completely De-Bottlenecked Upgrade Set
Note: refer to the Appendix for a detailed project-by-project walk forward of successive projects that build serially upon one another to achieve the end state shown above
Generation Pocket
Load Pocket

## Slide 6: Observations
A project with a large Societal Surplus, but a Negative Consumer Surplus, is an indication that more upgrades are likely needed
Project would be recommended if NPV of SS > NPV of TCOS
3 projects where the Societal Surplus consists entirely of Consumer Surplus
Each project would be recommended if NPV of SS > NPV of TCOS
Project with substantially smaller Societal Surplus than Consumer Surplus
Without considering a Consumer Surplus metric this project may not be funded leaving loads / REPs in a precarious situation
Project with negligible Societal Surplus and negative Consumer Surplus
Loads / REPs shouldn’t be required to fund this project

## Slide 7: Observations (cont.)
It is important to look at the cumulative Societal & Consumer Surplus of the package of individual projects within a project set
If the de-bottlenecking of a constraint is stopped too soon, the loads / REPs will be left paying for a set of upgrades without recognizing a fair return for their investment
This example illustrates that projects up through Scenario 6 should be approved to properly treat the loads / REPs who are funding the project(s)

## Slide 8: Conclusion
We have illustrated:
  Why the potential concern of approving a project based on Societal Surplus benefits, but has negative Consumer Surplus is a non issue. It means that more upgrade projects are still needed
  How it is necessary to approve projects based on Consumer Surplus even if Societal Surplus alone doesn’t justify it. This is necessary to allow loads to recognize a fair & timely return on their transmission upgrade investments
Request of WMS
Approve the proposed economic benefit metric shown below:
Reject Project
NPV of SS > NPV of TCOS
NPV of CS > NPV of TCOS
Quantify SS & CS over life of project
RPG Recommend Project Approval
RPG Recommend Project Approval
Yes
No
No
Yes

## Slide 9: APPENDIX

## Slide 10: Scenario1: Base Case
Generator Term Definitions
Equiv. Hourly OOMC Start Cost ($/hr) – cost to start out of merit unit ($18k in this example) divided by total run hours (10 hrs in this example)
Running Cost ($/hr) – Output MW * Production Cost
Production Cost ($/hr) – Running Cost + Equiv. Hourly OOMC Start Cost
Generator Revenue ($/hr) – Output MW * Locational Marginal Price (LMP) at the bus + reimbursement for OOMC Start Cost
Generator Profit ($/hr) – Generator Revenue minus Production Cost
Load Term Definitions
Clear Price ($/MWh) – Load Zone LMP
Initial Cost ($) – Load MW * Load Zone LMP
Out Of Merit Uplift ($) – Equivalent Hourly OOMC Start Cost allocated to each Load Zone on a load ratio share (LRS) basis
Congestion Refund ($) – [Initial Cost + Out Of Merit Uplift] minus Generator Revenue, which is allocated to each Load Zone on a LRS basis
Final Cost ($) – Initial Cost minus Congestion Refund
Net Load Cost ($/MWh) – Final Cost by Load Zone divided by Load Zone MWs

## Slide 11: Scenario 2: Upgrade Transfer Capability by 100 MW

## Slide 12: Scenario 3: Upgrade Transfer Capability by 200 MW

## Slide 13: Scenario 4: Upgrade Transfer Capability by 300 MW

## Slide 14: Scenario 5: Upgrade Transfer Capability by 400 MW

## Slide 15: Scenario 6: Upgrade Transfer Capability by 500 MW

## Slide 16: Scenario 7: Upgrade Transfer Capability by 600 MW