## Slide 1: Frequency Control Task Force
Report to WMS
March 22, 2006

## Slide 2: Overview
Background / FCTF Charge
Issues Examined by FCTF
Framing the Issues
Options
Next Steps

## Slide 3: Background
The ERCOT Single Control Area frequently experiences poor system frequency control.
Originally noticed during the morning and evening ramps, frequency excursions actually occur throughout the day.
It was theorized that minimizing generator Schedule Control Error should contribute to an improvement in system frequency control.
Prior to the adoption of PRR 525, resource QSEs were only held to an SCE standard during intervals in which they provided Regulation Service.

## Slide 4: Background (cont.)
Through PRR 525, stakeholders elected to address poor system frequency control by improving SCE through application of an SCE performance measure to all resource QSEs.
PRR 525 did not address penalties for non-compliance, so the discretionary “death penalty” in Protocols 6.10.12 became the default penalty for failure to meet the metric.
PRR 586 was filed by PUCT Staff to further address SCE through reallocation of Regulation Service costs to resource QSEs with poor SCE.

## Slide 5: PRS action on PRR 586
Remanded to ROS 5/19/05 with instructions to:
  Frame the issue
  Determine whether PRR 586 resolves that issue
  Either amend PRR 586 to resolve issue or draft new PRR to resolve issue
  Determine any unintended consequences of PRR 586

## Slide 6: ROS Response on PRR 586
ROS response to PRS on 7/21/05 framed the technical requirements:
  PRR 586 will not solve the frequency problem in ERCOT, but may be part of a broader package of solutions
  420 MW / 0.1 Hz should remain the frequency response standard, applicable to frequency disturbances defined as a Measurable Event in Protocols 5.8.
  For deviations +/ -0 .0613 Hz, 282 MW / 0.1 Hz should be used as the standard minimum.
  With a 420 MW / 0.1 Hz frequency response standard, the appropriate SCE deadband is one that covers the large majority of typical system control errors, such as the greater of 2% of QSE scheduled load or 12 MW.
ROS recommended the last two bullets of the PRS charge be addressed by WMS

## Slide 7: more PRS action
On 7/21/05 PRS remanded PRR 586 to WMS with the following motion:
  PRS refers PRR586 to WMS to consider frequency control problems identified by the PDCWG and ROS and develop commercial solutions, such as incentives that should be re-aligned. WMS should also consider the commercial implications of the global plan that ROS is being asked to develop to address those problems. PRS also requests that ROS continue its work related to frequency control and develop a concrete global plan, including prioritized actions and a timeline, to address the frequency issues it identified. In addition, ROS should complete the analysis of primary and secondary response issues it identified.

## Slide 8: Frequency Control TF Charge
WMS formed the FCTF in response to the significant number of PRRs filed to address SCE calculation methodology, performance measurement, and compliance.
The TF was never formally charged, but WMS determined the TF should take a “holistic” approach to examining the commercial structures, performance measures, incentives, and penalties needed to achieve satisfactory system frequency control.
The Frequency Task Force first met Aug. 2, 2005 to determine whether commercial solutions could be devised to improve system frequency control.

## Slide 9: FCTF Issues Examined
Contribution of SCE to poor frequency control
Contribution of SCE to regulation deployment
Contribution of load forecast error to regulation deployment
Market obligations / incentives to provide primary frequency response
Market incentives / penalties for SCE Performance
Uncontrollable Renewable Resource Forecast Error
Re-evaluation of Protocols 6.10.5.3 (PRR 525)
Accuracy of ERCOT RGS signals and impact on QSE SCE calculation

## Slide 10: Contribution of SCE to poor frequency control
Neither PRR 525 nor PRR 586 specifically addresses primary or secondary frequency response. Instead, each addresses SCE, which impacts the amount of Regulation Service deployed to maintain system frequency.
SCE is one of many factors contributing to poor system frequency control and the need for Regulation Service.
Other factors include:
  ERCOT load forecast error / Real-time variations in load
  Poor governor response

## Slide 11: Contribution of SCE to regulation deployment
SCE is a contributor but not necessarily a large driver for Regulation Service procurement and deployment.
Allocation of some portion of RGS costs to QSEs with poor SCE (a la PRR 586) could provide appropriate incentive to maintain low SCE.
Allocation of RGS costs to QSEs with poor SCE should be proportional to SCE impact.

## Slide 12: Market obligations / incentives to provide primary frequency response
Operating Guides require all generators online to place their governors in service
The FCTF is thus far unable to determine whether ERCOT is getting adequate governor response
ERCOT is an “energy only” market in which generators have neither an obligation nor an incentive to reserve capacity for frequency response.
In fact, the reverse is true – the market structure incentivizes generators to maximize production from units online, sometimes leaving little room for machines to respond to frequency excursions

## Slide 13: Market incentives / penalties for SCE Performance
Pre-PRR 525: CPS2 performance measure provided incentive for resource QSEs to not bid Regulation Service during intervals with high SCE.
Post-PRR 525: “Death Penalty” provides strong incentive to minimize SCE
  Especially for ancillary service providers
  Affects all resources, which must maintain DBES obligation
    Inability to make mandatory DBES offer violates PUCT Rule
    Jeopardizes PGC registration

## Slide 14: Uncontrollable Renewable Resource Forecast Error
URR schedules based on resource forecast
Historically poor forecasting performance by URRs
URR SCE contributes to regulation deployment
Holding an uncontrollable resource to control performance standard makes little sense and, in fact, provides a disincentive for the market to meet a statutory obligation to install URRs in Texas
“Persistence Forecasting” methodology explored to improve URR SCE and minimize system impacts

## Slide 15: Persistence Forecasting Methodology
Notes: Source: FPL Energy
Notes: Chart represents one 114MW wind facility. Compares actual production 20 minutes prior to start of interval with generation meter data for end of interval to determine accuracy of persistence forecasting methodology. Four months of data gathered – March, August, October 2005 and January 2006 to get seasonal perspective. Forecast error averaged for each day and averaged for each month demonstrates 5-8% average forecast error.

## Slide 16: Re-evaluation of Protocols 6.10.5.3 (PRR 525)
Monitoring and evaluating SCE Performance scores under PRR 525 metric.
No recommendation but it is safe to say nearly everyone agrees with one of the three following statements:
  PRR 525 does not use a good performance measure
  SCE Compliance penalty structure is inappropriate
  Both the of statements above are true
Some changes to the exemption list are in order

## Slide 17: ERCOT’s CPS1 12 Month Rolling Average Trend
Notes: Source: ERCOT Compliance

## Slide 18: ERCOT CPS1 by Interval
Notes: Source: ERCOT Compliance

## Slide 19: March MTD CPS1 by Interval
Notes: Source: ERCOT Compliance

## Slide 20: QSE PRR525 10-Minute Interval Scoring
Notes: Source: ERCOT Compliance

## Slide 21: 525 Passing 10-Min Interval Percentage Trends
Notes: Source: ERCOT Compliance

## Slide 22: Accuracy of ERCOT RGS signals and impact on QSE SCE calculation
TXU supplied data suggesting frequent implied ramp rate violations in ERCOT URS and DRS signals
ERCOT agrees a problem exists. ERCOT system apparently randomly skips an AGC cycle, resulting in the next value being higher or lower than it should
ERCOT staff agrees this has some impact on QSE SCE calculation
ERCOT system analysis and applicability to other QSEs ongoing

## Slide 23: Framing the Issues
Group issues into 3 categories
  Address SCE performance measure calculation and/or penalty structure before July 1 “death penalty” deadline
  Address the “low-hanging fruit” clean up items related to SCE performance measure
  Address incentives / penalties / performance measures for primary frequency response

## Slide 24: Options
PRR 656: SCE Performance Charge (Cat. 1)
Draft PRR: SCE Compliance Enforcement (Cat. 1)
Draft PRR: Ancillary Service Deployment Performance Conditions (Cat. 2)
Draft SCR: Persistence Forecasting Methodology for URRs (Cat. 2)
Draft PRR: Governor Response Service (Cat. 3)

## Slide 25: Option 1 PRR 656: SCE Performance Charge
Addresses both SCE calculation methodology and enforcement regime
Creates an SCE Performance Charge to replace current SCE Performance Monitoring
QSEs will be charged for each 5-minute interval for SCE average outside their deadband that contributes to Regulation Service deployment

## Slide 26: Option 2 Draft PRR: SCE Compliance Enforcement
Basically keeps the PRR 525 SCE calculation methodology intact
Substitutes alternate penalty structure for existing “death penalty only” regime
Poor performing QSEs ability to offer Regulation Service “ratcheted down” following failure to meet SCE performance measure.

## Slide 27: Option 3 Draft PRR: Ancillary Service Deployment Performance Conditions
Addresses the “low-hanging fruit”
Amends Protocols 6.10.6
Exempts URRs from SCE enforcement regime
Clarifies ramp rate violation impacts in QSE SCE calculation
Clarifies intent behind unit trip exemption from QSE SCE calculation

## Slide 28: Option 4 Draft SCR: Persistence Forecasting Methodology for URRs
System changes required to implement persistence forecasting
Question about whether QSEs should submit performance data or whether ERCOT should capture and utilize data on behalf of QSEs
Changes to Lodestar, SPD likely
SCR development ongoing

## Slide 29: Option 5 Draft PRR: Governor Response Service
FCTF discussed bid-based service, pay-as-you-go service, and governor response performance measure
Service to provide primary frequency response
As a bid-based service it would be treated similar to how RRS is treated today. Offers from generation resources would take the form of “MWs/0.1 Hz deviation” and those offers struck would get a capacity payment for the amount of MWs struck in the Day Ahead ancillary service procurement process.

## Slide 30: Option 5 Draft PRR: Governor Response Service
As a “pay-as-you-go” service, the generation resource presumably offers in some amount of “MWs/0.1 Hz” value and be paid nothing in the DA A/S procurement process.
Payment would only occur if a frequency event actually occurred in real time. Then some yet to be proposed “look back” approach would be used for settlements. Payments could be paid on a capacity basis (using RRS as proxy value?, just the hour of the event/all day?) or on a flat fee basis using some other value as a proxy.

## Slide 31: Next Steps
Next FCTF meeting on 3/31/06
  Refine options into recommendations
  Request action to address Category 1 Issues
  Request action to address Category 2 Issues
  Determine next steps to address Category 3 Issues
  Address pending PRRs 586, 605, 607, and 608
Next ROS meeting on 4/13/06
  Comment on FCTF recommendations
Next WMS meeting on 4/19/06
  Comment on FCTF recommendations
April 21 PRS meeting
  Vote on FCTF-submitted PRRs (Urgent Status requested)