## Slide 1: ROS Feb 2006
The Model
Curtis Crews
Network Model Engineering Supervisor
512-248-3139

## Slide 2: Line Comparison between Operations & Planning
 | Matched Lines | with MVA or Imp. differences | with MVA or Imp. differences
Jan '05 | 3622 | 1272 | 35.1%
Mar '05 | 3736 | 1018 | 27.2%
Jul '05 | 3763 | 1095 | 29.1%
Aug '05 | 3730 | 860 | 23.1%
Sep '05 | 3724 | 608 | 16.3%
Jan '06 | 5035 | 1279 | 25.4%
Criteria for “with differences”:
R, X, & I difference of 0.0001 (pu) or greater (not including Operation’s “Internal Bus bar” entries that have a difference = 0.0001)
Rate B vs. Emergency & for Rate A vs. Continuous Line Limits that have 1 MVA or greater difference
Jan 2006 Comparison completed on Operations Jan 5 Database and Planning 06 Winter Peak

## Slide 3: Matched Lines with MVA differences
Total of over 500 MVA differences noted
For MVA differences of 100+ MVA:
  Planning’s Rate A / Operation’s Continuous = 89
  Planning’s Rate B / Operation’s Emergency = 83
For MVA differences of less than 10 MVA (but equal or greater than 1 MVA)
  Planning’s Rate A / Operation’s Continuous = 150
  Planning’s Rate B / Operation’s Emergency = 168

## Slide 4: Where do the numbers come from?
Charging attribute was not considered in original comparison.
Note the comparison increased in terms of number of lines being compared (from 3622 to 5035)
Jan 2006 Comparison completed on Operations Jan 5 Database and Planning 06 Winter Peak

## Slide 5: Why is this important?
What information is correct?
Which methodology for rating lines is correct?
Future Nodal Protocols call for consistency (Reference Nodal Protocols Section 3 specifically 3.10 (5), 3.10 (9), 3.10.2 (1), 3.10.8 (1), 3.10.8.4 (2) )
Network Model Management System Software Proposal

## Slide 6: What now?
Encourage ROS to endorse internal efforts to correlate data fully understanding that there will be differences due to the nature and intent of models.
Understand that the intent of OGRR 181 is to correlate data of existing equipment.
Other equipment comparisons to follow.

## Slide 7: Energize Date Requirement
8.8.2.1 TSP Information to be provided to ERCOT
The TSP shall notify ERCOT at least thirty (30) days before starting to energize or place into service any new or relocated Facility.

## Slide 8: Why is this important?
ERCOT has 15 days to approve or reject data submittal
Coordination of model data is vital
Nodal Protocols call for a 90 day minimum data submittal time period. There is a requirement for Summer Model data to be submitted a minimum of 180 days in advance. (See Protocol 3.10.1)

## Slide 9: Challenges
ERCOT does not control data submittal quantity
Outage Scheduler
Database Loads
Incomplete Data re-submittal

## Slide 10: In Service Notification Approval to Energize
8.8.1 Coordination with ERCOT
Prior to energizing and placing into service any new or relocated Facility connected to the ERCOT Transmission Grid, TSPs shall coordinate with and receive approval from ERCOT.
Temporary Re-Route Process is currently being revised. Expect a new process soon.

## Slide 11: Challenges
Reliability of system could be affected.
Has model data been provided in a timely manner?
Has model data been provided?
Timing of energization.

## Slide 12: References
Nodal Protocol 3 http://www.ercot.com/committees/board/tac/tptf/np/index.html
OGRR 181 http://www.ercot.com/mktrules/issues/ogrr/175-199/181/index.html
Current Protocol 8 http://www.ercot.com/mktrules/protocols/current/
Temporary ReRoute/InService Notification http://www.ercot.com/mktrules/guides/procedures/