## Slide 1: The Need for PRR 647
Properly Modeling the Reactive Behavior of Generators

## Slide 2: PRS Remand
On 1/19/06, PRS voted unanimously to refer PRR647 to ROS for determination of ERCOT needs and identification of data already being reported to ERCOT by Market Participants, and directed ROS to report to PRS at its March meeting. All market segments were present for the vote.

## Slide 3: Data Already Reported
Net MW (All)
Net MVAr injection (All)

## Slide 4: ERCOT Needs
Gross MW/MVAr at generator terminals
  Every generator should have this information already
  Asking for this to be telemetered (RTU/ICCP) to ERCOT

## Slide 5: Pictorial Protocol
QSE must provide
Net MW/MVAr OR
Gross & Plant MW/MVAr
Net = Gross – Plant - XFMR
Gross
Aux/Plant
XFMR Consumption
Net

## Slide 6: Current State of Affairs in ERCOT (Protocol)
(1) A QSE representing a Generation Entity that has Generation Resources connected to a TDSP shall provide the following Real Time data to ERCOT for each individual generating unit at a Generation Resource plant location and ERCOT will make the data available to the Generation Resource’s host TDSP (at TDSP expense):
(a) gross or net real power;
(b) gross or net Reactive Power;
(c) if gross quantities are provided, the plant auxiliary Load data will also be supplied;

## Slide 7: Model “Reality”
Gross
Aux/Plant
XFMR Consumption
Net
Net used
As Gross

## Slide 8: Problem: As System Becomes More Vulnerable to Voltage Collapse, Reactive Reserve Modeling Becomes Crucial

## Slide 9: How Generator MVArs are Modeled
Gross Generator Output
Net Generator Output
True Reactive Reserve
Modeled Reactive Reserve
If Net output is incorrectly
used in place of Gross Output
Q
(MVAr)
P(MW)
Aux/Plant Load
Gross Reactive Capability Curve (CURL)
Usually Created by Generator Manufacturer

## Slide 10: Solution
Gross
Aux/Plant
XFMR
Loss
Net (High Side)
Net (Low Side)
Provided
Calculated

## Slide 11: Metering Freq/Accuracy
Frequency (To be placed in operating guides)
  Net MW RTU (Same as current)
  Gross/Net MVAr, Gross MW ICCP or RTU, at least 2x/5 minute
Accuracy
  No change to 6.5.1.1(6) “Real Time data for reliability purposes must be accurate to within three percent (3%). This telemetry may be provided from relaying accuracy instrumentation transformers.”