## Slide 1: ECONOMIC TRANSMISSION PLANNING Discussion of WMS Resolution Passed on March 22, 2006
Technical Advisory Committee
April 7, 2006

## Slide 2: Overview- Approved WMS Resolution
Approve a transmission project when:
NPV of Societal Surplus (SS) > NPV of Incremental Transmission Cost of Service (TCOS)
Additionally, consider a secondary test for approval:
NPV of Consumer Surplus (CS) > NPV of Incremental Transmission Cost of Service (TCOS)

## Slide 3: TAC Request
Approve a revision of ERCOT’s Planning Charter that supports the WMS recommendation to reflect both Societal and Consumer Surplus tests:
Reject Project
NPV of SS > NPV of TCOS
NPV of CS > NPV of TCOS
Quantify SS & CS over life of project
RPG Recommend Project Approval
RPG Recommend Project Approval
Yes
No
No
Yes

## Slide 4: Background and Details
Extensive discussion at WMS/CMWG over the past two months
Various stakeholder concerns were voiced and reviewed:
  Important to build projects that provide long-term system benefits based on Societal Surplus metric as proposed by ERCOT Staff
  Would a Societal Surplus benefit metric sometimes lead to recommending projects that actually have negative Consumer Surplus? If so, how should these be treated?
  Will the Societal Surplus metric alone fully identify all of the projects that may provide significant near-term delivered cost reductions (i.e. CS) to REPs/Consumers by increasing their access to more efficient generation outside their load centers?
A simple two area system was developed to examine a series of individual transmission upgrade proposals to help answer these questions

## Slide 5: Base Case - Highly Constrained System (Scenario 1 in Appendix)
Generator Term Definitions
Equiv. Hourly OOMC Start Cost ($/hr) – cost to start out of merit unit ($18k in this example) divided by total run hours (10 hrs in this example)
Running Cost ($/hr) – Output MW * Production Cost
Production Cost ($/hr) – Running Cost + Equiv. Hourly OOMC Start Cost
Generator Revenue ($/hr) – Output MW * Locational Marginal Price (LMP) at the bus + reimbursement for OOMC Start Cost
Generator Profit ($/hr) – Generator Revenue minus Production Cost
Load Term Definitions
Clear Price ($/MWh) – Load Zone LMP
Initial Cost ($) – Load MW * Load Zone LMP
Out Of Merit Uplift ($) – Equivalent Hourly OOMC Start Cost allocated to each Load Zone on a load ratio share (LRS) basis
Congestion Refund ($) – [Initial Cost + Out Of Merit Uplift] minus Generator Revenue, which is allocated to each Load Zone on a LRS basis
Final Cost ($) – Initial Cost minus Congestion Refund
Net Load Cost ($/MWh) – Final Cost by Load Zone divided by Load Zone MWs
Generation Pocket
Load Pocket

## Slide 6: Completely De-Bottlenecked Upgrade Set (Scenario 7 in Appendix)
Note: refer to the Appendix for a detailed project-by-project walk forward of successive projects that build serially upon one another to achieve the end state shown above
Generation Pocket
Load Pocket

## Slide 7: Observations
A project with a large Societal Surplus, but a Negative Consumer Surplus, is an indication that more upgrades are likely needed
Project would be recommended if NPV of SS > NPV of TCOS
3 projects where the Societal Surplus is dominated by Consumer Surplus
Each project would be recommended if NPV of SS > NPV of TCOS
Project with substantially smaller Societal Surplus than Consumer Surplus
Without considering a Consumer Surplus metric this project may not be funded leaving Consumers/REPs in a precarious situation
Project with negligible Societal Surplus and negative Consumer Surplus
Consumers/REPs shouldn’t be required to fund this project

## Slide 8: Observations (cont.)
Suppose that a project set with upgrades 2 thru 5 was approved based on the Societal Surplus (SS) test and upgrade 6 could not be justified on SS alone
Upgrade 6 provides eight times more Consumer Surplus benefit than Societal Surplus benefit and will likely would be justified by the secondary Consumer Surplus test.
If the de-bottlenecking of a constraint is stopped too soon, the Consumers/REPs will be left paying for a set of upgrades without recognizing a fair return for their investment

## Slide 9: Conclusion
Our sample system has illustrated:
  Why the potential concern of approving a project based on Societal Surplus benefits that has negative Consumer Surplus is a non issue. It likely means that more upgrade projects are still needed
  How it is necessary to approve projects based on Consumer Surplus even if Societal Surplus alone doesn’t justify it. This is necessary to allow Consumers/REPs to recognize a fair & timely return on their transmission upgrade investments

## Slide 10: TAC Request
Approve a revision of ERCOT’s Planning Charter that supports the WMS recommendation to reflect both Societal and Consumer Surplus tests:
Reject Project
NPV of SS > NPV of TCOS
NPV of CS > NPV of TCOS
Quantify SS & CS over life of project
RPG Recommend Project Approval
RPG Recommend Project Approval
Yes
No
No
Yes

## Slide 11: APPENDIX

## Slide 12: Scenario1: Base Case
Generator Term Definitions
Equiv. Hourly OOMC Start Cost ($/hr) – cost to start out of merit unit ($18k in this example) divided by total run hours (10 hrs in this example)
Running Cost ($/hr) – Output MW * Production Cost
Production Cost ($/hr) – Running Cost + Equiv. Hourly OOMC Start Cost
Generator Revenue ($/hr) – Output MW * Locational Marginal Price (LMP) at the bus + reimbursement for OOMC Start Cost
Generator Profit ($/hr) – Generator Revenue minus Production Cost
Load Term Definitions
Clear Price ($/MWh) – Load Zone LMP
Initial Cost ($) – Load MW * Load Zone LMP
Out Of Merit Uplift ($) – Equivalent Hourly OOMC Start Cost allocated to each Load Zone on a load ratio share (LRS) basis
Congestion Refund ($) – [Initial Cost + Out Of Merit Uplift] minus Generator Revenue, which is allocated to each Load Zone on a LRS basis
Final Cost ($) – Initial Cost minus Congestion Refund
Net Load Cost ($/MWh) – Final Cost by Load Zone divided by Load Zone MWs

## Slide 13: Scenario 2: Upgrade Transfer Capability by 100 MW

## Slide 14: Scenario 3: Upgrade Transfer Capability by 200 MW

## Slide 15: Scenario 4: Upgrade Transfer Capability by 300 MW

## Slide 16: Scenario 5: Upgrade Transfer Capability by 400 MW

## Slide 17: Scenario 6: Upgrade Transfer Capability by 500 MW

## Slide 18: Scenario 7: Upgrade Transfer Capability by 600 MW