## Slide 1: ERCOT Compliance PRR607
August 2006

## Slide 2: QSE PRR525 10-Minute Interval Scoring
Notes: Performance has clearly improved among QSEs (except windfarms). Is this really needed?
Note in January we had 28 QSEs (non-wind) but in July we have 36

## Slide 3: 525 Passing 10-Min Interval Percentage Trends
Notes: Another. Anecdotally, several QSEs report enhanced controls and operator training that should provide benefits all the time. Some of these are just now being implemented.

## Slide 4: ERCOT’s CPS1 Monthly Trend
Notes: Looks good, improvement is evident. Of course, we expect it to fall back somewhat under lighter loads.

## Slide 5
Notes: ERCOT’s frequency average is still clearly not at the level experienced prior to Single Control Area Opns. In 2000, things had already started to slip somewhat.

## Slide 6: ERCOT CPS1 by Interval
Notes: The risk to ERCOT is highest during certain intervals that typically coincides with large start up and shut down ramping periods. We appear to have improved this during July, but again this is high loading.
If this PRR results in re-appearance of large frequency deviations during predictable portions of the day, ERCOT Operations is likely to again request ADDITIONAL REGULATION SERVICES during these periods.

## Slide 7: SCE Performance Scoring
Exclusions are manually adjusted from scores.
All QSEs are scored; the number is increasing.
Processing exclusions proposed for PRR607 could prove complex and time consuming.
Additional FTE(s) will be requested.
Notes: This will tax the group.
We also need some definitions to accurately scope the work:
What is the start up time precisely? Shut down time? Are we talking about single intervals or several hours? Is it limited to once a day? From QSEPM discussion, it sounds like hours with a 50% change (before and after) will be involved – this is not defined yet.
SCE calculations need to be reviewed, basically we need to create a new ramp and perform 4-second checks to come up with a new SCE. This again will have to be done manually for requested intervals.
Will it really help? If the actual ramp is different, the QSE score could be worse still.