## Slide 1: PRS RPRS Task Force Status Summary
Prepared for WMS and PRS
August 2006

## Slide 2: Task Force Objectives
Evaluate Effect of Load Forecast Sigma Bias and Power Balance on procurement of RPRS
  Is the amount of bias appropriate?
  Does the Power Balance create additional Bias?
  Is there a presence of n-2 criteria in this procurement?
  How much unutilized capacity is on the system?
  Can other ancillary services be used?
Resolve Allocation of Excess Funds

## Slide 3: Is the Amount of Sigma Bias appropriate?
Sigma Bias is based on historic peak hour error between day-ahead forecast and actual.
Error has improved in the last two months and the amount of sigma bias has been reduced from 1800 MW to 1500 MW.
There has been sufficient capacity committed even during record-breaking loads.
Accounts for less than half of RPRS procurements.
No consensus on appropriateness has been reached but the bias is recognized as an ERCOT derived reliability parameter in day-ahead planning.

## Slide 4: Power Balance
Checks for NERC n-1 deliverability criteria given a Resource Plan profile.
Calls on more capacity until n-1 criteria is met.
Can account for a significant amount of capacity procurement with most of the effect in Step 2.
Is an integral part of the RPRS engine that went into effect earlier this year.
Prior to that, process was manually intense and not as complete with respect to n-1 compliance.

## Slide 5: Illustration: June 20, 2006
Load
Resource Plan Capacity
Step 1 (for transmission constraints) Procurement
Step 2 Capacity insufficiency and Step 1 and 2 Power Balance
Total Step 1 and 2 Capacity Procured
Final Capacity for load
48,940 MW
55,505
933 MW
404 MW
1,337 MW
56,842 MW

## Slide 6: June 20th, 2006 HE 1300
Capacity
Dispatchable Generation is available generation which is not limited by an n-1 transmission constraint
Capacity is the sum of HSL of all generation online
55,505
56,842
48,536
MW
55,505
RPRS Stage
Initial
Initial
Step 2
Step 1
Step 2
Step 1
N-1 Dispatchable Generation
48,940
Power Balance Constraint
50,990
Capacity Constraint
Notes: Initial Condition
Load Forecast = 48940
URS + RRS = 2050
Resource Plan Max = 55505
Dispatchable Generation = 55505
System Capacity Constraint 48940 + 2050 ≤ 55505 (Satisfied for rest of solution)
Power Balance Constraint 48940 = 48940
Step 1 Procurement (for transmission constraints)
Step 1 Procurement = 933*
Resource Plan Max = 56423
Dispatchable Generation = 48536
Power Balance Constraint 48536 < 48940 (Not satisfied)
Step 2 Procurement (to meet load forecast and capacity)
Step 2 Procurement = 404
Resource Plan Max = 56842
Dispatchable Generation = 48940
Power Balance Constraint 48940 = 48940 (satisfied)
* Note: when compared to RPRS report online, this number seems 15 MW too large. For this actual day, 15 MW of RPRS generation was deselected by the ERCOT operator.

## Slide 7: Use of Other Ancillary Services to meet Sigma Bias ?
Sigma Bias:
  A proposal to use the non-spin reserve market for sigma bias has been offered by stakeholders.
  ERCOT is looking at this as an alternative day-ahead procurement.
  A key issue: how does ERCOT know if offline reserve is being used to satisfy non-spin reserve service vs. satisfying RPRS or OOMC?

## Slide 8: Use of Other Ancillary Services to meet Power Balance?
The Power Balance logic is intertwined with the Step 1 and 2 RPRS engine.
More analysis is needed with respect to Power Balance results.
A special task force or consulting services may be needed to perform this analysis due to the confidential nature of actual generator data.

## Slide 9: Allocation of Excess Funds
Discussions have centered around what constitutes assignability of RPRS procurement:
  Insurance for sigma bias and n-1 criteria (power balance) vs. QSE short-scheduling

## Slide 10: Three PRRs Have Been Submitted, All of which address the Allocation of Excess Funds
PRR674:
  Eliminates the uplift/assignment due to QSE short positions and uplifts all RPRS costs incurred on a load ratio share basis.
PRR676:
  Pays for RPRS with generic cost.
  Assigns short QSEs up to twice the cost rate for RPRS procurement and then uplift the remainder on a load ratio share basis.
PRR678:
  Allocates Excess Funds to QSEs relative to their “long” position.

## Slide 11: Pros/Cons for PRR 674
CONS
  Does not encourage self-scheduling of next day capacity via accurate load and balanced schedules.
PROS
  Assumes primary cost of RPRS is for reliability and security procurement reasons and not QSE “Shortness”; thus, most of the cost should be uplifted.
  Easiest proposal to implement (turns off Step 2 procurement and corresponding settlement).
  Can serve as a temporary solution until the allocation issues are assessed in greater detail.

## Slide 12: Pros/Cons for PRR678
PROs
  Encourages QSEs to self schedule generation capacity via accurate day-ahead load and balanced schedules.
  Although more difficult to implement than PRR674, is easier to implement than PRR676.
CONs
  No guarantee that corresponding Resource Plans match load schedules provided.
  Could lead to “long schedule” gaming in order to get Excess Fund payment.

## Slide 13: Pros/Cons for PRR676
PROs
  Offers a compromise position between the polar opposites 674 and 678.
  Uses a method that is similar to what Nodal will use for RUC procurement.
CONs
  By paying for RPRS with generic costs instead of MCPC it diminishes market incentives for providing RPRS.
  Most difficult PRR to implement.

## Slide 14: Questions and Next Steps?