## Slide 1: SCR 747
WMS August 2006
Presented by Young Li

## Slide 2: SCR 747
Approved for implementation by ERCOT board on 12/13/2005
Part of PR-60080_01
  AIMMS 3.6 Upgrade
  Code Separation of MCE and UI
  SCR 747
Currently scheduled for implementation in production October 2006.

## Slide 3: SCR 747
Purpose of SCR 747
  Change current price administration logic to not have SPD post process solution results when no solution is available to solve zonal congestion.
  Currently, price administration sets zonal MCPE to marginal price of each zone (cost of last Mw cleared in that zone).
  New logic will allow the shadow price cap of $2500 to set prices across zones.

## Slide 4: SCR 747
Required changes to penalty factors to allow implementation of SCR 747
  Currently: Shadow Price penalty factor set to $2500.00, and BES ramp rate penalty factor set to $1001.00.
  Proposed: To ensure SPD will not violate BES ramp rate constraint (which would produce unwanted price administration results), ERCOT plans to increase the BES ramp rate penalty factor to $1400.00

## Slide 5: SCR 747
Required changes continued:
  The new penalty factor is suggested based on historical maximum zonal shift factor differentials.
  Ex. OC1 SP Pf = $2500.00
    Current: 1001/.411 = $2435.52
    Proposed: 1400/.411 = $3406.32
  By increasing the BES Ramp Rate Penalty Factor to 1400, we preclude SPD from violating this constraint before the OC1.

## Slide 6: SCR 747
Questions?