| PRR Number | 687 | PRR Title | Replacement Reserve Under-Scheduled Capacity Delineation |
| --- | --- | --- | --- |
| Protocol Section(s) Requiring Revision (include Section No. and Title) | 6.9.2.1 |
| Requested Resolution (Normal or Urgent) | Urgent – This PRR makes corrections to PRR666, Modification of RPRS Under-Scheduled Capacity Charge Calculation (approved by the Board on July 18, 2006). These corrections are necessary for expeditious implementation of PRR666. |
| Revision Description | This PRR corrects discrepancies in the Replacement Reserve Under-Scheduled Capacity charge equation. |
| Reason for Revision | PRR 666 was finalized after many iterations and discussions regarding modification of the Replacement Under-Schedule Capacity charge calculation. Some of these modifications contributed to discrepancies in the description of the Net Load position and mismatch components of the equation. |
| Credit Implications (Yes or No, and summary of impact) | No |
| Relevance to Nodal Market (Yes or No, and summary of impact) | No |
| Nodal Protocol Section(s) Requiring Revision (include Section No. and Title) | None |
| Timeline |
| Date Posted | August 23, 2006 |

| Sponsor |
| --- |
| Name | Ino Gonzalez |
| E-mail Address | igonzalez@ercot.com |
| Company | ERCOT |
| Company Address | Taylor |
| Phone Number | 512-248-3954 |

ERCOT/Market Segment Impacts and Benefits

Instructions:  To allow for comprehensive PRR consideration, please fill out each block below completely, even if your response is “none,” “not known,” or “not applicable.”  Wherever possible, please include reasons, explanations, and cost/benefit analyses pertaining to the PRR.

| Assumptions | 1 | This PRR is a correction to PRR666, and, therefore, does not change the cost or benefit of PRR666. |
| --- | --- | --- |
|  | Impact Area | Monetary Impact |
| Market Cost | 1 | None – see assumptions. | None – see assumptions. |
|  | Impact Area | Monetary Impact |
| Market Benefit | 1 | None – see assumptions. | None – see assumptions. |
| Additional Qualitative Information | 1 |  |
| Other | 1 |  |

Proposed Protocol Language Revision

[PRR666: Replace Section 6.9.2.1 and 6.9.2.1.1 (above), with the following upon system implementation:] 6.9.2.1 Settlement for RPRS Procured for System-wide Capacity Insufficiency The Settlement for RPRS procured for system-wide capacity insufficiency, for each QSE, is as follows: 6.9.2.1.1 Replacement Reserve Under Scheduled Capacity (1) The product of the maximum MCPC of Replacement Reserve procured for the hour, across all Congestion Zones (where the MCPC evaluated across all RPRS markets executed for the hour), multiplied by the QSE’s maximum capacity insufficiency evaluated across all zones for each hour. A QSE’s capacity insufficiency amount includes the maximum mismatch amount, evaluated across all zones for the hour. For the Operating Hour, a QSE’s maximum capacity insufficiency, is the sum of (a) and (b) where (a) and (b) are as follows: (a) The greater of zero (0) or the maximum interval sum of the difference, evaluated across the four (4) intervals in the hour, between a QSE’s Adjusted Meter Load and the QSE’s scheduled Load in each Settlement Interval for the Operating Hour at the time of procurement. (b) The maximum mismatch amount that results from either (i) a mismatch in the QSE’s Schedule as defined in Section 4.7.2, Schedule Validation Process, or (ii) a QSE selecting ERCOT as a Resource, at the time of procurement, evaluated over all applicable RPRS market snapshots for the hour for all Supply and Obligation mismatch combinations. (2) When ERCOT procures Replacement Reserve Service to resolve system-wide capacity insufficiency, the calculation for Replacement Reserve Service Obligation for underscheduled capacity is: Where: Where: h Hour in trade day for which ERCOT purchased RPRS for capacity insufficiency i Hourly interval being evaluated, i=1, …4 where intervals 1, 2, 3, and 4 denote the set of 15-minute Settlement Intervals in a given hour M RPRS markets, in the event of multiple RPRS markets for a particular Operating Hour. This includes both the Day Ahead RPRS market all applicable RPRS markets executed during the Adjustment Period q QSE w Evaluated across all QSEs z Zone AMLiq Adjusted Metered Load (MWh) summed across all zones for a QSE, for Settlement Interval, i, of the settlement hour, h. This value includes estimated and/or actual meter values and the associated Transmission Losses & Distribution Losses and UFE. CLiq QSE’s Scheduled Load (MWh) by Settlement Interval, i, summed across all zones. (This quantity is evaluated across all snapshots of QSE’s schedule for all RPRS markets for the particular hour) MCPCRPzh Replacement Reserve Service Market Clearing Price of Capacity ($/MW), for the hour h, procured for system-wide insufficiency, over applicable markets, M, for the hour, per zone. MMQhq Maximum Mismatched net amount (MW), by hour , h, for the QSE. (This value is summed across all zones for all intervals in the hour and is evaluated across all applicable schedule snapshots.) MMShqi Mismatched Schedule Quantity (MW) representing either Inter-QSE Trades, or ERCOT scheduled as a Resource by settlement hour, h, by QSE, for each Replacement Reserve Market. QSSATORPi QSE Supply Schedule for the buying QSE, A, by Settlement Interval, i, of the settlement hour, h, at the time of the Replacement Reserve Market. QOSATORPi QSE Obligation Schedule for the selling QSE, A, by Settlement Interval, i, of the settlement hour, h, at the time of the Replacement Reserve Market. QOSBTORPi QSE Obligation Schedule for the selling QSE, B, by Settlement Interval, i, of the settlement hour, h, at the time of the Replacement Reserve Market. QSSCTORPi QSE Supply Schedule for the buying QSE, C, by Settlement Interval, i, of the settlement hour, h, at the time of the Replacement Reserve Market. USRPhq Replacement Reserve Service Under Scheduled Charge ($) by hour for the QSE