## Slide 1: ERCOT Load Forecast Uncertainty V2
August 2, 2006

## Slide 2: Load Forecast
Load forecast is load forecast
    Results should not be manipulated
Load forecast has some uncertainty
    Uncertainty should be addressed
      ERCOT should decide the uncertainty amount
      Market should recommend market solution
Load forecast is a system wide concern
    Load uncertainty fix should be uplifted system wide

## Slide 3: Present Day-Ahead Process
ERCOT Forecast = Load forecast (LF) + 1800 MW
ERCOT compares unconstrained on-line capacity to (LF + 1800)
ERCOT purchases RPRS if (LF + 1800) exceeds unconstrained on-line capacity
    ERCOT skips capacity bids behind a constraint
    ERCOT assumes constrained capacity cannot serve load increase within the constrained area
    ERCOT assumes all constrained capacity pockets will experience an N-2 event simultaneously
    Awarded NSRS is not considered as available capacity
    Preliminary data shows 8 to 10% of on-line capacity being constrained

## Slide 4: Proposal
Short-Term Solution
    Separate out load forecast uncertainty (LFU) from RPRS
    Solve LFU with on-line products
Long-Term Solution
    Scrub the model to find inefficiencies in the modeling
    Review assumptions
    Review uncertainty amount
    Review distribution of load increases
    Review available capacity not being considered

## Slide 5: Short-Term Solution
ERCOT determines load forecast
ERCOT compares unconstrained on-line capacity to load forecast
ERCOT purchases RPRS if load forecast exceeds unconstrained on-line capacity
ERCOT determines LFU
ERCOT procures sufficient capacity equal to the hourly LFU by procuring incremental Ancillary Services

## Slide 6: Procurement of Ancillary Services
ERCOT procures from Ancillary Services Markets
    1/3 from Responsive Reserve Service
    1/3 from Up Regulation Service
    1/3 from NSRS
ERCOT procures only as much hourly LFU as is required (peak LFU for peak hour and less than 100% LFU for non-peak hours)
ERCOT assigns the incremental AS on a load-ratio-share
Settlement process remains the same

## Slide 7: Benefits of Short-Term Solution
No start charge paid
No minimum energy (LSL) at high cost
Energy is paid only if deployed
No generator lead time issues (gen responsibility)
No generator min up times (minimizes procurement)
No concern with units failing to start (already on-line)
Selection across multiple AS markets minimizes depletion of any one bid stack
RPRS is handled separately, but this solution minimizes, if not eliminates, RPRS procurement (quantity and hours)

## Slide 8: Long-Term Solution
Scrub the model to confirm that 8 to 10% of on-line capacity is constrained
Determine whether the probability of multiple N-2 events occurring simultaneous is realistic or required
Analyze the ability of constraint capacity to serve load increases within the generation pocket
Determine the capability of combine cycle units or other units to provide “reserve” capability during emergencies (duct fired, over-pressure, ….)

## Slide 9: Benefits of Long-Term Solution
Minimizes, if not eliminates, RPRS procurement (quantity and hours)
Properly assigns cost of LFU
Utilizes available capacity
Corrects divergence of Day-Ahead and Real-time Market
More efficient Market