## Slide 1: ERCOT Emergency Interruptible Load Program
Paul Wattles
Steve Krein
WMS
Oct. 18, 2006

## Slide 2: History of this Issue
May 2005 At TAC request, WMS asks Demand Side WG to work on the issue of an emergency load program to address 1-in-10-year LOLE
2005 ERCOT staff & DSWG subgroup research emergency demand response programs in other ISOs
Oct. 2005 DSWG presentation to WMS; WMS defers decision in light of PUC rulemaking
Oct. 2005 PUC resource adequacy draft rule includes Emergency Load Response (ELR) section; numerous parties submit comments
July 2006 ELR section dropped from proposed rule; deferred to Demand Response project (32852)
9/15/06 ERCOT proposes EILR program at PUC Demand Response Workshop
10/2/06 More discussion at second PUC Demand Response Workshop

## Slide 3: Emergency Interruptible Load Program
Purpose of the EILP:
To provide ERCOT Operations with an additional emergency tool to lessen the likelihood of involuntary firm load shedding (a.k.a. rolling blackouts)

## Slide 4: Emergency Interruptible Load Program
What the EILP is:
Service provided by loads willing to interrupt immediately prior to the need for involuntary firm load shedding, in exchange for a payment
  Deployed only in emergency situations, when no more resources are available at any price from the market or other sources in real time
  Part of EECP, deployed just prior to final step (rolling blackouts)
  Closest cousins: Black Start and RMR

## Slide 5: Emergency Interruptible Load Program
What the EILP is NOT:
It is not a market-based program in which loads bid into day-ahead or real-time markets. EILP loads:
  Cannot bid into Balancing Energy market
  Cannot bid into Ancillary Services markets
  Cannot participate as price-responsive load unless additional load is available for EILP
EILP will not suppress energy prices during an EECP event
It is not a resource that is deployed to recover or replace regular ancillary services
It is not a resource that will ever be deployed ahead of available market resources
It is not a backstop for insufficient planning reserve margins, or a tool to meet long-term capacity needs

## Slide 6: Emergency Interruptible Load Program
How the need for EILP relates to the Planning Reserve Margin:
Low reserve margin is related to this program ONLY as one indicator of an increased likelihood for the need
  EILP is less likely to be needed in times of large generation surpluses
EILP will NOT impact the reserve margin
  Will not be part of the reserve margin calculation
  Unlike LaaRs, which are built into the reserve margin calculation as an offset to total peak demand

## Slide 7: Emergency Interruptible Load Program
When the EILP may be needed:
Emergencies can occur at any time:
  Cold weather months (due to natural gas curtailment & higher forced outages)
  Shoulder months (due to unforeseen weather events & large amounts of scheduled maintenance)
  Traditional summer peaks
  Anytime, as may be caused by:
    generation outages (scheduled, forced or both)
    transmission outages beyond likely contingencies
    extreme weather events
    multiple simultaneous contingencies

## Slide 8: Emergency Interruptible Load Program
Background
  Under normal circumstances, adequate resources (RRS, NSRS, RPRS) are on line or available to deal with most situations
  Historical need for additional resources due to abnormal events (usually weather related)
    Cold weather events can lead to abnormally high load combined with fuel curtailments (Dec. 1989, Feb. 2003)
    Shoulder month events caused by unusual weather at unexpected times (100º weather on April 17, 2006, with 20% of capacity offline for seasonal maintenance)
  When abnormal events occur, additional ERCOT tools could reduce the possibility of a need for involuntary firm load shedding and the associated public health and safety risks

## Slide 9: ERCOT Emergency Operations
Current Operating Procedures
Event/Action | Trigger
Operating Condition Notice | Physical responsive reserve below 3300 MW
ADVISORY | Physical responsive below 3000 MW
ALERT: Start RMR units, suspend unit testing, deploy RPRS & NSRS | Physical responsive below 2500 MW
Emergency Electric Curtailment Plan | 
Step 1: Dispatch all generation & DC Ties, issue public media appeal | Physical responsive below 2300 MW
Step 2: Deploy LaaRs | Physical responsive below 1750 MW
Step 3: Instruct transmission operators to shed firm load | Frequency below 59.8 hz

## Slide 10: ERCOT Emergency Operations
A proposed new tool for the ERCOT toolbox
Event/Action | Trigger
Operating Condition Notice | Physical responsive reserve below 3300 MW
ADVISORY | Physical responsive below 3000 MW
ALERT: Start RMR units, suspend unit testing, deploy RPRS & NSRS | Physical responsive below 2500 MW
Emergency Electric Curtailment Plan | 
Step 1: Dispatch all generation, public media appeal, DC Ties | Physical responsive below 2300 MW
Step 2: Deploy LaaRs | Physical responsive below 1750 MW
Step 3: Instruct transmission owners to shed firm load | Frequency below 59.8 hz
New Step: Deploy EMERGENCY INTERRUPTIBLE LOAD

## Slide 11: EILP Deployment Scenario
Emergency Electric Curtailment Plan Event
Step 1 Step 2 ‘Step 2A’ Step 3
All available generation deployed
LaaRs deployed
EILP deployed
Rolling blackouts (firm load shedding)
(Moving MCPE to the price cap during EECP is currently under consideration by TPTF)
Loads respond to scarcity pricing

## Slide 12: Emergency Interruptible Load Program
Loads would be deployed:
  After all market-based resources have been deployed
  Under low frequency conditions
  Prior to rolling blackouts
Quantity would be based on averting historical firm load shedding events which have occurred in winter peak or shoulder months
  Initial proposal: 1000 MW, based on history
Need for program and quantity to be procured could be adjusted periodically based on various operating conditions
Low probability of deployment
Controlled load interruption vs. uncontrolled

## Slide 13: Advantages of the EILP
Shedding voluntary load from prepared end-use customers is preferred over involuntary load shedding from unprepared customers
Provides ERCOT operations an additional tool in emergency situations
Shedding load is 100% effective to maintain balance with generation
ERCOT believes that EILP cost will be lower than the societal cost of rolling blackouts

## Slide 14: Potential Program Characteristics
Procurement
  Loads, through their QSEs, would bid to provide service (similar to Black Start)
  Contract is with the QSE
  Initial 2-year contract term
    After that, evaluate annually
    Possible renewal or re-bid if deployments exceed predefined number of hours

## Slide 15: Potential Program Characteristics
Dispatching and Operations
  Dispatched By ERCOT thru QSEs
  Deployed as a single block after all existing generation resources and LaaRs are deployed
    Under low frequency conditions but before any firm load shedding
  Quick response required (10 minutes or less)
  Require interval data metering for measurement and verification
    But no telemetry or under frequency relay requirement
  Limit number of hours to be curtailed in any given year

## Slide 16: Potential Program Characteristics
Potential payment options offered by ERCOT at stakeholders’ request
  1 CAPACITY & ENERGY
    Initial up-front payment based on bids at time of contract award
    Pay for performance based on actual load response
      QSE receives energy imbalance credit equal to MWh delivered (based on validated performance) times the MCPE, or price cap in place
  2: Energy Only with DEFINED PRICE
    No up-front payment
    Energy-only payment for performance based on actual load response
      QSE receives a double energy imbalance credit/payment equal to:
        MWh delivered (based on validated performance)
        x MCPE price cap in place (guaranteed amount, known in advance)
        x 2
    Subscription would be first-come, first-serve (as opposed to competitive bidding)
      Similar to Standard Offer Programs
  3 Energy Only with COMPETITIVE PRICE
    No up-front payment
    Energy-only payment under a call agreement
    Open bid process (QSEs bid on customers behalf)
      ERCOT recommends a ‘descending clock auction’
    QSEs paid auction clearing price x MWh delivered (based on validated load performance)
  All options subject to clawback or penalty for underperformance

## Slide 17: Potential Program Characteristics
Clawback/penalty for underperformance
Eligible customer must not:
  Participate as LaaR
  Participate as BUL or voluntary load response unless sufficient EILP load is also available
ERCOT will verify:
  Actual curtailed demand based on review of 15-minute interval data
    Using actual load from last full interval prior to instruction, minus actual load from next full interval following 10-minute response period
  Prior performance under high price periods and 4 CP days
No energy payment will be provided (other than energy imbalance credit) if load underperforms
  If QSE has received a capacity payment (i.e., under payment option 1), it will be subject to performance-based clawback

## Slide 18: Potential Program Characteristics
Allocation (Option 1)
  Charged to QSEs representing load on load-ratio share
Allocation (Option 2)
  Allocate using RPRS methodology (including PRRs 666, 676 & 687)
    Short-scheduled LSEs bear a higher portion of the cost
ERCOT is open to recommendations on how to accommodate self-providing of EILP
Program should be open to QSEs serving both competitive and NOIE load

## Slide 19: Questions?