## Slide 1: ERCOT Tool to manage unexpected incremental load
December 13, 2006

## Slide 2: Disclaimer
The numbers presented in this presentation may or may not represent actual capabilities of a generic Combine Cycle unit. The numbers within this presentation are for the sole purpose of conveying the concept of stranded capacity.

## Slide 3: ERCOT’s Desire
Need a tool that can be used prior to interrupting load in order to minimize or prevent load interruption.

## Slide 4: Stranded Capacity
  Note: ERCOT demands a 10 minute window to execute Ancillary Services deployment
Max Use of Slow Response Duct Burner:
150 MW Deployment (350 to 500) @ 11.4 MW per min ramp ~ 13.2 min (70 MW@1.5/min & 80 MW@20/min)
LSL MW
LSL MW
Duct Burners
70 MW
1.5 MW/Min
Combine Cycle
430 MW
20 MW/Min
430 MW
No Use of Slow Response Duct Burner:
150 MW Deployment (280 to 430) @ 20 MW per min ramp ~ 7.5 min
280 MW
70 MW
80 MW
40 MW
110 MW
Blend of Slow and Fast Response Capacity:
150 MW Deployment (320 to 470) @ 15 MW per min ramp ~ 10 min (40 MW@1.5/min & 110 MW@20/min)
30 MW
Stranded
LSL MW
70 MW
Stranded
Inefficient use of Capacity:
Can Perform Incremental AS in the Remaining 2.5 minutes
Efficient use of Capacity:
But Violates 10 Minute Performance Rule
Maximizes AS Sales, but Still Strands a Portion of Capacity
500 MW CC Unit

## Slide 5: Proposed Concept
Activate Stranded Capacity that is online but not presently being offered into the market because of its negative effect on the performance of contractual Ancillary Services obligations
Ancillary Services must still be performed, but the Market Participant is allowed longer than 10 minutes to achieve the full performance of the Ancillary Services

## Slide 6: 5.6.5 Alert
If the Alert Notice is the result of a capacity short supply situation, QSEs with stranded capacity will provide ERCOT with the quantity of such stranded capacity that can become available if a waiver is issued from compliance of the SCE Performance and the Ancillary Services 10 minute ramp requirement

## Slide 7: 5.6.6 Emergency Notice
If the Emergency Condition is the result of a short supply situation, each QSE having reported stranded capacity during the Alert period, will update their Resource Plan to reflect the enabling of such incremental capacity. Each QSE shall load the enabled incremental capacity to its full capability. Each QSE that utilizes such capacity to deploy incremental energy will be considered to have received a VDI and a waiver from compliance for the SCE Performance and the Ancillary Services 10 minute ramp requirement.
If the short supply Emergency Condition continues, then the Emergency Electric Curtailment Plan procedures will be followed.

## Slide 8: 5.6.7.1 Restoration of Market Operations
ERCOT shall continue EECP until sufficient bids are received and deployed by ERCOT to eliminate the conditions requiring the EECP. Upon ERCOT notifying the market that the EECP is cancelled, each QSE that enabled capacity during Emergency Condition will unload the output of the Resource to its scheduled level. Each QSE shall update its Resource Plan to reflect the stranded capacity as unavailable.

## Slide 9: 5.6.8 Emergency Compensation
There will be no compensation other than normal settlement methods to Resources for the utilization of stranded capacity.

## Slide 10: Benefits
Tool (Stranded Capacity) is available on short notice (Probably more than 1,000 MW available)
Tool is available all seasons
No short term or long term contracts required
No incremental cost to loads
Minor system changes (if any)
Enables capacity, that is represented in the Planning Reserve calculations as available capacity, to become available (non-stranded)

## Slide 11
Comments?