# ERCOT Operations Report for ROS & OWG

# December 2006

## Frequency Control Disturbance (Less than 59.9 Hz or higher than 60.1Hz)

| Disturbance Data |
| --- |
| Time | Frequency (Hz) | Duration (mm:ss) | Details | Notes |
| 12/03/2006 01:04 | 60.109 | 00:18 | Unit Trip, and then overshot. |  |
| 12/03/2006 17:23 | 59.838 | 01:00 | Unit trip. 520MW lost |  |
| 12/09/2006 13:17 | 60.110 | 01:56 | Decreasing Reg Down Overshoot |  |
| 12/11/2006 00:04 | 60.103 | 00:04 | Large base power schedule changes |  |
| 12/11/2006 01:02 | 59.784 | 02:50 | Unit ran back around 780MW |  |
| 12/13/2006 04:20 | 59.873 | 00:25 | Unit ran back around 511MW | EECP followed |
| 12/14/2006 21:58 | 59.873 | 08:48 | Multiple units being taken off line |  |
| 12/14/2006 22:40 | 60.105 | 00:32 | Ran out of down reg available |  |
| 12/15/2006 23:15 | 59.894 | 00:10 | Unit trip. 520MW lost |  |
| 12/20/2006 10:48 | 59.893 | 00:08 | Unit trip. 430MW lost |  |
| 12/22/2006 02:54 | 59.792 | 01:40 | Unit trip. 2000MW lost | EECP followed |
| 12/25/2006 06:01 | 59.880 | 00:04 | Units trip. 475MW lost |  |
| 12/29/2006 17:36 | 59.891 | 00:06 | Unit trip. 600MW lost |  |

## Deployed Responsive (22) (Reported Above)

## Day-Ahead RMR and OOMC Capacity Purchases

| Historical RMR & OOMC Totals | Dec-05 | Nov-06 | Dec-06 |
| --- | --- | --- | --- |
| Austin | 4 | 19 | 11 |
| Bryan Area | 18 | 0 | 0 |
| Corpus | 9 | 0 | 0 |
| DFW | 34 | 3 | 27 |
| E RIO | 83 | 12 | 5 |
| Houston | 0 | 1 | 1 |
| Laredo | 40 | 66 | 90 |
| North | 4 | 1 | 0 |
| Northeast | 2 | 2 | 0 |
| San Antonio | 24 | 4 | 1 |
| South | 0 | 5 | 0 |
| W RIO | 63 | 80 | 62 |
| Western | 18 | 19 | 0 |
| Total | 299 | 212 | 197 |

| Dec 06 Data in detail | RMR | OOMC | RPRS | Total |
| --- | --- | --- | --- | --- |
| Austin | 0 | 11 | 32 | 43 |
| Bryan Area | 0 | 0 | 0 | 0 |
| Corpus | 0 | 0 | 2 | 2 |
| DFW | 0 | 27 | 0 | 27 |
| E RIO | 0 | 5 | 16 | 21 |
| Houston | 0 | 1 | 0 | 1 |
| Laredo | 90 | 0 | 0 | 90 |
| North | 0 | 0 | 0 | 0 |
| Northeast | 0 | 0 | 0 | 0 |
| San Antonio | 0 | 1 | 25 | 26 |
| South | 0 | 0 | 6 | 6 |
| W RIO | 0 | 62 | 5 | 67 |
| Western | 0 | 0 | 0 | 0 |
| Total | 90 | 107 | 86 | 283 |

http://www.ercot.com/mktinfo/services/rprsdr/index.html

## Yearly MTLF Error Comparison

| Month | MAPE for MTLF run at 16:00 Day Ahead (2005) | MAPE for MTLF run at 16:00 Day Ahead (2006) | MAPE for MTLF run at 16:00 Day Ahead (2006) with Standard Deviation |
| --- | --- | --- | --- |
| January | 5.02 | 4.79 | N/A |
| February | 3.47 | 4.81 | N/A |
| March | 3.41 | 4.95 | N/A |
| April | 3.37 | 5.59 | N/A |
| May | 4.21 | 3.59 | N/A |
| June | 3.91 | 2.65 | 3.46 |
| July | 5.22 | 2.62 | 3.29 |
| August | 4.86 | 2.09 | 2.61 |
| September | 6.24 | 4.03 | N/A |
| October | 4.51 | 3.63 | N/A |
| November | 4.53 | 3.28 | N/A |
| December | 5.95 | 3.44 | N/A |
| Average MAPE for Year | 4.56 | 3.79 | N/A |

## OOME / Congestion Management Activity:

Indicates congestion affected by outages

Indicates a Remedial action plan has been developed for the element

| Contingency | Overloaded Element | Days of Occurrences |
| --- | --- | --- |
| Menard - Gillespe 138 kV | Menard 138/69 kV | 8 |
| Temple Pecan Creek - Tradinghouse & Lake Creek - Temple Switch 345kV | Evant - Adamsville 138kV | 7 |
| Temple Pecan Creek - Tradinghouse & Lake Creek - Temple Switch 345kV | Lake Creek - Temple Pecan Creek 138kV | 6 |
| Fisher Rd - Oklaunion & Fisher Rd - Bowman 345kV | Vernon - Grayback 69kV | 4 |
| Fisher Rd - Oklaunion & Fisher Rd - Bowman 345kV | Lake Pauline 138/69 kV auto | 4 |
| Jack County - Hill Top 138 kV | Rhome - Decatur 138 kV | 4 |
| Temple Pecan Creek - Tradinghouse & Lake Creek - Temple Switch 345kV | Goldthwaite - Evant | 4 |
| Lon Hill - Whitepoint 345 kV | Whitepoint Series Reactor | 3 |
| Calavers- Braunig & Cagnon 345 kV | Medical Center - Hamilton Wolf 138 kV | 3 |
| Temple Pecan Creek - Tradinghouse & Lake Creek - Temple Switch 345kV | Temple Switch - Pecan Creek 138 kV | 3 |
| Sandow 345/138 kV | Sandow - Elgin Switch 138 kV | 2 |
| Sandow Unit 4 | Sandow 345/138 kV auto | 2 |
| STP - Skyline & Whitepoint 345 kV | Blessing - Lolita 138 kV | 2 |
| Comanche Peak - Decordova & Wolf Hollow - Rocky Creek 345kV | Concord 345/138kV Auto | 1 |
| Elgin Switch - Sandow SES | Sandow SES - Salty 138 kV | 1 |
| Asherton - Excondido 138 kV | Asphalt Mines - Uvalde 138 kV | 1 |
| Asherton - Excondido 138 kV | San angelo Concho - San Angelo lake Nasworthy 138 kV | 1 |
| Enterprise - Trinidad & Matin Lake - Stryker Creek 345 kV | Nacogdoches SE 345/138 kV auto | 1 |
| Lon Hill - Whitepoint 345 kV | Port Arkansas - Mustang Island 69 kV | 1 |
| Sandow SES - Taylor 138 kV | Elgin Switch - Taylor 138 kV | 1 |
| Sonora - Friend Ranch 138 kV | San Angelo Concho - San Angelo Lake Nasworthy 69 kV | 1 |
| Brownwood - Goldthwaite 138 kV | Copperas Cove TU - Killeen Clark Road 138 kV | 1 |
| Sandow Switch - Austrop 345 kV | Copperas Cove TU - Killeen Clark Road 138 kV | 1 |
| Temple Switch - Bell County 138 kV | Seaton - Poage 69 kV | 1 |
| Comanche Switch - Comanche Peak 345 kV | Copperas Cove TU - Killeen Clark Road 138 kV | 1 |
| Dilley Switch - San Miguel Switch 138 kV | Derby - Pearsall 69 kV | 1 |
| Twin Oaks - Gibbons Creek 345 kV | Watson Chapel - Robinson 138 kV | 1 |

## Zonal OC1’s

| CSC | Days |
| --- | --- |
| South - Houston | 12 |
| South - North | 1 |
| North - Houston | 0 |
| Northeast - North | 0 |
| West - North | 0 |
| North - West | 0 |

## New RAPs

Loss of Temple Pecan Creek – Tradinghouse / Temple Switch – Lake Creek 345 kV Double Circuit overloads Evant – Adamsville 138kV line.

## New Procedures/ Forms/Operations Bulletins

| Date | Subject | Bulletin No. |
| --- | --- | --- |
| 12/12/2006 | Frequency Control Desk - V3R49 | 306 |
| 12/11/2006 | Frequency Control Desk - Relief of Non Spin Obligation | 305 |
| 12/11/2006 | Frequency Control Desk - Fast Start Emergency Schedules to SPP | 304 |
| 12/11/2006 | Frequency Control Desk - Maintain DC Tie Spreadsheet | 303 |
| 12/04/2006 | Shift Supervisor Desk - SMP Alarm | 302 |

## Blackout/Load Shed incidences

None

## EECP

12/13 Implemented EECP

12/22 Implemented EECP

12/23 Implemented EECP

## Major system voltage problems

12/5 Loss of the Sandow 345/138kV auto caused low voltage in the area.

## Voltage Instructions

None

## Major Computer Problems, Enhancements & Fixes

RTB intervals - 0

AGC Control lost - 0 minutes

Database Loads

12/05/2006

12/06/2006

12/20/2006

12/21/2006

12/31/2006

## Communication

None

## ERCOT peak (Unofficial)

12/08/2006	07:00	44506MW

## OCN, Advisory, Alerts, and Emergency Notices:

### Insufficient Capacity:

| Date | Start | End | Details | Subject |
| --- | --- | --- | --- | --- |
| 12/3/2006 | 8:00 | 10:00 | Capacity shortage for hours 19:00 to 21:00. | OCN |
| 12/2/2006 | 8:00 | 10:16 | Adjusted Responsive Reserve is below 3000MW's. | Advisory |
| 12/3/2006 | 6:56 | 13:50 | Adjusted Responsive Reserve is below 3000MW's. | Advisory |
| 12/3/2006 | 17:31 | 23:00 | Alert issued due to Adjusted Responsive Reserve is below 2500MW's. | Alert |
| 12/4/2006 | 19:22 | 22:08 | Adjusted Responsive Reserve is below 3000MW's. | Advisory |
| 12/5/2006 | 6:39 | 8:00 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/6/2006 | 7:09 | 10:30 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/6/2006 | 17:40 | 22:05 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/7/2006 | 17:32 | 24:00 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/8/2006 | 0:15 | 2:03 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/8/2006 | 6:39 | 11:37 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/8/2006 | 17:37 | 20:30 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/9/2006 | 0:15 | 12:55 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/9/2006 | 8:21 | 12:55 | Adjusted Responsive Reserve below 2500MW's. | Alert |
| 12/9/2006 | 17:30 | 22:30 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/10/2006 | 7:04 | 21:45 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/10/2006 | 12:27 | 15:30 | Adjusted Responsive Reserve below 2500MW's. | Alert |
| 12/11/2006 | 6:30 | 12:30 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/11/2006 | 18:00 | 21:40 | Adjusted Responsive Reserve below 3000MW's. | Advisory |
| 12/13/2006 | 6:20 | 8:40 | Adjusted Responsive Reserve less than 3000 MW | Advisory |
| 12/13/2006 | 6:39 | 7:30 | Adjusted Responsive Reserve less than 2500 MW | Alert |
| 12/13/2006 | 6:52 | 7:16 | EECP Step 1 Adjusted Responsive Reserve less than 2300 MW | EECP Step 1 |
| 12/13/2006 | 17:50 | 21:55 | Adjusted Responsive Reserve less than 3000 MW | Advisory |
| 12/14/2006 | 18:38 | 21:55 | Adjusted Responsive Reserve less than 3000 MW | Advisory |
| 12/15/2006 | 10:25 | 12:45 | Adjusted Responsive Reserve less than 3000 MW | Advisory |
| 12/15/2006 | 18:09 | 21:45 | Adjusted Responsive Reserve less than 3000 MW | Advisory |
| 12/16/2006 | 9:15 | 13:45 | Adjusted Responsive Reserve less than 3000 MW. | Advisory |
| 12/16/2006 | 17:51 | 22:02 | Adjusted Responsive Reserve less than 3000 MW. | Advisory |
| 12/16/2006 | 17:58 | 18:25 | Adjusted Responsive Reserve less than 2500 MW | Alert |
| 12/17/2006 | 1:02 | 4:11 | Adjusted Responsive Reserve less than 3000 MW. | Advisory |
| 12/17/2006 | 10:20 | 16:40 | Adjusted Responsive Reserve less than 3000 MW. | Advisory |
| 12/17/2006 | 17:45 | 20:51 | Adjusted Responsive Reserve less than 3000 MW. | Advisory |
| 12/18/2006 | 14:06 | 21:54 | Adjusted Responsive Reserve less than 3000 MW. | Advisory |
| 12/19/2006 | 10:13 | 21:20 | Adjusted Responsive Reserve less than 3000 MW. | Advisory |
| 12/20/2006 | 17:55 | 19:30 | Adjusted Responsive Reserve less than 3000 MW. | Advisory |
| 12/22/2006 | 3:03 | 4:07 | Implemented EECP Step 1 - Adjusted Responsive Reserve less than 2300 MW | EECP Step 1 |
| 12/22/2006 | 4:07 | 8:37 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/22/2006 | 22:15 | 23:15 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/23/2006 | 17:10 | 24:00 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/23/2006 | 17:45 | 23:45 | Adjusted Responsive Reserve below 2500 MW. | Alert |
| 12/23/2006 | 18:10 | 20:45 | Implemented EECP Step 1 - Adjusted Responsive Reserve less than 2300 MW | EECP Step 1 |
| 12/24/2006 | 0:15 | 0:30 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/24/2006 | 9:08 | 14:31 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/25/2006 | 18:30 | 24:00 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/26/2006 | 0:15 | 11:04 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/26/2006 | 18:15 | 0:00 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/27/2006 | 0:00 | 0:20 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/28/2006 | 17:45 | 21:00 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/29/2006 | 10:05 | 15:00 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/30/2006 | 10:00 | 13:10 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/30/2006 | 18:15 | 24:00 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/31/2006 | 0:15 | 10:15 | Adjusted Responsive Reserve below 3000 MW. | Advisory |
| 12/31/2006 | 18:00 | 24:00 | Adjusted Responsive Reserve below 3000 MW. | Advisory |

### Transmission:

| Date | Start | End | Details | Subject |
| --- | --- | --- | --- | --- |
| 12/1/2006 | 0:15 | 24:00 | Transmission Emergency for the Del Rio Area | Emergency |
| 12/1/2006 | 5:24 | 22:22 | Transmission Alert for the loss of Sonora - Friend Ranch 138kV overloads San Angelo Concho - San Angelo Live Oak 69kV beyond first contingency limits. | Alert |
| 12/2/2006 | 0:15 | 23:00 | Transmission Emergency for the Del Rio Area | Emergency |
| 12/4/2006 | 6:58 | 10:05 | Transmission Alert issued for the loss of Burnet - Wirtz 138kV overloads Coronado 138/69kV AT4 Autotransformer beyond first contingency limits. | Alert |
| 12/5/2006 | 1:27 | 1:35 | XXXX tripped with 646 MW, ERCOT load 33100 MW | Mkt Notice |
| 12/5/2006 | 5:45 | 22:30 | Transmission Alert issued due to the forced outages in the XXXX area causing low voltage. | Alert |
| 12/5/2006 | 6:36 | 22:30 | The XXXX limit was changed from 1000 MW's to 130 MW's due to forced outages and in accordance with Section 2.2.2 of the Transmission Security Desk procedures. | Mkt Notice |
| 12/7/2006 | 15:20 | 15:50 | Transmission Alert issued for the loss of Sandow SES Unit #4 overloads Sandow SES 345/138kV Autotransformer beyond first contingency limits. | Alert |
| 12/13/2006 | 4:21 |  | XXXX tripped with 363mw | Mkt Notice |
| 12/20/2006 | 18:00 | 24:00 | South - Houston limit raised to 2300 mws by ERCOT Engineering. | Mkt Notice |
| 12/22/2006 | 2:52 | 4:30 | XXXX tripped due to low voltage, 210 MW was lost. | Mkt Notice |
| 12/22/2006 | 2:54 | 3:03 | XXXX tripped with 513 MW's, XXXX tripped with 804 MW's, and XXXX tripped with 129 MW's. | Mkt Notice |
| 12/29/2006 | 17:07 | 24:00 | XXXX to XXXX OC1 limit was lowered from 3420 to 1750 due to forced outages, storm damage. | Mkt Notice |

### Weather:

| Date | Start | End | Details | Subject |
| --- | --- | --- | --- | --- |
| 12/1/2006 | 0:15 | 24:00 | Weather Advisory issued for 12/1 and 12/02/06 | Advisory |
| 12/2/2006 | 0:15 | 10:16 | Weather Advisory issued for Saturday December 2. | Advisory |
| 12/3/2006 | 15:00 |  | Advisory - Weather for Monday 12/04/06 morning peak. | Advisory |
| 12/4/2006 | 0:15 | 10:45 | Advisory - Weather for Monday 12/04/06 morning peak. | Advisory |
| 12/7/2006 | 1:00 | 24:00 | Weather advisory issued for Thursday evening, Friday morning and evening peaks due to arctic air in the state. | Advisory |
| 12/8/2006 | 0:15 | 16:00 | Weather advisory issued for Friday morning and evening peaks due to arctic air in the state. | Advisory |
| 12/29/2006 | 15:05 | 24:00 | Weather Operation Condition Notice (OCN) issued due to severe weather developing across the ERCOT region. | OCN |

### Miscellaneous:

| Date | Start | End | Details | Subject |
| --- | --- | --- | --- | --- |
| 12/7/2006 | 9:50 | 10:20 | A local failover was performed on the EMMS and IT also stopped web services for about 10 minutes to perform this month's migration. | Misc |
| 12/15/2006 | 1:15 | 3:30 | NOAA issued Geomagnetic Disturbance Warning K-8 | Misc |
| 12/20/2006 | 7:15 | 7:30 | ERCOT held interval 07:15 due to bad short term forecast. Resumed at 07:30. | Misc |
| 12/21/2006 | 9:20 | 10:00 | ERCOT completed planned database load. | Misc |
| 12/22/2006 | 2:58 | 3:58 | VDI giving to all QSE’s to deploy remaining LAAR’s that were bid in for Responsive Reserve Service due to potential DCS Event. | Misc |
| 12/24/2006 | 16:25 | 20:00 | Operation Condition Notice (OCN) issued due to insufficient BES bids for intervals 1900 thru 2200. | OCN |
| 12/31/2006 | 23:45 | 24:00 | Interval Ending 24:00 failed to run during a planned failover Interval 23:45 deployments were held and Resumed with 00:15. | Misc |

# Text boxes

| ID | Time of deployed | Duration (h:mm:ss) | Max Deployed (MW) |
| --- | --- | --- | --- |
| 1 | 12/01/2006 22:06 | 0:10:06 | 270.41 |
| 2 | 12/03/2006 00:25 | 0:09:28 | 266.25 |
| 3 | 12/03/2006 17:24 | 0:18:32 | 476.06 |
| 4 | 12/05/2006 01:27 | 0:12:48 | 382.73 |
| 5 | 12/05/2006 06:01 | 0:05:42 | 209.82 |
| 6 | 12/08/2006 22:04 | 0:05:04 | 253.76 |
| 7 | 12/11/2006 01:02 | 0:17:32 | 773.76 |
| 8 | 12/13/2006 04:20 | 0:13:20 | 511.68 |
| 9 | 12/14/2006 21:58 | 0:24:34 | 525.21 |
| 10 | 12/15/2006 23:15 | 0:08:54 | 395.20 |
| 11 | 12/16/2006 23:00 | 0:08:56 | 436.80 |
| 12 | 12/17/2006 12:12 | 0:05:12 | 327.60 |
| 13 | 12/18/2006 22:03 | 0:05:32 | 317.20 |
| 14 | 12/20/2006 01:04 | 0:09:54 | 332.82 |
| 15 | 12/20/2006 10:49 | 0:06:32 | 400.40 |
| 16 | 12/22/2006 02:52 | 0:30:16 | 2102.00 |
| 17 | 12/25/2006 06:01 | 0:13:14 | 468.00 |
| 18 | 12/25/2006 17:43 | 0:17:38 | 338.01 |
| 19 | 12/27/2006 07:23 | 0:05:08 | 338.01 |
| 20 | 12/29/2006 05:02 | 0:04:44 | 275.61 |
| 21 | 12/29/2006 17:36 | 0:06:54 | 514.81 |
| 22 | 12/31/2006 17:04 | 0:13:06 | 327.60 |