## Slide 1: Texas Nodal Network Modeling and Telemetry TAC Meeting By Raj Chudgar, ERCOT Thursday, 01/04/2007

## Slide 2: NMT – Network Operations Modeling & Telemetry - Project
Agenda
  Network Model Data Update
  Measurement Weights Modeling
    Analysis Overview
    Recommendations and Next Steps
  Summary

## Slide 3: NMT – Network Operations Modeling & Telemetry - Project
Model Data Issues Progress by MP – as of 12/22/2006
Note 1: Blank indicates MPs that ERCOT has not contacted to date
Note 2: NMT inherited ~400 legacy model issues

## Slide 4: NMT – Network Operations Modeling & Telemetry - Project
  Measurement Weights Modeling

## Slide 5: NMT – Network Operations Modeling & Telemetry - Project
Measurement Weights Analysis Overview
  Worked Jointly with ERCOT Operations SE staff to identify areas to tune
  Setup Tuning Environment with near real-time feeds from Production
    Measurement weights were re-defined
    Implemented a software change to add plausibility checks on negative load telemetries
    Added plausibility checks for unit capability curves

## Slide 6: NMT – Network Operations Modeling & Telemetry - Project
Measurement Weights Analysis - Tuning Environment Results
  The maximum bus mismatch (Mw/Mvar) after SE convergence were reduced to about 5Mw and 5Mvar.
  The maximum difference in Mw/Mvar flows between SE and Power Flow (RTCA base case) were reduced to about 5Mw and 5Mvar.
  The performance index was improved.
Next Steps
  Continue to compare Tuning Environment results to Production thru January 2007
  Report results to the Operations Group
  Determine implementation plan with the Operations group and implement

## Slide 7: NMT – Network Operations Modeling & Telemetry - Project
Summary
  Major Model clean-up underway
    Target to complete by 3/31/2007
  Major effort to reduce critical measurements and improve observability underway
    Target to have all justifications and schedules for new implementations by 3/31/2007
    Implementation schedule will be published end of 1Q2007
  Measurement Weights tuning recommendations to be implemented into Production
  ERCOT will continue to provide progress reports to TPTF, TAC, and ROS on a regular basis