## Slide 1: PRR 705 ERCOT Emergency Interruptible Load Service
PRS
January 22, 2007

## Slide 2: Background
May 2005 At TAC request, WMS asks Demand Side WG (DSWG) to work on the issue of an emergency load program to address 1-in-10-year Loss of Load Event (LOLE)
2005 ERCOT staff & DSWG subgroup research emergency demand response programs in other ISOs
Aug. 2005 TAC rejects new Ancillary Service for alternative fuels; cites ongoing consideration of ‘demand-side services for emergency curtailments’ as one alternative
Oct. 2005 DSWG presents emergency Load proposal to WMS; WMS defers decision in light of PUC rulemaking
Oct. 2005 PUC resource adequacy draft rule includes Emergency Load Response (ELR) section; numerous parties submit comments
July 2006 ELR section dropped from proposed rule; deferred to Demand Response project (32853)
Sept./Oct. 2006 ERCOT proposes Emergency Interruptible Load (EIL) program at PUC Demand Response Workshop & presents to TAC and WMS
Oct. 2006 Commissioners propose parallel rulemaking & Protocol development; WMS instructs EIL Task Force to deliver PRR by 12/06

## Slide 3: Recent History
Dec. 2006 WMS votes to consider energy-only versions of the EIL Service program & endorses PRR draft proposed by Reliant/TXU
At same meeting, ERCOT expresses concern that none of the PRR drafts can be implemented in time for April 2007 procurement, and states intention to file its own version as an interim alternative
Dec. 2006 Reliant/TXU draft is filed as PRR703 with EIL TF as sponsor
Dec. 2006 PRR702 filed by Oxy, Eagle Energy, & EnerNOC
Jan. 2007 PRR704 filed by steel mills
Jan. 2007 ERCOT alternate/interim version filed as PRR705

## Slide 4: Emergency Interruptible Load Service
Purpose:
To provide ERCOT Operations with an additional emergency tool to lessen the likelihood of involuntary firm Load shedding (a.k.a. rolling blackouts)
Description:
Service provided by Loads willing to interrupt immediately prior to the need for involuntary firm Load shedding, in exchange for a payment
  Deployed only in emergency situations, when no more Resources are available at any price from the market or other sources in real time
  New Step 3 of Emergence Electric Curtailment Plan (EECP)

## Slide 5: ERCOT Emergency Operations under PRR 705
A new tool for the ERCOT toolbox
Event/Action | Trigger
Operating Condition Notice | Physical responsive reserve below 3300 MW
ADVISORY | Physical responsive below 3000 MW
ALERT: Start RMR units, suspend unit testing, deploy RPRS & NSRS | Physical responsive below 2500 MW
Emergency Electric Curtailment Plan | 
Step 1: Dispatch all generation, public media appeal, DC Ties | Physical responsive below 2300 MW
Step 2: Deploy LaaRs | Physical responsive below 1750 MW
Step 4: Instruct transmission owners to shed firm load | Frequency below 59.8 hz
New Step 3: Deploy EMERGENCY INTERRUPTIBLE LOAD

## Slide 6: ERCOT Firm Load Shed Events
December 22, 1989
  “12 Days of Christmas” – extended sub-freezing weather
  500 MW of firm Load shed at approx. 7 AM
April 17, 2006
  100 degrees with 20% of generation fleet down for planned maintenance
  1,000 MW of firm Load shed approx. 4 PM
Neither case was related to summer peaking
In both cases, firm Load shedding preserved the system
In both cases, EIL Service could have avoided the need for firm load shedding if program was adequately subscribed and Loads performed

## Slide 7: PRR 705: ERCOT Proposal
ERCOT’s EIL proposal (PRR705):
  Can be implemented in time for April EIL procurement assuming Urgent approval
  Can serve as an interim proposal
  Could also serve as a full-time solution if other PRRs are either not approved or fail to attract subscribers
  Is designed to keep overall cost consistent with low risk of actual deployment
  Is designed to balance low cost with flexibility for Loads

## Slide 8: PRR 705: EIL Procurement
Black Start-style bid solicitation
  Load Resources or QSEs bid to provide service
Procured for 4-month blocks built around 4CP months
Loads may bid to provide service during business hours (8-8 M-F on ERCOT Business Days) or non-business hours, or both
Loads are paid a capacity payment as bid to be available for interruption through contract period
  Loads may schedule downtime (i.e., for maintenance) of up to 2% of committed hours in contract period at no penalty
  Maximum of 2 deployments or 8 hours of deployment per contract period
Cost of service is capped at $___ per year
  Amount purposely left blank to obtain market feedback on the appropriate cost of the service

## Slide 9: Cost/Value Matrix

## Slide 10: PRR 705: Operations
EILS deployed to maintain frequency after all market-based Resources have been exhausted (i.e., after RRS depleted)
Dispatched through single VDI hotline call to QSEs
10-minute response required
Deployed as a block, similar to LaaRs
  500 MW floor on procurement
  1,000 MW cap on procurement
ERCOT may instruct firm Load shed even if 10-minute response period has not yet expired if conditions warrant
Recalled after all RRS restored and LaaRs have been recalled
  EILs have up to 10 hours to return to service

## Slide 11: PRR 705: Performance & Payment
Default baseline & event compliance method:
  Loads are assigned to their own unique baseline, based on historical meter data, weather & calendar factors
    Uses ERCOT’s existing industry-standard Load profiling tools
  Baseline will validate size of load’s MW bid, and establish Load’s expected level at time of deployment
  EILS Resource required to deploy contracted amount from that baseline level
Alternate baseline:
  Some Loads (e.g., highly fluctuating or batch process Loads) cannot be accurately profiled in the default method
  Loads in alternate baseline will be permitted to bid their average (not peak) Load over prior 12 months, and must shed to declared minimum during an event

## Slide 12: PRR 705: Performance & Payment
Payment for availability:
  QSEs are paid no later than 60 days after end of contract period
  Payment adjusted based on availability factor:
    100% payment if 95% of load was available 95% of hours
    If below 95% of hours, payment is adjusted pro-rata
Payment for performance in an EIL deployment event:
  Loads must shed 95% of committed capacity within 10 minutes
  Successful performance guarantees a minimum of 50% of capacity payment
Compliance & Testing:
  ERCOT may conduct unannounced Load shed tests at any time
  ERCOT may suspend or revoke an EIL’s qualification for lack of availability, failure to perform in an event, or failing a test

## Slide 13: Questions?