## Slide 1: Using Additional NSRS to Reduce Step2 RPRS
Wholesale Market Subcommittee
February 21, 2007

## Slide 2: NSRS Concepts
System-based service
NSRS obligations can be self-provided by QSEs
Probability of energy dispatch at LSL is zero for expected normal conditions
PRR650 MCPE adjustments minimize adverse impacts on energy markets when deployed

## Slide 3: RPRS Concepts
Step1 RPRS is a location-based, local area service:
Procurement is based on applying local constraints
Unlike Regulation, Responsive and Non-Spin, Step1 RPRS is not procured for system purposes
Probability of energy dispatch at LSL is 100% for expected normal conditions

## Slide 4: RPRS Concepts (continued)
Step2 RPRS is a non-locational, system-based service:
It is not locally procured (i.e., procurement should not be based on applying local constraints)
It is not zonally procured (i.e., procurement should not be based on zonal constraints)
Step2 RPRS obligations cannot be self-provided currently by QSEs
Probability of energy dispatch at LSL is 100% for expected normal conditions

## Slide 5: RPRS Impacts
ERCOT has provided data:
Hourly RPRS aggregate LSL energy
Separately stated for Step1 and Step2 procurements
RPRS data was compared to hourly UBES deployments
For Sep-Dec, 2006:
Step2 RPRS was procured in 6% of all hours
The amount of Step2 RPRS LSL energy exceeded the total amount of UBES deployments in some hours
At times Step2 RPRS LSL energy is multiples of UBES deployments

## Slide 9: Resource Commitment
Every MW of RPRS at LSL has a 100% probability of dispatch, therefore:
  BES price signals move in a direction opposite of encouraging self-commitment.
On the other hand, NSRS has a near-zero probability of dispatch, therefore:
  if additional NSRS was utilized to reduce Step2 RPRS, BES price signals would be more compatible with the goal of encouraging self-commitment.

## Slide 10: Conclusions
Unlike NSRS, RPRS interferes with the proper functioning of energy markets by distorting the BES market
The ERCOT-provided RPRS data indicates that there may have been opportunities for ERCOT to procure additional NSRS, instead of Step2 RPRS, since Step2 RPRS was not, or should not have been, procured to resolve or avoid local or zonal constraints
Excessive Step2 RPRS procurement:
  Is not compatible with an Energy-Only market design;
  Moderates supply-side investment incentives;
  Discourages price-responsive demand participation; and
  Does nothing to encourage Resource Adequacy

## Slide 11: Recommendation
ERCOT should take all steps operationally feasible to procure:
  RPRS for local constraints only, when possible;
  Additional NSRS for other system-based purposes (including but not limited to load forecast uncertainty and capacity insufficiency) up to the limit of all available on-line and off-line NSRS; and
  Step2 RPRS to the extent additional NSRS is not available

## Slide 12: ROS Follow-Up
Work with ERCOT Operations Staff:
  Pros and Cons
  Substitutability
  Changes in procedures, protocols or both
  Discuss at next ROS meeting