## Slide 1: ERCOT
COPS
Round 2
Sample Design Review
April 10, 2007

## Slide 2: Overview
Reference to PUCT Rule 25.131 Section C
Background information
Sample design overview
Class level dollars by sample cells
Precision versus sample size
Sample allocation optimization
Additional Round 2 considerations
Final Design and Round 1 sample point retention

## Slide 3: PUC Rule §25.131, Load Profiling and Load Research
Assigns responsibility for load research sample design to ERCOT
  Determine study objectives
  Define population
  Determine accuracy level
  Select sampling technique
Assigns data collection responsibility to TDSPs
If a TDSP has a separate load research sample, ERCOT shall coordinate sample designs
ERCOT shall consult with TDSPs on load research data transfer process

## Slide 4: PUC Rule §25.131, Load Profiling and Load Research
Section (C):
  Load research responsibility. Each TDU shall perform load research to support ERCOT’s load profiling activities, as directed by ERCOT.
      ERCOT shall be responsible for load research sample design and sample point selection for ERCOT-directed load profiling and load research samples. ERCOT shall coordinate with each TDU to optimize load research programs of both ERCOT and the TDU. The same samples shall be used to support both the TDU’s load research activities and ERCOT’s load profile research needs whenever reasonably possible. Each TDU shall coordinate with ERCOT to synchronize its load research cycles and sample replacement with those of ERCOT.
      ERCOT, in consultation with the TDUs, shall specify the manner of data collection for ERCOT load profile research samples and the means and frequency of transmission of such information to ERCOT. Each TDU shall adhere to the specifications for data collection and transmission specified by ERCOT.
      A TDU may recover its reasonably and necessary costs incurred in performing load profile research as required by this section.
      This section shall not be interpreted to require a TDU to redeploy any existing samples that were deployed less than five years before the effective date of this section, although this section shall also not be interpreted as addressing the appropriateness of continued deployment of existing TDU samples apart from the ERCOT request to do so. Notwithstanding the foregoing, the TDU shall deploy additional samples as requested by ERCOT in order to support ERCOT’s load profiling activities.

## Slide 5: Background Information
For Round 1 of the LRS sample design ERCOT offered to coordinate our sample designs with all of the TDSPs
  TXU-ED was interested in coordination
  ERCOT incorporated their sample into ours
  ERCOT and TXU have already agreed to do this again for Round 2
ERCOT presented an initial LRS precision analysis and sample design options for Round 2 at the June 28, 2006 PWG meeting
  Extensive discussion with Market participants took place
ERCOT presented an updated LRS precision analysis at the February 27, 2007 PWG meeting.
  AEP suggested that ERCOT perform analysis to determine if the recommended separate primary voltage samples were necessary
  ERCOT had a follow-up meeting with Kathy Scott on March 5 to discuss TDSP concerns related to the recommended complete sample replacement for Round 2
Based on TDSP input, ERCOT revisited the Round 2 sample design for the March 27, 2007 PWG meeting.
  ERCOT incorporated retention of some Round 1 sample points for Round 2
  ERCOT reduced Round 2 requirement for Primary Voltage Sample Points

## Slide 6: Round 1 Sample High Level Design
Round 1 Sample was designed and selected mid-2004
  Approximately half-sized samples were selected to facilitate load research start-up process
  The need to increase sample sizes in subsequent rounds was expected and communicated to the market during Round 1 planning
Population was defined with 48 Sample Cells (one for each of the Profile Type / Weather Zone Combinations)
High level sample design process consists of determining total sample size and allocating sample points to each cell

## Slide 7: Sample Design Overview
Round 2 High Level Sample Design
Lodestar
ESIID
Profile Assignment
Usage
Total Sample Size
Allocation To Sample Cells
Expected Precision
Round 2 Detail Sample Design
Round 2 Sample Selection
Round 1 Sample Analysis
Round 1 Sample Size
Interval Mean kWh
Interval Precision
Stratum Boundaries
Stratum Allocation
TDSP Sample Lists Selected Sample Points
Alternate Sample Points

## Slide 8: Dollars by Profile Type
Dollars = Σ (MWh * MCPE)
Is accuracy more important for RESLOWR (33.4% of Dollars) than for BUSNODEM (1.6% of Dollars)?
9.8%
12.4%
16.3%
1.6%
26.3%
33.4%

## Slide 9: Sample Cell Dollars
Cells shown in descending order by dollars
Top 5 cells account for 54% of the dollars
Bottom 28 cells account for only 10% of the dollars
Bottom 10 cells account for 1% of the dollars

## Slide 10: Precision vs Sample Size
Precision improvement varies across sample cells and across intervals
Increasing sample size has a diminishing return on precision improvement
Thus the impact over a year of adding sample points varies by sample cells
Illustration of the relationship between precision and sample size for a median interval by Profile Type

## Slide 11: Sample Allocation Optimization
Minimum Sample Size
  For Round 1 analysis, profile migration caused numerous issues due to small sample sizes in some cells
  For Round 2 minimum sample size per sample cell will be 120
Maximum Sample Size
  Maximum set to avoid excessive sampling in a few sample cells
  Maximum for Business sample cells set to 400
  Maximum for Residential sample cells set to 600
Optimization method: Iteratively allocate increments of 20 sample points to a selected sample cell
  At each step, allocate points to produce the most improvement in reducing dollar estimation error
  Where, dollar estimation error = (Precision × Dollars) summed across all intervals
The allocations are based on both
  The Dollars associated with each of the sample cell in each interval, and
  The precision improvement that would be realized by adding 20 sample points, and the diminishing return on that improvement

## Slide 12: Examples of Iterative Allocation at Selected Sample Sizes
Reducing Dollar estimation error (Precision × Dollars) summed across all intervals

## Slide 13: Annualized Dollar Error Reduction Based on Sample Size Increases
Non - Optimized
Allocation of points
Optimized Allocation of Additional Points
Round 1
Min sample size
Round 2

## Slide 14: Oil and Gas Sample Treatment
Lists of known Oil and Gas ESIIDs were provided by TDSPs
These ESIIDs will be excluded from the population and sample for Round 2
  Many are expected to migrate to BUSOGFLT beginning in September 2007
  For Round 2 analysis, sample estimates will be adjusted to account for known Oil and Gas ESIIDs which have not migrated at that time

## Slide 15: Primary Voltage Sample Review
ERCOT followed up on AEP suggestions
Four Business sample cells have a significant saturation of primary voltage ESIIDs/energy
These cells will have a separate primary voltage stratum added to their sample design with 40 additional sample points allocated to that stratum
For all other cells, primary voltage ESIIDs will be grouped with secondary voltage ESIIDs

## Slide 16: Final Round 2 High Level Design
Total sample size 9,160
Round 2 Sample

## Slide 17: Round 1 Sample Point Retention
Round 1 sample points will be retained if they have the same profile assignment as when initially selected … lists have been distributed
Round 1 primary voltage sample points are not eligible for retention because of sample point weighting issues
Non-retained sample points may be selected for the Round 2 sample
TDSPs should consider waiting until Round 2 sample list is provided to start recorder removal

## Slide 18: Next Steps
ERCOT will complete detail sample design
  Stratification within sample cells
  Allocation of sample points to strata within sample cells
Sample lists will be provided to TDSPs prior to the April PWG meeting
PWG will discuss installation timelines for the new IDR installs and other issues related to Round 2
PWG will work on LPG Section 15 to reflect PUCT Rule and procedures being adopted to conduct load research in the ERCOT market

## Slide 19: Questions