## Slide 1: Changes Resulting from February RPRS Market Failure
Brandon Whittle
Supervisor, Market Support

## Slide 2: Failure of 02/16/07 RPRS (run on 02/15/07)
QSE submitted an unreasonably high HSL in Resource Plan
SFT didn’t converge causing RPRS to fail
ERCOT identified the QSE with incorrect HSL
QSE updated the Resource Plan for the HSL
ERCOT re-executed RPRS but it failed again since the original Resource Plan was used
ERCOT was unable to clear and close the RPRS Market
ERCOT was unable to open an adjustment RPRS Market since the Day-Ahead RPRS Market was not closed
ERCOT Proposed Fixes for RPRS Market Failure
ERCOT Proposed Fixes for RPRS Market Failure
T i m e l i n e

## Slide 3: ERCOT Fixes for the RPRS Failure
Fix1: Add Resource Plan Validation for HSL to prevent incorrect HSL entry
  Estimated Migration time is end of May, 2007
  Market Notice before implementation
Fix2: Capture the latest Resource Plan for RPRS Rerun in case of RPRS failure
  Estimated Migration time is end of April, 2007
Fix3: Allow ERCOT Operator to Un-Approve failed RPRS Market Case so that Operator can open another adjustment RPRS Market later
  Estimated Migration time is end of April, 2007
NOTE: Estimates are Best Case Scenarios

## Slide 4: Resource Plan Validation for HSL
ERCOT will validate each HSL using the Nameplate Rating multiplied by a parameter
If HSL is greater than the adjusted Nameplate Rating,
  ERCOT will notify the QSE submitting the Resource Plan that the Resource Plan is invalid due to the high HSL
  The QSE may then resubmit the Resource Plan within the appropriate market timeline

## Slide 5: Nameplate Rating Multiplier Study
Note: Multiplier will be determined by ERCOT based on review of previous practices. Please communicate any of your concerns or suggestions to me via your Wholesale Client Representative
Notes: This analysis covers the resource plan submission records between 04/01/06 to 03/31/07. The nameplate rating of each resource is obtained from NameplateMW column in the LODSTAR.GENERATORHIST table.
As expected, the majority of HSL in the resource plan is submitted between 90% to100% of nameplate rating MW. However, there exist cases where QSE submitted HSL at a very high percentage nameplate rating value. Observing the list, part of these resources is the wind generation resources (with very low MW rating). It might be possible that QSE reported individual turbine rating to ERCOT for settlement nameplate rating but submitted HSL as aggregated MW for the whole wind farm. This problem should be identified and corrected before ERCOT implements the nameplate rating from settlement to validate the resource plan HSL.

## Slide 6
End
Slide Credits: Hailong Hui, Kittipong Methaprayoon