## Slide 1: CRR Optimization Recommendation
Beth Garza
Manager, Congestion Analysis & Revenue Rights
CRR Project Team

## Slide 2: Why are we here today?
The Annual CRR auction as defined in the Nodal protocols is a problem too big to be solved in a reasonable amount of time with available software and hardware.
Through multiple discussions with TPTF the CRR project team has developed a recommendation for restructuring the Annual CRR auction.
At their April 3 meeting, TPTF asked that WMS review and opine about the CRR team’s recommendation

## Slide 3: Today’s Objectives
Review CRR products
Describe optimization runtime issue
  Protocol defined annual auction is estimated to take 1300 hours to solve.
  Requirement SR-1 specifies that the annual auction optimization complete within 80 hours.
Review options to reduce optimization run-time and trade-offs
Present recommended solution
Receive input from WMS
Would like to leave with a WMS vote, either an endorsement of the recommendation
or
change in direction
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: CRR Products / Time of Use
Weekday On Peak Time of Use Blocks (hours 0700 – 2200 M-F)
Weekend On Peak Time of Use Blocks (hours 0700 – 2200 SS)
Off Peak Time of Use Blocks (hours 0000 – 0600; 2300 – 2400 all days)
24-hour combination of the above
  The winner of a 24-hour block, will be awarded the three primary times of use
Awarded in whole month strips, not less than one month
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Auction
Annual Auction
55% of network capacity for months 1-12
15% of network capacity for months 13-24
Offers of PCRRs, MCFRIs and previously awarded CRRs; whole months not less than one month
Obligations are available for one-month strips for one-month terms, between any source and sink
  Obligations are available between a limited set of sources and sinks for other times
Monthly Auction
90% of network capacity for coming month
Offers of PCRRs, MCFRIs and previously awarded CRRs; in whole month strips
Obligations will be available between any sources and sinks
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: Optimization Runtime Description & Background
NPRR 005 (August 2006 Nodal Protocols) clarified that the annual CRR auction should simultaneously optimize three Time-Of-Use (TOU) blocks across 24 months.
  Combination is referred to as 72 periods (24 months x 3 TOU).
  Supports bids/offers for any number (1 to 24) of consecutive months.
CRR Team is not aware of another software solution that can optimize 72 periods simultaneously within the 80 hour timeframe.
  PJM’s largest solution (using Nexant competitor software) solves 12 6 periods simultaneously and was thought to be pushing the envelope.
  ERCOT now understands that this optimization takes 15-40 hours to solve.
  Note that comparison is not one-to-one due to differences in other elements, such as number of buses, branches, contingencies, etc.
Time-of-Use
WD = Week Day
WE = Week End
OP = Off Peak
P = On Peak
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: Optimization Run-Time Approaches Previously Discussed
Eliminating a Time-Of-Use block – each TOU acts as another period
Increasing Duration of Calendar Periods, such as seasonal models instead of monthly models
Decoupling Optimizations – separating groups of periods (e.g. Year One and Year Two)
These approaches can be applied individually or in combination.
The selected approach must also apply to the allocation process
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Approach Dimensions
Approach Legend:
A = Eliminate Time-Of-Use (TOU)
B = Increase Duration of Calendar Periods
C = Decouple Optimizations
Recommended approach
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Recommended Approach Decouple Time-Of-Use and Years / Maintain Monthly Granularity
 | Calendar Period | TOU Blocks | Period | Approach
Decouple TOU and Decouple Years / Monthly | 12 – Year 1 | 1 – WD | 12 | C
 | 12 – Year 2 | 1 – WD | 12 | 
 | 12 – Year 1 | 1 – WE | 12 | 
 | 12 – Year 2 | 1 – WE | 12 | 
 | 12 – Year 1 | 1 – OP | 12 | 
 | 12 – Year 2 | 1 – OP | 12 | 
The Annual CRR Auction would be comprised of six separate optimizations
Notes: <number>
<footer>
<header>
<date/time>

## Slide 10: Considerations
High confidence that six separate auctions will solve within the 80-Hour requirement individually and all together (with additional hardware).
Annual decoupling is supported by:
  Significant difference in how much network capacity is made available in Year 1 versus Year 2.
  No previously awarded CRRs exist for Year 2 of the next annual auction.
Separate auctions for each year will not support submittal of bids or offers for a 24-month strip.
  Results from the Year 1 Auction will have no bearing on the results from Year 2.
  24-month strips will not be available.
Time of Use block decoupling is supported by:
  Nodal Protocols already reflect that the winner of a 24-Hour CRR product will be awarded the capacity in three Time-Of-Use blocks.

## Slide 11: More Considerations
Separate auctions for each Time-Of-Use block will not support submittal of bids or offers for a 24-Hour product.
  Results from the auction of one TOU will have no bearing on the results from the auction of other TOUs.
  24-Hour product will not be available.
Maintains monthly granularity which facilitates the allocation of Capacity Option PCRRs with their associated 40% annual capacity factor limit.
Credit Limits for each of the six optimizations will be managed via the self-imposed credit limit.
  The sum of the six self-imposed credit limits will not be allowed to exceed the CRR Auction activity credit limit, as defined in Section 16.11.4.6.1 per NPRR047.

## Slide 12: Summary and Next Steps
Proposed Motion from WMS
  WMS endorses ERCOT’s recommendation to restructure the Annual CRR auction from a single optimization to six independent optimizations.
The CRR team will begin the process to implement this recommendation.
  Draft proposed NPRR for TPTF consideration at an upcoming meeting.
  Perform detailed review of CRR documentation to determine if revisions are required.
  Draft revised CRR documentation, if necessary, for TPTF review and/or approval.
  Initiate review for impact assessment by other Nodal project teams.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13
ADDITIONAL DETAIL Optimization Runtime Reduction Alternatives

## Slide 14: Eliminate Weekend Time-Of-Use
Eliminating a TOU only does not reduce optimization runtime sufficiently.
Including a third TOU block increases the number of periods by 50% and optimization runtime exponentially.
24-Hour product could still be made available.
All other markets only offer two TOU blocks.
Is differentiation in Weekend (WE) congestion costs enough to warrant a separate CRR product?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: Changing from Monthly to Seasonal
Current planning model development activities transition easier as each season represented by one Network Model.
As seasons will not likely align with calendar quarters, annual auction timing would require modifications.
  Example: A season could be December 1st through February 28th.
Will it be problematic for CRRs to be for terms that bridge calendar years?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 16: Decoupling Years - Monthly
Results from Year 1 have no bearing on the results from Year 2.
Significant difference in how much network capacity is made available in Year 1 versus Year 2.
No previously awarded CRRs in the next annual auction
Separate auctions for each year will not allow the award of a 24 month strip.
What is more valuable -- Long term products (24 month CRRs) or access to CRRs in second year?
Notes: <number>
<footer>
<header>
<date/time>

## Slide 17: Decouple Time-Of-Use
Results from the auction of one TOU will have no bearing on the results from the auction of other TOUs.
24-Hour product will not be available.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 18
CRR Product Background

## Slide 19: Buying in an Auction
Example 1 shows an Account Holder’s ability to buy a 24-Hour block that includes ALL Hours Everyday (Not supported in annual auction with six optimizations)
Example 2 shows an Account Holder’s ability to buy a Weekday block that includes Hours 0700 – 2200 Every Monday through Friday
Example 3 shows an Account Holder’s ability to buy multiple time period in separate blocks, in this example:
  A Weekday block that includes Hours 0700 – 2200 Everyday, and
  A Weekend block that includes Hours 0700 – 2200 Saturday through Sunday
  Not shown – an Off-Peak block.
  Bids for multiple blocks are not linked.
Example 1
Example 2
Example 3
Notes: <number>
<footer>
<header>
<date/time>

## Slide 20: Products in the Auction
24-Hour Buy awarded to the Account Holder as three separate blocks: Weekend, Weekday, and Off-Peak
An Account Holder can offer his holdings in three types of blocks: Weekday, Weekend, and Off-Peak.
  Weekday, Weekend, and Off-Peak blocks offered are not linked. Therefore, there is no guarantee that all will be sold.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 21: UNsupported Bid (Buy) Alternatives in Auction
Example 4 shows that an Account Holder may NOT buy a block that includes hours other than 0700 – 2200.
Example 5 shows that an Account Holder may NOT buy a block that does not include all of the days of the month.
Example 4
Example 5
Notes: <number>
<footer>
<header>
<date/time>

## Slide 22: Bilateral Trading
CRRs can be traded:
Between any two registered Account Holders
  Initiated by the seller
  Approved by the buyer
In time of use amounts for a particular day(s)
Once a single day of a CRR month is bilaterally traded, the remaining days of the month may not be offered into an annual or monthly auction
Approval of bilateral trades will be subject credit approval based on the impact of the trade to both the current owner and proposed owner
All bilateral trades must be registered in the CRR system at a time TBD to be available in the Day Ahead Market
Notes: <number>
<footer>
<header>
<date/time>

## Slide 23: Supported Bilateral Trade Alternatives
Account Holder that won a 24-Hour block, will be awarded the three Time-of-Use blocks which may be separately traded.
  Any of the blocks can be for any number of days.
  Weekday and Weekend blocks can only be traded for hours 0700 – 2200.
  Off-Peak blocks can be traded for hours 0100 – 0600 and 2300 – 2400.
Notes: <number>
<footer>
<header>
<date/time>