## Slide 1: Analysis of the IDR Threshold Requirement at ERCOT
Presented by:
Carl Raish
Lindsey Turns

## Slide 2: Overview
ERCOT responsibilities
  Settlements and billing
  Load Profiling
Current IDR requirements
IDR Threshold Analysis
  Methodology
  Results

## Slide 3: Load Profiling in the ERCOT Market
Load Profiles
  Reconcile ~50% of energy in the ERCOT market
  9 profile segments and 8 weather zones yields 72 profile types
Load Research program
Evaluate impact of
the IDR requirement

## Slide 4: Current IDR Requirement
Once an IDR always an IDR
Peak demand greater than 1000 kW (1000 kVa)
Service provided at transmission voltage (above 60 kV)
Retailer may have an
IDR installed and used
for settlement purposes
IDR
REMOVAL

## Slide 5: Protocol Revision Request
Protocol revision request (PRR) to optionally remove any IDR with peak load less than 1000 kW for a year
  Addresses new customer with smaller load than predecessor
  Existing customer whose load has dropped
In the approval process

## Slide 6: IDR Threshold Analysis Scenarios
The analysis addressed three scenarios:
Allowing a voluntary removal threshold
Lowering the mandatory installation threshold
Lowering the required installation threshold and allowing voluntary removal below that threshold

## Slide 7: IDR Threshold Analysis Criteria
The analytical process addressed the following criteria:
Profiling Error
Quantifying impact of increasing or decreasing profiling error by increasing or decreasing number of IDRs
Premise Level Impacts
Settlement and TDSP charges
Societal Impacts
Deadweight Loss
System Reliability Benefits

## Slide 8: Methodology Overview
Calculated the load factor and made a profile assignment (BUSHILF, BUSMEDLF, or BUSLOLF)
Applied ERCOT’s data aggregation process to allocate usage to profiles
Quantified energy differential between actual energy used and energy allocated by profiles
  Net Profiling Error/Cost
  Total Profiling Error/Cost
  Cross Customer Error/Cost

## Slide 9
METHODOLOGY

## Slide 10: Methodology Profiling Error
Profiling Error illustrates whether the profile overestimates or underestimates the true usage. The formula is:
where PE = Profiling Error (kWh) for a premise
Eiactual= Actual Energy (kWh) for a 15-minute interval, and
Eiprofiled = Profiled Energy (kWh) for a
15-minute interval.

## Slide 11: Actual vs. Profiled Energy Example for a Day

## Slide 12: Actual vs. Profiled Energy Example for a Month

## Slide 13: Balancing Energy Market MCPE
ERCOT’s market is primarily bilateral … prices are not transparent
One day ahead ERCOT receives balanced load and resource schedules from QSEs
ERCOT buys balancing energy in each congestion zone as needed for each interval approximately 30 minutes ahead
MCPE (Market Clearing Price for Energy) is determined through bidding and is the only transparent energy price in the ERCOT market

## Slide 14: Methodology Settlement Cost
Settlement Cost is used as a basis for comparison of other calculated costs in the analysis and is found by:
where SE = Settlement Cost for an ESIID ($),
Eiactual = Actual energy (kWh) for a 15-minute interval i, and MCPEi = Market Clearing Price of Energy for a 15-minute interval i.

## Slide 15: Methodology Net Profiling Error Cost
Net Profiling Error Cost indicates whether, at the end of the year, the profile allocates higher or lower costs than the IDR. The formula is:
where NPEC = Net Profiling Error Cost ($) for an esiid,
PEi = Profiling Error (kWh) for a 15-minute interval i,
MCPEi = Market Clearing Price of Energy ($/MWh) for a 15-minute interval i

## Slide 16: Methodology Net Error
The percentage of the Net Profiling Cost to the Settlement cost is given by:
where NPEC = the Net Profiling Error Cost ($), and SE = Settlement Cost ($)

## Slide 17: Methodology Total Profiling Error
Total Profiling Error represents the total amount of Profiling Error over the year and is found by:
  where TPE = the Total Profiling Error (kWh),
  Eiactual = Actual energy (kWh) for an ESIID for a 15-minute interval,
  Eiprofiled = Profiled Energy (kWh) for a 15-minute interval for an ESIID

## Slide 18: Methodology Cross Customer Error
Cross Customer Error represents Profiling Error at the premise level or can be thought of as the measure of the total amount of settlement cost being incorrectly allocated to premises within the group. Cross Customer is found by:
where CCE = Cross Customer Error ($) for an ESIID,
PEi = Profiling Error for a 15-minute interval, and
MCPEi = Market Clearing Price of Energy for a 15- minute interval.

## Slide 19: Estimates for IDR Costs
  ERCOT estimated the annualized
  incremental cost of IDR metering using
  the following assumptions:
  IDR Purchase/Installation $1000
  Annual Reading Cost $72
  Amortization Period 15 years
  Interest Rate 5.0%
  Annualized IDR Cost $168

## Slide 20
RESULTS

## Slide 21: Distribution of IDRs Less Than 1000 kW
3,752 ESIIDs

## Slide 22: Dead Weight Loss Results Based on Annual Consumption

## Slide 23: Voluntary Removal Threshold
Current requirement specifies that once an IDR is installed it must remain and be used for settlement
ERCOT analyzed the impact of establishing a demand threshold below which IDRs could be voluntarily removed

## Slide 24: Voluntary Removal Net Profiling Error Cost

## Slide 25: Voluntary Removal Net Profiling Error Cost

## Slide 26: Voluntary Removal Net Profiling Error Cost

## Slide 27: Voluntary Removal Net Profiling Error – All IDRs 0 kW to 1000 kW

## Slide 28: Distribution of Net Profiling Error

## Slide 29: Voluntary Removal Cross Customer Error

## Slide 30: Voluntary Removal Cross Customer Error

## Slide 31: Voluntary Removal Cross Customer Error Summary - All IDRs 0 kW to 1000 kW

## Slide 32: Voluntary Removal Cumulative Cross Customer Error-All IDRs 0 kW to 1000 kW

## Slide 33: Voluntary Removal Distribution of IDRs by Tariff Impact and Demand Level

## Slide 34: Tariff Savings for Premises which Benefit by Removing IDR Meter

## Slide 35: Voluntary Removal Net Profiling Error Summary of IDRs with Lower Tariff Charges

## Slide 36: Voluntary Removal Cumulative Cross Customer Error Summary of IDRs with Lower Tariff Charges

## Slide 37: Mandatory Installation Threshold
Current requirement specifies an IDR shall be installed when peak demand is greater than 1000 kW (more than two times in a year)
ERCOT considered lowering the threshold required for installation

## Slide 38: Mandatory Installation Cross Customer Error

## Slide 39: Mandatory Installation Cross Customer Error Per IDR

## Slide 40: Mandatory Installation Number of IDRs that would be Required

## Slide 41: Mandatory Installation Cumulative Cross Customer Error All NIDRs 450 kW to 1000 kW

## Slide 42: Combination Required Installation and Optional Removal Thresholds
ERCOT considered lowering the required installation threshold and allowing voluntary removal of IDRs below that threshold

## Slide 43: Mandatory Installation and Optional Removal Cross Customer Error

## Slide 44: Mandatory Installation and Optional Removal Cross Customer Error Per IDR

## Slide 45: Reliability Benefits
With IDRs accurate price signals at
times of short supply can reduce
demand levels and increase reliability
Value to customer of maintaining load
Avoided costs of rationing
Avoided costs of restoration
Avoided damage to reputation of utility/ISO
Avoided payments from lawsuits
More opportunities for demand side resources

## Slide 46: ERCOT Recommendations
Initially set IDR threshold at 700 kW
  964 IDRs would need installation
  Cross Customer Error reduction ~ $2 million per year
Optional removal below 200 kW
  802 premises impacted however likely that only 364 would experience tariff reductions
  TDSP tariff reductions ~ $635/premise
  ~ $208 Cross Customer Error introduced

## Slide 47: ERCOT Recommendations Additional Research
Incorporate UFE calculation and adjustment and extend analysis down to 100 kW for mandatory installation
Analyze benefits of a mandatory TOU provision
Analyze load research data to refine estimates particularly in 100 kW t0 700 kW range