## Slide 1: Oil & Gas Final Sample Analysis
April 27, 2006

## Slide 2: Background Information
TXU ED provided a list of ESI IDs with SIC codes indicating Oil & Gas (8,583)
These were mapped into LRS sample cells
  421 LRS sample points were identified as Oil & Gas
  15 LRS sample cells identified with significant population counts having no sample points available
  Requestor agreed to fund IDR installation/data collection for ERCOT selected sample points in those cells (data collected for March – May 2005)
TXU ED performed field verification on all Oil & Gas sample points
7,342 ESI IDs were included in this preliminary analysis covering the March – May time period
ESI IDs included in analysis based on
  Active during the analysis period
  Complete NIDR usage available
  Profile Group was BUSNODEM, BUSLOLF, BUSMEDLF, BUSHILF
  Belong to a cell with LRS interval data available for one or more ESI IDs
Sample data was scanned to verify that usage patterns were likely to be Oil & Gas (none were considered miss-classified)

## Slide 3: Oil & Gas Sample Size by Stratum
Population Size: 7,342
Sample Size: 412
Strata: 76 out of 104

## Slide 4: Oil & Gas Sample Size by Stratum
For statistical analysis purposes original sample strata were consolidated into 22 analysis strata
Minimum of 5 sample points per analysis stratum
Strata were consolidated based on the same or similar case weights
  (Case weight = sample size/population size)

## Slide 5
Example: BUSNODEM ESI ID March 1 – May 31
kWh

## Slide 6: Example: BUSNODEM ESI ID March 1 – May 31

## Slide 7: Example: BUSLOLF ESI ID March 1 – May 31

## Slide 8: Example: BUSLOLF ESI ID March 1 – May 31
kWh
kWh

## Slide 9: Example: BUSLOLF ESI ID March 1 – May 31
kWh

## Slide 10: Example: BUSMEDLF ESI ID March 1 – May 31
kWh

## Slide 11: Example: BUSMEDLF ESI ID March 1 – May 31
kWh

## Slide 12: Example: BUSMEDLF ESI ID March 1 – May 31
kWh

## Slide 13: Example: BUSHILF ESI ID March 1 – May 31
kWh

## Slide 14: Example: BUSHILF ESI ID March 1 – May 31
kWh
kWh

## Slide 15: Distribution of Sample Precision
Mean 6.4%
Precision for 93% of Intervals < 10%

## Slide 16: Composite Profile Development
Defined in Load Profiling Guides Section 12.6.2.5
Used for comparison if a single profile is to be used across several Weather Zones.
Where:
f*t = interval fraction at interval t for the composite Load Profile
Ez = total annual energy of ESI IDs in the proposed segment in Weather Zone z
fzt =interval fraction at interval t for the existing Load Profile using the weather data for Weather Zone
n = total number of Weather Zones

## Slide 17: Profile and Sample Comparison
1 Day of lowest total absolute kWh difference for 11/01/04 thru 10/31/05

## Slide 18: Profile and Sample Comparison
2 Day of 25th percentile total absolute kWh difference for 11/01/04 thru 10/31/05

## Slide 19: Profile and Sample Comparison
3 Day of median total absolute kWh difference for 11/01/04 thru 10/31/05

## Slide 20: Profile and Sample Comparison
4 Day of 75th percentile total absolute kWh difference for 11/01/04 thru 10/31/05

## Slide 21: Profile and Sample Comparison
5 Day of highest total absolute kWh difference for 11/01/04 thru 10/31/05

## Slide 22: Profile and Sample Comparison

## Slide 23: Profile and Sample Differences

## Slide 24: Profile and Sample Differences

## Slide 25: Profile and Sample Differences

## Slide 26: Profile and Sample Differences

## Slide 27: Differences for Fall

## Slide 28: Differences for Winter 2004-2005

## Slide 29: Differences for Spring 2005

## Slide 30: Differences for Summer 2005

## Slide 31: Profile and Unscaled Sample Differences

## Slide 32: Profile and Sample Differences

## Slide 33: Oil Gas LRS vs Composite Profile Load Factor

## Slide 34: Oil Gas LRS vs Composite Profile On Peak vs Off Peak kWh

## Slide 35: Oil Gas LRS vs Composite Profile Monthly kWh Fractions

## Slide 36: Oil Gas LRS vs Composite Profile Monthly kWh Fractions

## Slide 37: Oil Gas LRS vs Composite Profile

## Slide 38: Oil Gas LRS vs Composite Profile

## Slide 39: Load Weighted Average Price (LWAP) in $/Mwh
An ideal profile model is applied to a homogeneous set of ESI IDs
Oil/Gas ESI-ID’s are dissimilar in both shape and load factor
If they have similar Load Weighted Average Prices (LWAP) they can be settled accurately with the same profile
For an ESI ID, LWAP is computed as
LWAP comparisons were performed to assess similarities.

## Slide 40: Load Weighted Average Price (LWAP) in $/Mwh

## Slide 41: Population LWAP MPU Estimation

## Slide 42: Population LWAP MPU Confidence Limits

## Slide 43: Population LWAP Estimation Energy Weighted
LWAP Variance is the Measure of Homogeneity referenced in the LPG

## Slide 44: Comparison of Estimated LWAP

## Slide 45: Weather Sensitivity Analysis Definition
Defined in Protocols Section 11.4.3.1
The following variables are calculated for each business day (excluding weekends and holidays):
  Daily kWh
  Average weather zone daily temp = ((Max + Min)/2)
A correlation factor, R-Square (Pearson Product Moment Coefficient of Determination), is calculated for each oil/gas sample point
If the resulting R-Square value is greater than or equal to 0.6, then the sample point is defined as “Weather Sensitive”.

## Slide 46: Weather Sensitivity Analysis Definition
Three weather sensitivity studies were performed.
  Summer: 06/01/05 – 09/31/05
  Winter: 12/01/04 – 02/28/05
  Study Period: 11/01/04 – 10/31/05

## Slide 47: Weather Sensitivity Analysis

## Slide 48: Weather Sensitivity Analysis

## Slide 49: Weather Sensitivity Analysis

## Slide 50: Weather Sensitivity Analysis

## Slide 51: Weather Sensitivity Analysis

## Slide 52: Weather Sensitivity Analysis

## Slide 53: Weather Sensitivity Analysis

## Slide 54: Weather Sensitivity Analysis