## Slide 1: ERCOT
LRS Sample
Design Review
PWG Presentation
March 27, 2007

## Slide 2: Overview
Background information
Review of different options considered
Summary results of Option 1- 3
Class level MWh & Dollars by Profile Type/ WZone
Precision versus sample size
Review and discussion of Option chosen
Review of existing sample points
Reference to PUCT Rule 25.131 Section C

## Slide 3: Background Information
ERCOT presented LRS precision analysis and sample design ideas and options at the June 28, 2006 meeting.
For Round 1 of the LRS sample design ERCOT offered to coordinate our sample designs with all of the TDSPs; only TXU-EDs’ was interested and we worked with them and incorporated their sample into ours. We are doing this again for Round 2.
At the request of AEP ERCOT performed analysis to determine if it was necessary to have a separate primary voltage sample
Analysis indicates 4 cells with 40 Sample Points each totaling 160 Primary Voltage Sample Points

## Slide 4: Options for Determining Round Two Sample Size Increases
Option 1:
  Determine minimum sample size needed to obtain ±10% Accuracy at 90% Confidence for a selected percent of intervals for the year independently for each Profile Type / Weather Zone Combination
For Options 2 – 5 ERCOT recomputed daily energy totals and dollars
  Used SAS data aggregation tool developed for transition analysis
  Applied load profiles from new models to spread monthly LSEG totals from Lodestar to intervals
  Multiplied by weather zone weighted MCPE to associate a dollar value with each interval
Option 2:
  Determine minimum sample size needed to obtain ±10% Accuracy at 90% Confidence for enough intervals to account for a selected percent of the MWh for each Profile Type / Weather Zone Combination
Option 3:
  Determine minimum sample size needed to obtain ±10% Accuracy at 90% Confidence for enough intervals to account for a selected percent of the dollars (ΣMWh * MCPE) for each Profile Type / Weather Zone Combination
Option 4:
  Iteratively allocate increments of 20 sample points to the Profile Type / Weather Zone Combination which produces the most gain in terms of reducing MWh estimation error
Option 5:
  Iteratively allocate increments of 20 sample points to the Profile Type / Weather Zone Combination which produces the most gain in terms of reducing Dollar estimation error

## Slide 5: Option 1
To obtain ±10% Accuracy at 90% Confidence By Profile Type - Independent of Interval
For example: to obtain ±10% Accuracy at 90% Confidence for 50% of the intervals for all Profile Type/Weather Zone combinations would require a sample size of 8,447 points

## Slide 6: Option 2
To obtain ±10% Accuracy at 90% Confidence for Intervals Accounting for Selected Percents of the MWH within Each Profile Type
For example: to obtain ±10% Accuracy at 90% Confidence for intervals accounting for 50% of the MWh for each of the Profile Type / Weather Zone combinations would require a sample size of 7,438 points

## Slide 7: Option 3
To obtain ±10% Accuracy at 90% Confidence for Intervals Accounting for Selected Percents of the dollars within each Profile Type
Continues on next slide
For example: to obtain ±10% Accuracy at 90% Confidence for intervals accounting for 50% of the Dollars for each of the Profile Type / Weather Zone combinations would require a sample size of 6,969 points

## Slide 8: Option 3
To obtain ±10% Accuracy at 90% Confidence for Intervals Accounting for Selected Percents of the dollars within each Profile Type

## Slide 9: Class Level MWH & Dollars
Is accuracy more important for RESLOWR (33.4% of Dollars) than for BUSNODEM (1.6% of Dollars)?

## Slide 10: Class Level MWH & Dollars - Descending Order by Dollars
* Note: Dollars = Σ (MWh * MCPE)
Continues on next slide
Top 5 classes account for 53% of the MWh and 54% of the dollars

## Slide 11: Class Level MWH & Dollars - Descending Order by Dollars
* Dollars = Annual MWh * MCPE
Continues on next slide
Bottom 28 classes account for only 10% of the MWh and dollars

## Slide 12: Class Level MWH & Dollars - Descending Order by Dollars
* Dollars = Annual MWh * MCPE
Continues on next slide

## Slide 13: Precision vs Sample Size
Increasing sample size has a diminishing return on precision improvement
Error Ratio (thus Precision improvement) varies across Profile Types / Weather Zones and across intervals
Thus the impact of adding sample points varies by Profile Type and Weather Zone

## Slide 14: Options 4 & 5
Options 4 & 5 iteratively allocate increments of 20 sample points to the next Profile Type / Weather Zone Combination in order to produce the most gain in
  Reducing MWh (Option 4) estimation error (Precision × MWh) summed across all intervals
  Reducing Dollar (Option 5) estimation error (Precision × Dollars) summed across all intervals
The allocations are based on
  The MWh (or Dollars) associated with each of the Profile Type / Weather Zone combinations in each interval
  The Error ratio in each interval for each Profile Type / Weather Zone combination
  The cumulative number of sample points allocated by preceding iterations (including the original sample size)
  The precision improvement that would be realized by adding 20 sample points, and the diminishing return on that improvement
Minimum Sample Size
  Profile to profile migration resulted in numerous instances of small sample sizes within strata
  Small sample sizes resulted in both accuracy degradation and the need to drop strata from load research analysis
  A minimum of 3 strata will be specified for each Profile Type / Weather Zone combination
  A minimum of 40 sample points will be allocated to each stratum
  Minimum sample size per Profile Type / Weather Zone combination will be 120
Maximum Sample Size
  Maximum for Business Profile / Weather Zone combinations set to 400
  Maximum for Residential Profile / Weather Zone combinations set to 600

## Slide 15: Option 4 – MWh Error Reduction Optimization
(Option 4) Reducing MWh estimation error (Precision × MWh) summed across all intervals
Cumulative sample sizes are shown in increments of 1,000; they were determined iteratively in increments of 20 sample points

## Slide 16: Option 5 – Dollar Error Reduction Optimization
(Option 5) Reducing Dollar estimation error (Precision × Dollars) summed across all intervals

## Slide 17: Dollar Error Reduction Based on Sample Size Increases
Non - Optimized
Allocation of points
Optimized Allocation of Additional Points

## Slide 18: Primary Voltage Sample Review
Four Business sample cells have significant saturation of primary voltage ESIIDs/energy
These cells will have primary voltage strata included in their sample design (40 per stratum)
Existing primary voltage sample points were selected based on separate stratified sample designs, complete retention not feasible because of sample point weighting issues

## Slide 19: Retainable Round 1 Sample Points
Table shows retainable secondary sample points only
Non retained sample points may be selected for the round 2 sample
TDSPs should consider waiting until round 2 sample list is provided to start recorder removal

## Slide 20: PUC Rule §25.131, Load Profiling and Load Research
Section (C):
  Load research responsibility. Each TDU shall perform load research to support ERCOT’s load profiling activities, as directed by ERCOT.
      ERCOT shall be responsible for load research sample design and sample point selection for ERCOT-directed load profiling and load research samples. ERCOT shall coordinate with each TDU to optimize load research programs of both ERCOT and the TDU. The same samples shall be used to support both the TDU’s load research activities and ERCOT’s load profile research needs whenever reasonably possible. Each TDU shall coordinate with ERCOT to synchronize its load research cycles and sample replacement with those of ERCOT.
      ERCOT, in consultation with the TDUs, shall specify the manner of data collection for ERCOT load profile research samples and the means and frequency of transmission of such information to ERCOT. Each TDU shall adhere to the specifications for data collection and transmission specified by ERCOT.
      A TDU may recover its reasonably and necessary costs incurred in performing load profile research as required by this section.
      This section shall not be interpreted to require a TDU to redeploy any existing samples that were deployed less than five years before the effective date of this section, although this section shall also not be interpreted as addressing the appropriateness of continued deployment of existing TDU samples apart from the ERCOT request to do so. Notwithstanding the foregoing, the TDU shall deploy additional samples as requested by ERCOT in order to support ERCOT’s load profiling activities.