## Slide 1: ERCOT Analysis of 2005 Residential Annual Validation Using the Customer Survey Results
ERCOT Load Profiling
Presented to PWG - October 26, 2005

## Slide 2
Residential Survey Analysis
Objective is to quantify the accuracy of the 2005 Annual Validation Residential Profile Assignment Changes
Based on the survey responses in conjunction with each responder’s usage history build an accurate algorithm to predict presence and use of electric space heating
Apply the algorithm to each of the 578,572 ESI IDs with 2005 Annual Validation Profile Assignment changes
Determine the percent of changes which are correct
  RESHIWR with electric heat
  RESLOWR without electric heat

## Slide 3
Residential Survey Analysis
If the majority of changes are correct then AV 2005 is improving Profile Assignment Accuracy
Survey status
  41,000 surveys were mailed on August 30 (plus earlier Pilot Survey)
  Returns have been received and processed
  Response rate is 11.4% (4,669 returns) as of 09/30/2005 cut-off
  4,630 responses indicated either a “Single-Family Dwelling” or “Multi-Family Dwelling” and a primary home heating type of either “Electricity” or “Natural gas or bottled gas (propane/butane)
  673 (14.5%) responses to the home heating type were deemed invalid by examination of their seasonal usage pattern
  3,957 responses were used to develop the final Profile Type classification algorithm

## Slide 4
Survey Response Validation
An initial algorithm was developed using Pilot Survey responses as a basis
The initial algorithm was applied to each of the 4,630 responses (with valid dwelling type and home heating type) to identify heating type responses which were inconsistent with the algorithm classification
857 inconsistent responses were identified … the usage patterns of each were examined graphically to assess whether the survey response was highly likely to be incorrect or not.
  673 responses were deemed to be incorrect and were eliminated from the subsequent analysis undertaken to fine tune the algorithm
  184 responses were deemed to be either correct or possibly correct and were retained in the analysis

## Slide 5
Survey Response Validation

## Slide 6
Algorithm Development – Usage Screening
For each ESI ID with a survey response usage values were selected from Lodestar for the January 2002 – September 2005 time period
Usage values were screened to prevent high and low outlier usage values as well as usage during periods of low/no occupancy from unduly affecting the Profile Type classification for an ESI ID and to improve the response validation process
Each usage value was converted into units of kWh/day to offset the impact of long or short reads (any read covering a period longer than 44 days was dropped from the analysis)
Each usage value was classified as a winter or shoulder reading
  Only shoulder and winter readings were used in the analysis
  Winter/Shoulder: start > September 20 and stop < May 11
  Winter: start > November 15 and stop < March 15
  Shoulder: all others

## Slide 7
Algorithm Development – Usage Screening
For each ESI ID compute a mean and standard deviation of the kWh/day values for the winter and shoulder readings and use these to “normalize” each usage value
Usage value dropped if:
  Z > 3 and kWh/day > 100
  Z > 3.5
  Z < -2
  kWh/day < 5 Low Occupancy
Outliers

## Slide 8
Usage Screening Examples
Usage less than 5 kWh/day dropped

## Slide 9
Usage Screening Examples
Usage with Z < -2.00 dropped

## Slide 10
Usage Screening Examples
Usage with Z > 3.50 dropped

## Slide 11
Usage Screening Results
1,006 ESI IDs (21.7%) with one or more usage values screened
2,414 usage values were screened out
1,825 usage values screened out because < 5 kWh/day
If an ESI ID had fewer than 3 winter readings or fewer than 3 shoulder readings it was classified as “RESLOWD” (Residential Low Winter Ratio Default) and was not used for fine tuning the algorithm

## Slide 12
Algorithm Basics
If an ESI ID has (and uses) electric heating, then the winter and shoulder usage values for that premise should be more similar to the RESHIWR profile loads than to the RESLOWR profile loads
The profile loads for a day reflect the weather conditions associated with that day in the specific weather zone as well as the day type (day-of-week/holiday) and season of the year
To perform the comparison for an ESI ID, the profile loads are summed across the intervals for the days in each of its meter reading periods (shoulder and winter months only)
  Example: If the reading starts on January 15, 2002 and ends on February 15, 2002, the RESHIWR and RESLOWR profile loads are summed for January 15 – February 14 to obtain comparable profile readings for the same time period

## Slide 13
Algorithm Basics
For each fall-winter-spring time period e.g., fall 2004 – spring 2005 the profile loads are scaled to equal the sum of the ESI ID’s readings for that time period
  If the ESI ID used 5,000 kWh for the fall-winter-spring time period and the RESHIWR profiled loads for that time period summed to 4,000 kWh, each of the RESHIWR profiled loads would be multiplied by 1.25
  If the RESLOWR profiled loads for that time period summed to 2,500 kWh, each of the RESLOWR profiled loads would be multiplied by 2.0
The correlation between the actual readings and the sum of the scaled profile loads for those readings is computed for each ESI ID
  The R2 correlation is determined with a weighted linear regression analysis
  Each reading is weighted as follows:
  Shoulder reading weight = 1
  Winter reading weight = 1 or
  Winter reading weight = 1 if RESHIWR kWh < RESLOWR kWh
  The weighting process associates more importance with winter readings for which the RESHIWR is greater than the RESLOWR kWh

## Slide 14
Algorithm Basics – An Example

## Slide 15
Algorithm Basics – An Example

## Slide 16
Algorithm - Classification Rules
If the highest winter reading kWh/day is less than 15 kWh/day
then assign “RESLOWR”
If R2RESHIWR > 0.60 and R2RESHIWR > R2RESLOWR
then assign “RESHIWR”
If the number of readings available > 9
and R2RESHIWR > 0.90
and (R2RESHIWR + 0.010) > R2RESLOWR
and Winter Max kWh/day > 50
then assign “RESHIWR”
If the number of readings available > 9
and R2RESHIWR > 0.95
and (R2RESHIWR + 0.015) > R2RESLOWR
and Winter Max kWh/day > 60
then assign “RESHIWR”
Otherwise assign “RESLOWR”

## Slide 17
Algorithm – Fine Tuning
Algorithm fine tuning was an iterative process to tune each classification criterion on the previous slide individually
Each classification criterion was adjusted to minimize miss-classification error based on validated survey responses
For each iteration, miss-classified ESI IDs were examined graphically to assess the accuracy of the Profile Type assignment and to establish new criteria
When the fine tuning was complete 184 (4.6%) validated survey responses regarding heating system type were different than the algorithm classification … most had usage patterns which were ambiguous

## Slide 18
Algorithm – Fine Tuning
For the final version of the algorithm 3,773 (95.4%) validated survey responses regarding heating system type agreed with the algorithm classification
Definitely not electric heat!

## Slide 19: Correctly Classified Example
Survey and algorithm both indicated electric heat, “RESHIWR”

## Slide 20: Correctly Classified Example
Survey and algorithm both indicated gas heat, RESLOWR”

## Slide 21
Algorithm – Fine Tuning
For the final version of the algorithm 184 (4.6%) validated survey responses regarding heating system type disagree with the algorithm classification – these usually had ambiguous usage patterns

## Slide 22
Survey and Algorithm Disagree on Classification
COAST Example
Survey said gas heat, algorithm said electric

## Slide 23
Survey and Algorithm Disagree on Classification
EAST Example
Survey said gas heat, algorithm said electric

## Slide 24
Survey and Algorithm Disagree on Classification
EAST Example
Survey said electric heat, algorithm said gas

## Slide 25
Survey and Algorithm Disagree on Classification
NCENT Example
Survey said electric heat, algorithm said gas

## Slide 26
Algorithm to Annual Validation Comparison
534 (13.5%) validated survey responses had 2005 Annual Validation assignments which were different than the assignments for the finalized algorithm … these were examined graphically to determine whether the algorithm was making more accurate assignments

## Slide 27
AV 2005 and Algorithm Disagree on Classification
EAST Example
AV 2005 said change to RESLOWR, algorithm said RESHIWR

## Slide 28
AV 2005 and Algorithm Disagree on Classification
FWEST Example
AV 2005 said change to RESLOWR, algorithm said RESHIWR

## Slide 29
AV 2005 and Algorithm Disagree on Classification
NCENT Example
AV 2005 said change to RESLOWR, algorithm said RESHIWR

## Slide 30
AV 2005 and Algorithm Disagree on Classification
NORTH Example
AV 2005 said change to RESLOWR, algorithm said RESHIWR

## Slide 31
AV 2005 and Algorithm Disagree on Classification
SOUTH Example
AV 2005 said change to RESLOWR, algorithm said RESHIWR

## Slide 32
AV 2005 and Algorithm Disagree on Classification
WEST Example
AV 2005 said change to RESLOWR, algorithm said RESHIWR

## Slide 33
AV 2005 and Algorithm Disagree on Classification
EAST Example
AV 2005 said change to RESLOWR, algorithm said RESHIWR

## Slide 34
AV 2005 and Algorithm Disagree on Classification
COAST Example
AV 2005 said change to RESHIWR, algorithm said RESLOWR

## Slide 35
AV 2005 and Algorithm Disagree on Classification
EAST Example
AV 2005 said change to RESHIWR, algorithm said RESLOWR

## Slide 36
AV 2005 and Algorithm Disagree on Classification
NCENT Example
AV 2005 said change to RESHIWR, algorithm said RESLOWR

## Slide 37
AV 2005 and Algorithm Disagree on Classification
NORTH Example
AV 2005 said change to RESHIWR, algorithm said RESLOWR

## Slide 38
AV 2005 and Algorithm Disagree on Classification
WEST Example
AV 2005 said change to RESHIWR, algorithm said RESLOWR

## Slide 39: SUMMARY OF 2005 ANNUAL VALIDATION PROFILE TYPE CHANGES

## Slide 40: ACCURACY OF AV 2005 PROFILE TYPE CHANGES

## Slide 41: RESIDENTIAL POPULATION ACCURACY BEFORE AV 2005 CHANGES

## Slide 42: RESIDENTIAL POPULATION ACCURACY AFTER AV 2005 CHANGES

## Slide 43
Conclusions
62% of 2005 Annual Validation Profile Type changes are accurate
Changes to RESHIWR are significantly more accurate (78.4%) than are changes to RESLOWR (43.5%)
Accuracy of the changes by weather zone range from a low of 59.8% in the SOUTH zone to a high of 68.8% in the EAST zone
Although AV 2005 has identified 578,572 Profile Type changes, the net impact of the changes overall is to increase the number of RESHIWR ESI IDs only by 39,418 … a 2.5% increase and a corresponding 1.1% decrease for RESLOWR
The Residential population will have somewhat more accurate Profile Type assignments as a result of conducting 2005 Annual Validation (81.4% vs. 78.7%)

## Slide 44
Conclusions
As a result of completing AV 2005 the RESHIWR assignment accuracy will be 88.2% (vs. 84.9%) and the RESLOWR assignment accuracy will be 78.2% (vs. 75.9%)
A significant amount of room exists to improve the overall Profile Type assignment accuracy
A significant limitation to the current Profile Type assignment algorithm is that it considers usage during a single fall-winter-spring season
Profile Type changes are much more frequently made as a result of occupancy and/or weather related changes than as a result of heating system changes … and as a result are frequently “out of phase” with settlement
This analysis supports the PWG conclusions to continue making use of the Residential Survey data to investigate ways to tailor the assignment algorithm based on the weather zone and on the actual weather during the assignment window

## Slide 45
Questions?