## Slide 1: Capacity, Demand and Reserves Report Bill Bojorquez May 4, 2007

## Slide 2: Approved CDR Methodology Changes
Treatment of new generation:
  Signed generation interconnection agreement and air permit.
Change capacity value for wind:
  Base wind capacity value on Effective Load Carrying Capability (ELCC) from ERCOT’s Loss of Load Probability Study (LOLP)—currently measured at 8.7% of installed capacity.

## Slide 3: GATF Recommended Format Changes
Eliminate the “High” and “Low” reserve margin calculations.
Eliminate the “Publicly Announced Thermal Units” calculation.
Add “Uncommitted Resources”:
  Remaining mothballed capacity;
  Remaining DC tie capacity; and
  New units with transmission full interconnection studies in process, but no signed interconnection agreement.

## Slide 4: Additional Board Input
Remove total “potential resources” at bottom of report
Break down “uncommitted” resources and consider a new title
Clarify units in Full Interconnection Study phase are included in the uncommitted category
Clarify (or consolidate) multiple “mothball” capacity and wind capacity lines in the report
Explain Private Networks
Eliminate footnotes
Treatment of nuclear plants
How often should the ELCC for wind be computed?
How often should the CDR be prepared?

## Slide 5
Format
Changes
Combine
Combine
Combine
Other Potential
List Mothball Capacity, DC ties and planned units in Full Interconnection study subtotals

## Slide 6: Proposed Format

## Slide 7: CDR Preparation Frequency
ERCOT proposes December and May reports
  May report will include new load forecast and all worksheets
  December report will only include summer summary table and list of resources – no updated load forecast
Requirements to support two CDR reports each year:
  Mothball return probability updated twice per year (PRR 713)

## Slide 8: TAC Actions
Endorse the CDR format changes
Recommend frequency of reports

## Slide 9: BACKUP SLIDE (Terminology)
Available Mothballed Generation
The probability that a mothballed unit will return to service multiplied by the capacity of the mothballed unit.
BULs
Balancing up load. Loads capable of reducing the need for electrical energy when providing Balancing Up Load Energy Service as described in the ERCOT Protocols, Section 6, Ancillary Services. BULs are not considered resources as defined by the ERCOT Protocols.
LaaRs (Loads acting as resource)
Load capable of reducing or increasing the need for electrical energy or providing Ancillary Services to the ERCOT System, as described in the ERCOT Protocols, Section 6, Ancillary Services. These Resources may provide the following Ancillary Services: Responsive Reserve Service, Non-Spinning Reserve Service, Replacement Reserve Service, and Regulation Service. The Resources must be registered and qualified by ERCOT and will be scheduled by a Qualified Scheduling Entity.
Mothballed Capacity
The difference in the available mothballed generation (see definition above) and the total mothballed capacity.
Mothballed Unit
A generation resource for which a generation entity has submitted a Notification of Suspension of Operations, for which ERCOT has declined to execute an RMR agreement, and for which the generation entity has not announced retirement of the generation resource.
Net Dependable Capability
Maximum sustainable capability of a generation resource as demonstrated by performance testing.
Net Dependable Wind Generation
The amount of wind generation that the Generation Adequacy Task Force (GATF) has mandated to be included in the CDR. The value is 8.7% of the capacity, both installed capacity and planned capacity.
Non-synchronous Tie
Any non-synchronous transmission interconnection between ERCOT and non-ERCOT electric power systems

## Slide 10: BACKUP SLIDE (Terminology)
Other Potential Resources
Capacity resources that include one or more of the following:
• Generating resources that have not been contracted nor have legal or regulatory obligation to deliver at time of peak.
• Generating resources that do not have or do not plan to have firm transmission service reserved or are constrained.
• Generating resources that have not had a transmission study conducted to determine the level of deliverability (including new generation plants)
• Generating resources that are designated as energy-only resources
• Mothballed capacity
• Available intertie capacity
Planned Units in Full Interconnection Study Phase
To connect new generation to the ERCOT grid, a generation developer must go through a set procedure. The first step is a high-level screening study to determine the effects of adding the new generation on the transmission system. The second step is the full interconnection studies. These are detailed studies done by the transmission owners to determine the effects of the addition of new generation on the transmission system
Private Networks
An electric network connected to the ERCOT transmission grid that contains load that is not directly metered by ERCOT (i.e., load that is typically netted with internal generation).
Reliability Must-Run (RMR) Unit
A generation resource unit operated under the terms of an agreement with ERCOT that would not otherwise be operated except that they are necessary to provide voltage support, stability or management of localized transmission constraints under first contingency criteria.
Signed IA (Interconnection Agreement)
An agreement that sets forth requirements for physical connection between an eligible transmission service customer and a transmission or distribution service provider
Switchable Unit
A generation resource that can be connected to either the ERCOT transmission grid or a grid outside the ERCOT Region.