## Slide 1: Nodal Verifiable Costs Process WMS Meeting
May 15, 2007
Ino Gonzalez
ERCOT
Lead, Settlements and Billing

## Slide 2: Objectives
Define – Three-Part Offer
Verifiable Costs – Offer Caps
- startup
- minimum energy
Mitigated Offer Cap
- O&M
- incremental heat rate
Force Outage of a RUC-Committed Resource
- verifiable actual costs
Verifiable Cost Time Line
6. Verifiable Costs Process – next steps

## Slide 3: Part 1. Three-Part Supply Offer
Consists of:
Startup Offer
Minimum-Energy Offer
Energy Offer Curve
$ to Startup
$/MWh to Operate at Low Sustained Limit
$/MWh to Operate at Given MW Quantity Above Low Sustained Limit
Notes: Graphic #24 – Three-Part Supply Offers
In addition to submitting a COP, a QSE may submit a Three-Part Supply Offer.
The components of the Three-Part Supply Offer are the Startup Offer, the Minimum-Energy Offer and the Energy Offer Curve.

## Slide 4: Three-Part Supply Offer (continue)
  The Startup Offer component represents all costs incurred by a Generation Resource in starting up and reaching breaker close.
  The Minimum-Energy Offer component represents the costs incurred by a Resource in producing energy up to and including the Resource’s Low Sustained Limit (LSL) after breaker close.
  The Energy Offer Curve represents
    an offer to sell energy at or above a certain price and at a certain quantity in the DAM or
    a willingness to dispatch a given unit in Real-Time.
  Startup Offers, Minimum-Energy Offers, and Energy Offer Curves are capped.
Notes: The Startup Offer represents all costs incurred upon starting a generator, synchronizing to the grid and closing the breaker that connects it to the grid.
The Minimum-Energy Offer represents all costs incurred from breaker close to operating at the Low Sustained Limit (LSL).
The Energy Offer Curve has a different purpose in the Day-Ahead Market than it does in Real-Time Operations. In the Day-Ahead Market, an Energy Offer Curve is an offer to sell energy at or above a certain price at a certain MW level. In Real-Time Operations it represents a Resource’s willingness to be dispatched by Security Constrained Economic Dispatch (SCED).

## Slide 5: Part 2. Verifiable Cost Process
The process for determining the verifiable actual costs must be:
  developed by ERCOT (5.6.3);
  approved by the appropriate TAC subcommittee; and
  posted to the MIS Secure Area within one Business Day after initial approval and after each approved change.

## Slide 6: Offer Caps
Startup Offers and Minimum-Energy Offers are limited by caps. (PR 5.6.1(1))
The cap will be the Resource Category Generic Caps for startup and minimum-energy until ERCOT approves the Resource’s verifiable startup and minimum-energy costs. (PR 5.6.1(1))
Once approved, the cap will be the resource’s verifiable costs for startup and minimum-energy. (PR 5.6.1(1))

## Slide 7: When Are The Caps Used?
ERCOT will use the Caps to limit the startup and minimum-energy offers as they are submitted.
The Day-Ahead Make-Whole Payment will use the startup and minimum-energy offer that has been limited by the cap. (PR 4.6.2.3.1(2))
RUC settlement will use the startup and minimum-energy offer to calculate the RUC Guarantee. If no offer exists, RUC settlement will use the verifiable costs or generic cap.
RUC settlement calculations which utilize the cap are:
  RUC Make-Whole Payment (PR 5.7.1(3))
  RUC Clawback Charge (PR 5.7.2(5))
  RUC Decommitment Payment (PR 5.7.3(3))

## Slide 8: Part 3. Mitigated Offer Cap
Energy Offer Curves may be subject to mitigation in Real-Time Operations under Section 6.5.7.3, Security Constrained Economic Dispatch, using a Mitigated Offer Cap. (4.4.9.4.1)
ERCOT shall construct an incremental Mitigated Offer Cap curve such that each point on the Mitigated Offer Cap is the greater of: (4.4.9.4,(a) – (c))
1. a specified heat rate times FIP (or FOP)
2. resource’s verifiable incremental heat rate (IHR) for the output level
multiplied by FIP or FOP, plus the O&M times a multiplier
IHR = 3ax2+2bx+c; where a, b and c are known coefficients

## Slide 9: Mitigated Offer Cap – When are the Caps Used?
to project energy output for each hour the resource was RUC’d. (5.5.2 (4))
Each Energy Offer Curve must be capped at the greater of the Reference LMP (from Step 1 of SCED) at the Resource Node or the appropriate Mitigated Offer Cap. (6.5.7.3 (5)(b))

## Slide 10: Part 4. Force Outage Verifiable Costs
If a RUC-committed Resource, that experiences startup failure that creates a Forced Outage before breaker close, ERCOT shall include the Resource’s verifiable actual costs in the Resource’s RUC Guarantee, limited to the lesser of:
(5.6.3 (2))
(a) costs that qualify as normal startup expenses, including fuel and operation and maintenance expenses, incurred before the event that caused the Forced Outage; or
(b) resource’s Startup Offer in the RUC.

## Slide 11: Part 5. QSE Verifiable Costs Submittal Timeline
The most recent ERCOT-approved verifiable costs must be used going forward. (PR 5.6.1(1))
This means that once verifiable costs are approved, they will continue to be used for each Operating Day after the approval until updated verifiable costs are submitted and approved.
This also means that the (zonal) option of submitting verifiable costs for a Resource after the Operating Day has executed through the dispute process for use in settlement of that Operating Day is no longer available to the QSE. The cap, either generic or verifiable, that was in effect while executing the Day-Ahead and Real-Time activities for an Operating Day, will be used in the settlement of that Operating Day.
A QSE may file verifiable costs for a Resource at any time. (PR 5.6.1(1))
This includes prior to a Resource receiving its first Commitment, either DAM or RUC.

## Slide 12: QSE Verifiable Costs Submittal Timeline
30 days after the first time the Resource receives a RUC Commitment.
(PR 5.6.1(1))
received more than 50 RUC Commitments (PR 5.6.1(5))
five years have passed since ERCOT previously approved verifiable cost data for that Resource if the Resource that has received at least one RUC instruction in the past. (PR 5.6.1(6))

## Slide 13: QSE Verifiable Costs Submittal Timeline
Within 30 days after receiving an update notice from ERCOT to update verifiable costs for a Resource, a QSE must submit verifiable cost data for the Resource. (PR 5.6.1(7))
If the QSE does not submit verifiable cost data within 30 days after receiving an update notice, then, until updated verifiable costs are approved, ERCOT shall determine payment using the lower of:
(a) Resource Category Startup Generic and Resource Category Minimum-Energy Generic Caps; and
(b) Current ERCOT-approved verifiable startup and minimum-energy costs.

## Slide 14: PART 6. Verifiable Costs Process – next steps
Must address submittal time line for:
a. Start up
b. Minimum energy
c. Incremental heat rate
d. O&M
e. Force outage actual costs

## Slide 15: Verifiable Costs Process – next steps
Must address verifiable costs for:
a. Jointly-Owned resources
b. Combined-Cycle configurations
c. Identical generic price for CC units
e. Any protocol changes

## Slide 16: Verifiable Costs Process – next steps
4.4.9.2.3 Startup Offer and Minimum-Energy Offer Generic Caps
(1) The Resource Category Startup Offer Generic Cap, by applicable Resource category, is determined by the following O&M costs by Resource category:
Resource Category | O&M Costs ($)
Nuclear, Coal, Lignite, Hydro, Renewable | 7,200
Combined Cycle greater than 90 MW with 5+ HRS off line | 6,810
Combined Cycle greater than 90 MW with less than 5 HRS off line | 5,310
Combined Cycle less than or equal to 90 MW with 5+ HRS off line | 6,810
Combined Cycle less than or equal to 90 MW with less than 5 HRS off line | 5,310
Gas steam supercritical boiler | 4,800
Gas steam reheat boiler | 3,000
Gas steam non-reheat or boiler w/o air-preheater | 2,310
Simple cycle greater than 90 MW | 5,000
Simple cycle less than or equal to 90 MW | 2,300
Diesel | 1
Hot, cold and intermediate start up

## Slide 17: Questions
?