## Slide 1: CRR Network Model Requirements - Review CRR activities - Identify concerns or limitations
Beth Garza
Manager, Congestion Analysis & Revenue Rights
CRR Project Team
Network Model Forum
May 18, 2007

## Slide 2: CRR Monthly Auction Timeline
The timeline indicates the basic flow of activities for the allocation and auction process in a sample month. The major activities are:
1. Building the CRR Network Model
2. Allocation
3. Auction
Additional tasks not on the calendar are Registration, Bilateral Trading, and transfer of CRR ownership information
Notes: <number>
<footer>
<header>
<date/time>

## Slide 3: Auction
Annual Auction
Network model scaled to 55% capacity for months 1-12
15% of network capacity for months 13-24
Owners of PCRRs, MCFRIs and previously awarded CRRs may offer sale for whole month strips not less than one month
Obligations are available for one-month strips for one-month terms, between any source and sink for three separate Times-Of-Use
  Obligations are available between a limited set of sources and sinks for other times
Monthly Auction
90% of network capacity for coming month
Offers of PCRRs, MCFRIs and previously awarded CRRs; in whole month strips
Obligations will be available between any sources and sinks
Notes: <number>
<footer>
<header>
<date/time>

## Slide 4: CRR Products / Time of Use
Weekday On Peak Time of Use Blocks (hours 0700 – 2200 M-F)
Weekend On Peak Time of Use Blocks (hours 0700 – 2200 SS)
Off Peak Time of Use Blocks (hours 0000 – 0600; 2300 – 2400 all days)
24-hour combination of the above
  The winner of a 24-hour block, will be awarded the three primary times of use
Awarded in whole month strips, not less than one month
NPRR059 deletes
Notes: <number>
<footer>
<header>
<date/time>

## Slide 5: Creating the CRR Network Models
Each period – Time-of-Use or Calendar – is represented by a separate datacase.
Each datacase is derived from a PSS/E RAWD file (enhanced format).
  A single PSS/E RAWD file may be the source for multiple datacases.
For the monthly auction,
  CRR Network Models are expected to be developed approximately 45 days in advance of the first day of the month represented.
  Only transmission facilities in-service at the time of model development are to be included.
For the annual auction, the CRR Network Models will be based on ‘planning cases’ from the NMMS, developed for the 1st day of each operating month for a 24 month period.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 6: CRR Network Model Information
These activities will be done within the NMMS by CRR Market Operators
(taken from NMMS use cases)
Creating CRR Model
CRR Market Operator will create the Congestion Revenue Rights Model using the NMMS software and the selected
Network Operations Model Change Requests (NOMCRs)
Planning Model Change Requests (PMCRs)
Outages as required and appropriate
Special Action Model Requests (SAMRs) will also be selected and included in the model package (including SPSs and RAPs)
The output is a PSS/E RAWD file. The CRR Contingency File and the CRR Settlement File should also be packaged and sent with this model if required.
Known assumptions, limitations, constraints, or variations that may affect this use case:
The CRR Model will be generated each month 45 days prior to the proposed auction month
The NOMCRs, SAMRs, Outages, PMCRs and Dynamic Ratings that will be applied include those up to and including the first day of the proposed auction month.
The CRR User will create this model using the Case Builder.
Topology Processing must be executed prior to inserting the PMCRs into the Model.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 7: CRR Network Model Information
Creating CRR Settlement File
Create the Settlement File for the CRR Model using the NMMS software and the CRR Model for a specified date. The output is a CSV or XML file.
Creating CRR Contingency File
Based on the dates used for the Congestion Revenue Rights Model, produce the Contingency File that corresponds to the date using the NMMS software. The output is a CSV or XML file.
Known assumptions, limitations, constraints, or variations that may affect this use case:
The Contingency File for the CRR Model will be generated each month will correspond to the CRR Model that is created on that same date.
The CRR User will create these files using the Case Builder.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 8: Network Model Format (PSS/E vs. CIM)
The proposed approach
  CRR uses PSS/E – native, out of the box format (enhanced)
  CIM > PSS/E is out of the box feature of NMMS tool
  NMMS publishes CIM and PSS/E – NMMS is CIM compliant
  Minimize cost and risk
Leverages the best of both worlds
  CIM compliant at the network model source (NMMS)
  Consistent with Nodal Program approach to support applications’ native interfaces and have data provider being responsible for data transformations.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 9: Current Interpretation
CRR Requirements
The CRR Network Model input into the CRR System shall be a CIM compliant file converted to PSS/E RAWD format file following the requirements noted below. The same CIM compliant file will be posted as the CRR Network Model.
Although not required, the expectation is to also post PSS/E RAWD format file.
  CRR requirement can be satisfied for CRR Monthly auctions but can not be satisfied with the annual auctions.
  Need to determine TPTF position on annual CRR auction topology posting.
Optional Plan
ERCOT will post only PSSE formatted RAWD files for the CRR annual Auction until Planning CIM becomes available. After which, when planning CIM becomes available, both formats will be posted for the CRR annual Auction.

## Slide 10: Background Information

## Slide 11: Optimization Runtime Description & Background
NPRR 005 (August 2006 Nodal Protocols) clarified that the annual CRR auction should simultaneously optimize three Time-Of-Use (TOU) blocks across 24 months.
  Combination is referred to as 72 periods (24 months x 3 TOU).
  Supports bids/offers for any number (1 to 24) of consecutive months.
CRR Team is not aware of another software solution that can optimize 72 periods simultaneously within the 80 hour timeframe.
  PJM’s largest solution (using Nexant competitor software) solves 12 6 periods simultaneously and was thought to be pushing the envelope.
  ERCOT now understands that this optimization takes 15-40 hours to solve.
  Note that comparison is not one-to-one due to differences in other elements, such as number of buses, branches, contingencies, etc.
Time-of-Use
WD = Week Day
WE = Week End
OP = Off Peak
P = On Peak
Notes: <number>
<footer>
<header>
<date/time>

## Slide 12: Recommended Approach Decouple Time-Of-Use and Years / Maintain Monthly Granularity
 | Calendar Period | TOU Blocks | Period | Approach
Decouple TOU and Decouple Years / Monthly | 12 – Year 1 | 1 – WD | 12 | C
 | 12 – Year 2 | 1 – WD | 12 | 
 | 12 – Year 1 | 1 – WE | 12 | 
 | 12 – Year 2 | 1 – WE | 12 | 
 | 12 – Year 1 | 1 – OP | 12 | 
 | 12 – Year 2 | 1 – OP | 12 | 
The Annual CRR Auction would be comprised of six separate optimizations
Notes: <number>
<footer>
<header>
<date/time>

## Slide 13: Email response to previous SSWG questions
1. How many models (just topology) are needed?
12 datacases (PSS/E raw files) will be needed for each of six auctions. Although within the CRR system they have to be unique files attached to an auction, there is no limitation on how many times a datacase can be duplicated. I see no reason for SSWG to worry about increasing the number of cases they assemble beyond the seasonal ones that are currently being generated. I think we’ll just duplicate the summer case for use in June, July and August, for example.
2. How many cases for voltage, stability, etc. cases are required?
All non-thermal constraints will be reflected as thermal, interface limits in the CRR auction. I expect the process to determine and define non-thermal constraints to take offline coordination between Operations, Planning and CRR.
2a. If only 4 seasonal cases are needed can we use existing Data Set A (seasonal) peak cases?
  I hope so, but we’ll have to coordinate timing.
2b. Will we need more cases for the 2nd year of the annual auction?
See above, we can duplicate the cases for each month in the season.
3. Who is planned to be the group to review the auction models (we are assuming SSWG is going to be)
I don’t have a clear picture of how that would work, but let’s talk about this. Again, the issue will be timing of activities.

## Slide 14: Network Model Format (PSS/E vs. CIM)
Why PSS/E?
  Format is de-facto industry standard
  Bus/branch model
  CRR Requires a bus/branch model
  CRR COTS imports PSS/E natively (out-of-box)
  Network Model size using PSS/E format is significantly smaller than the same model in CIM XML
CIM Characteristics
  Well accepted Industry standard
  CIM model extensions may be required to cover CRR needs
  From the network model perspective, CIM describes bus/breaker model that is much more detailed
  NMMS is CIM compliant – can export in both CIM and PSS/E
  CIM -> PSS/E possible (out-of-box feature of the NMMS tool); PSS/E -> CIM not possible
  For CRR CIM bus/breaker must be translated to bus/branch by either:
    Sender/Provider (NMMS – Low Cost, Low Risk, No Schedule Impact)
    Receiver/Consumer (CRR - High Cost, High Risk, High Schedule Impact)
    Integration Layer (High Cost, High Risk, High Schedule Impact)
The proposed approach
  NMMS publishes CIM and PSS/E
  CRR uses PSS/E
  Minimize cost and risk
Leverages the best of both Worlds
  CIM compliant at the network model source (NMMS)
  Leverages PSS/E as de-facto standard native to the CRR off-the-shelve product
  Consistent with Nodal Program approach to support applications’ native interfaces and have integration layer or data provider being responsible for data transformations.
Notes: <number>
<footer>
<header>
<date/time>

## Slide 15: CIM to PSS/E Transformation
Notes: <number>
<footer>
<header>
<date/time>