## Slide 1: Affects of Wind on Frequency
TAC June 7, 2007

## Slide 2: Objectives
Review the ERCOT CPS1 scores
Describe the Wind Only QSEs affect on the Balancing Energy Offset
Describe the Wind Generation affect on Frequency

## Slide 3: Not Covered
Probability of severe wind gusts and trips due to over-speed.
Probability of sudden loss of wind generation
Predictability of wind generation and the affects on reserves
Impacts to the Grid with increasing levels of wind generation

## Slide 4: Frequency Performance Measure
CPS1 simply means: A violation occurs when the 1 minute average of frequency deviation in ERCOT exceeds +/- 0.03 Hz

## Slide 5: CPS1 Score Historical Trend

## Slide 6: ERCOT CPS1 Scores by Interval

## Slide 7: Wind Capacity in the ERCOT System
Total Installed Wind Capacity:
3148 MW
Additional 1928 MW
(5076 MW Total) by 1/1/2008
1628 MW
+800 MW
756 MW
244 MW
+402 MW
255 MW
+160 MW
65 MW
200 MW
+200 MW
186 MW
120 MW
60 MW

## Slide 8: ERCOT Monthly Profiles

## Slide 9: Determination of the Balancing Energy Offset
Balancing Energy is the difference between the Short Term Load Forecast and the sum total of the QSEs base power schedules
  Resource Plans are utilized to validate a QSE’s ability to meet their base power schedules
A manual offset is utilized when there are known issues with the base power schedules and/or generating resources
The Balancing Energy Ramp begins 5 minutes before the start of the interval and ends 5 minutes after the start of the interval
The Balancing Energy Deployment objective is to maintain Regulation Up and Down Reserves

## Slide 10: Determining Offset for Wind SCE
Note: Positive SCE indicates actual wind output exceeds schedules
Negative SCE indicates actual wind output is less than scheduled

## Slide 11: What is the relationship between Frequency and Real Power?
ERCOT interconnect - approximately 500 – 600 MW loss of generation results in 0.1Hz drop in frequency
Eastern interconnect - approximately 3000 MW loss of generation results in 0.1Hz drop in frequency
Sudden changes in generation and/or load will result in frequency deviations

## Slide 12: Frequency During High Wind Output (0500-0600 March 25)

## Slide 13: Change in Wind and Load vs. Frequency (0500-0600 March 25)

## Slide 14: Frequency During High Wind Output (0200-0300 May 4)

## Slide 15: Change in Wind and Load vs. Frequency (0200-0300 May 4)

## Slide 16: Frequency During Large Wind Drop-Off (0900-1200 Feb. 24)

## Slide 17: Change in Wind and Load vs. Frequency (1100-1200 Feb. 24)

## Slide 18: Conclusion
Detail consultant study on the affects of wind on A/S requirements may change these initial findings
Actual Wind Generation Output is considered in the manual offset for Balancing Energy
The minute to minute change in Wind Generation Output, at current installed wind capacity, doesn’t appear to have a significant impact on Frequency
The minute to minute change in Load Output has a significant impact on Frequency
Wind can have a significant impact on Responsive Reserve during disturbance type events