## Slide 1: TX SET Update to RMS
Wednesday, July 11, 2007

## Slide 2: Congratulations to ALL
On the weekend of June 23rd and 24th, 2007, the TX Market “Successfully Implemented” TX SET Version 3.0. This implementation provides the market with:
  An “Automated Process” to Transition ESI IDs from Defaulting CR to POLRs during a Mass Transition event, which will also reduce the number of days the Market completes all ESI IDs involved in the transition compared to previous Mass Transitions.
  New “Processes and Functionality” based upon requirements identified in the new “IOU” Terms and Conditions (PUCT Project 29637).
  New transaction processing times for ERCOT to better support and communicate “Priority Move-Ins” to TDSPs.
  New “Processes and Functionality” based upon requirements identified in the new “POLR” Rulemaking (PUCT Project 31416)

## Slide 3: Workshop Action Item for TX SET
TX SET received the following Action Item from the Retail Market Workshop on Small Renewable Generation.
  Workshop would like TX SET to provide options and recommendations on how to facilitate generation values.
    How does the TDSP send generation values?
TX SET discussed a Short Term solution via conference call on Thursday, June 28. We also made a decision that Long-Term discussions would be deferred to subsequent meetings in July and August.

## Slide 4: Short-Term Discussions
TX SET’s Definition of Short-Term is “What is available today in the TX SET 867_03 Monthly Usage Transaction that could be used to support or communicate Generation?”
We felt that our short-term recommendation should be able to support both input and output readings regardless if one, two, or more meters were being utilized to provide the information.

## Slide 5: Short-Term Recommendation
867_03 Monthly Usage Transaction
  REF~JH (Meter Role) Segment
    I - Ignore Flag
      This consumption did not contribute to the summarized total (do nothing)
    Example of 867_03 used to communicate generation in this segment:
        REF|JH|I
        REF|MT|KHMON
        QTY|QD|7044
        MEA|AA|PRQ|7044|KH|65463|66637|51
        MEA||MU|6
        PTD|PL|||MG|297649
        DTM|150|20070411
        DTM|151|20070510

## Slide 6: Next Steps for TX SET
Review and Update where necessary the Retail Market Guide Procedures as it pertains to:
  Working Groups shall submit the following materials for RMS approval:
    Texas SET Implementation Guides
    Texas SET Change Controls
If changes are recommended by TX SET, we will submit an RMGRR to RMS for Approval in August.

## Slide 7: Next Steps for TX SET
Small Renewable Generation
  Short-term business requirements will be discussed at the July 12th
  Long Term Recommendations that could involve changes to the TX SET 867_03 Implementation Guide, along with developing requirements will be on the July and August agenda.
Monitor the Advanced Metering Rule for changes to TX SET transactions/processes
Lessons Learned
  TX SET will work in conjunction with Market Coordination Team and Texas Test Plan Team to evaluate feedback from Version 3.0 Lessons Learned to improve future implementations.

## Slide 8: Questions?