## Slide 1: HOUSTON AREA CONSTRAINT MITIGATION: PHASE II
Technical Advisory Committee
Dan Woodfin
August 2, 2007

## Slide 2: Singleton / Zenith Substations
New 345 Kv Singleton Sub
New 345 Kv Zenith Sub
Singleton Sub Cost Zenith Sub Cost
$23.7 Million $15.4 Million
In-service by peak
2009 2011

## Slide 3: Project Need
North to Houston import constraints
Congestion on the Tomball 345/138 kV autotransformer
This set of projects relieves the autotransformer congestion and increases the North to Houston import capability

## Slide 4
Economic Analysis
YES
26.63
2011 w Sandow, Oak Grove 1,2, Sandy Creek 1 and TNP – Bell County Project.
YES
7.89
2010 w Sandow 5, Oak Grove 1 and 2
YES
4.8
2009 w only Sandow 5
RECOMMEND
Annual
PCS ($M)
GENERATION SCENARIO
PRODUCTION COST SAVINGS (PCS) OF HACM Phase II PROJECT
Singleton Substation Addition
The annual carrying charge is the first year annual revenue requirement for the project (capital cost x 16.8%), which should be less than the annual production cost savings for the project to be considered economic.
3.95
3.95
3.95
ANNUAL
CARRYING
CHARGE

## Slide 5
Economic Analysis
YES
4.53
2011 w Sandow 5, Oak Grove 1,2, Sandy Creek 1
RECOMMEND
Annual
PCS ($M)
GENERATION SCENARIO
PRODUCTION COST SAVINGS (PCS) OF HACM Phase II PROJECT
Zenith Substation Addition with Singleton Project In-Service
The annual carrying charge is the first year annual revenue requirement for the project (capital cost x 16.8%), which should be less than the annual production cost savings for the project to be considered economic.
2.57
ANNUAL
CARRYING
CHARGE

## Slide 6: Stakeholder Review
The Stakeholder review period for the Singleton Substation was held in January 2007.
There were no dissenting comments on the project.

## Slide 7: ERCOT Support for the Project
With Sandow 5 generation on-line by 2009 and Oak Grove Units #1 #2 on-line by 2010, the Singleton Substation project is economic
With Sandow 5 / Sandy Creek / Oak Grove Units #1 #2 on-line by 2011, the Zenith Substation project is also economic
ERCOT Staff recommends that the project be endorsed by the Board.

## Slide 8
QUESTIONS ?