## Slide 1: LFC EDS Testing - Settlements
LFC Workshop
10-10-2007

## Slide 2
Table of Contents
Phase 1 and 2 Settlement - Details
Phase 3 Settlement - Assumptions
Phase 3 Settlement - Details
Phase 3 Settlement – Formulas & Examples

## Slide 3: Phase 1 and 2 Settlement - Overview
Phase 1 LFC Testing
No Zonal Settlement Impacts
Phase 2 LFC Testing – Individual QSE Test
ERCOT Operators will issue Settlements a VDI noting test Start and Stop Times
Settlements will not calculate URC for hour before test, during the test, and the hour following the test
QSEs will receive an SCE exception throughout the test intervals noted on the VDI

## Slide 4: Phase 3 Settlement - Assumptions
Assumptions required for accurate Phase 3 Settlement:
The resource specific energy offer curves provided by QSEs will be representative of the Balancing Energy Service Bids submitted to the Zonal Market during LFC System testing.
QSEs will continue to update their Resource Plans and Base Power Schedules during the test period
QSEs shall continue to update their Zonal Schedules throughout the test period.
QSEs shall follow the base points provided by the Nodal System and ignore instructions from the Zonal System.
The same constraints will be activated in both Zonal RTCAM and Nodal TCM, and the same resources will be deployed to resolve local congestion by both the Zonal and Nodal Systems.

## Slide 5: Phase 3 Settlement - Details
Steps for Phase 3 Settlement:
Transactions will be settled according to the Zonal Protocols using MCPEs calculated in the Zonal Market.
All QSE VDI will be issued to define the “test period”
  Test period starts when first QSE is brought under Nodal control and stops when last QSE is returned to Zonal Control
Settlements will not calculate URC during the “test period”
  URC will not be calculated for hour before test period, during the test period, and the hour following the test period
All QSEs will receive and SCE exception during the test period
Settlements will replace Zonal Instructed Output levels for all units deployed in the Zonal Market for OOME and Local Balancing with integrated SCED base points

## Slide 6: Base Point Integration - Formula
Below is the formula that will be used to integrate SCED base points into 15 minute values used to settle OOME and Local Balancing
AABP = Σy ((BP y + BP y-1)/2 * TLMP y) / (Σy TLMP y)
Variable | Unit | Definition
AABP | MW | Adjusted Aggregated Base Point—The Generation Resource’s aggregated Base Point NOT adjusted for Ancillary Service deployments, for the 15-minute Settlement Interval.
BP y | MW | Base Point by interval—The Base Point for the Generation Resource at the Resource Node, for the SCED interval y.
TLMP y | second | Duration of SCED interval per interval—The duration of the portion of the SCED interval y within the 15-minute Settlement Interval.
y | none | A SCED interval in the Settlement Interval. The summation is over the total number of SCED runs that cover the 15-minute Settlement Interval.
NOTE* The average regulation instruction will not be factored into the base point in order to ensure similarity between the SCED base point and the Zonal calculated instructed output level.

## Slide 7: OOME Settlement - Formulas
Below are the formulas that will used to settle OOME during Phase 3 of LFC Testing
OOME Up Payment to Provider
EOOMAMT = -1 * (MAX(RCGFCU - MCPER), 0)
* MAX(0, MIN(GSITETOT-RP, OOMUEQ))
Where for Zonal: OOMUEQ = MAX(0, OOMEVDI or OOMIOL - RP)
Where for LFC Testing: OOMUEQ = MAX(0, ¼*AABP - RP)
OOME Down Payment to Provider
EOOMDNAMT = -1 * [(Max (0, (MCPER - RCGFCD))
* MAX (0, (Min ((RP - GSITETOT), OOMDEQ))]
Where for Zonal: OOMDEQ = Max (0, (RP - OOMEVDI or OOMIOL))
Where for LFC Testing: OOMDEQ = Max (0, (RP - ¼*AABP))

## Slide 8: Local Balancing Energy - Formulas
Below are the formulas that will used to settle Local Balancing during Phase 3 of LFC Testing
Local Balancing Energy Up to Provider
LBEUPAMT = -1 * [(MAX (OOMLEUPBP, MCPER)) - MCPER)
* (MAX (0, MIN ((GSITETOT - RP), LBEUQ)))]
Where for Zonal: LBEUQ = Max (0, (LEIOL - RP))
Where for LFC Testing: LBEUQ = Max (0, (¼*AABP - RP))
Local Balancing Energy Down to Provider
LBEDNAMT = -1 * [Max(0, (MCPER - OOMLEDNBP))
* MAX (0, MIN ((RP - GSITETOT), LBEDQ))]
Where for Zonal: LBEDQ = Max (0, (RP - LEIOL))
Where for LFC Testing: LBEDQ = Max (0, (RP - ¼*AABP))

## Slide 9: Base Point Integration Example
 | Length of SCED (seconds) "TLMP" | Base Point for G1 (MW) "BP"
Last SCED in 15 min | 300 | 90
1st SCED in 15 min | 300 | 100
2nd SCED in 15 min | 300 | 120
3rd SCED in 15 min | 100 | 140
4th SCED in 15 min | 200 | 150
AABP |  | 115
Total | 900 | 
Base Point Integration Example

## Slide 10: OOME Settlement Example
OOME Up Payment to Provider Example
Input Data | Total | interval 1 | interval 2 | interval 3 | interval 4 | interval 5
RP_GT1 (converted to MWh) | 100 | 20 | 20 | 20 | 20 | 20
AABP *1/4 | 1300 | 80 | 80 | 80 | 80 | 80
Actual Unit Output | 410 | 82 | 82 | 82 | 82 | 82
MCPER | 152.8 | 22.35 | 27.46 | 35.89 | 34.64 | 32.46
Payment Where OOMIOL = AABP | Total | interval 1 | interval 2 | interval 3 | interval 4 | interval 5
OOMIOL_GT1 = AABP | 400 | 80 | 80 | 80 | 80 | 80
RP_GT1 (converted to MWh) | 100 | 20 | 20 | 20 | 20 | 20
MCPER | 152.8 | 22.35 | 27.46 | 35.89 | 34.64 | 32.46
Unit Generic Cost per MWh | $750.00 | $150.00 | $150.00 | $150.00 | $150.00 | $150.00
EOOMUP Quantity | 300 | 60 | 60 | 60 | 60 | 60
OOME Up Payment | -$35,832.00 | -$7,659.00 | -$7,352.40 | -$6,846.60 | -$6,921.60 | -$7,052.40

## Slide 11: Bill Determinant and Extract Details
Settlements will determine which units received a Zonal unit specific instruction during Phase 3 LFC Testing
Unit Specific instructions consist of the following Bill Determinants:
  OOMIOL – OOME Instructed Output Level
  OOMEVDI – VDI OOME Instructed Output Level
  LEIOL – Local Energy Instructed Output Level
Next, Settlements will request all SCED generated base points for the generation resources that received Zonal unit specific instructions
Settlements will integrate the base points into 15 minute settlement values
The integrated base points will replace the original OOMIOL, OOMEVDI and LEIOL values
The updated values will be imported to the Settlement system before Initial Settlement. QSEs will receive in their extracts.