## Slide 1: COPS ERCOT Usage Data Loading & Data Aggregation
Jackie Ashbaugh
ERCOT

## Slide 2: Issue
  The Data Aggregation process requires a considerable amount of extra NIDR kWh data to be loaded into memory for profiling purposes, as ERCOT’s current usage loading process allows usage data to load that covers up to 184 days. This significantly increases processing time.
  ERCOT must also include additional logic when implementing new functionality that would not be required if usage reads were limited to a reasonable number of days, i.e., based upon the monthly requirement.
Notes: No comment.

## Slide 3: Background
  February 2003 867_03 usage data loading implementation at ERCOT
    867_03 NIDR usage data submitted by the TDSPs allows for a read that includes up to 184 days
    867_03 Activity Report - Error code 20 – ‘STOPTIME minus STARTTIME exceeds 184 days for data submitted.’
  Protocol References
  10.3.3.1 Data Responsibilities
  TDSPs shall be responsible for the following:
  (1) Providing consumption data for each ESI ID and RID on a monthly basis according to the data timeliness and accuracy standards defined in this Section and in the SMOG;…
  (5) Calculating consumption for any unmetered services by ESI ID and submitting such data monthly to ERCOT, subject to ERCOT audit. These calculations must be made pursuant to TDSP approved tariffs; and…
Notes: No comment.

## Slide 4: Background
  Protocol References cont’d
  10.3.3.3.1 Past Due Data Submission
  ERCOT shall provide a report to the appropriate TDSP for any ESI ID or RID for which consumption data has not been received in the past thirty-eight (38) days. Upon receipt of the missing consumption data report, the TDSP shall have two (2) Business Days to submit the missing consumption data.
  11.2.2 Data provision and verification of Non EPS Metered Points
  The TDSP will provide data for TDSP Metered Entities as defined in Section 10, Metering, of these Protocols.
  The TDSP will provide data in accordance with the TDSP meter data responsibilities detailed in Section 10, Metering, and will conform to data formats specified in Section 19, Texas Standard Electronic Transaction (TX SET).
  ERCOT will:
  …
  (3) Provide a report to the TDSP listing each ESI ID for which ERCOT has not received consumption data for thirty-eight (38) days; and
Notes: No comment.

## Slide 5: Data Aggregation
  Data for Scaling Factor
  The profiling process computes a scale factor by dividing the meter usage (kWh) by the kWh sum of the profile data for the same time period. For performance reasons, at the beginning of this process Data Aggregation loads the maximum amount of profile data that may be required. Since reads are allowed to span 184 days, 733 days of profile data must be loaded.
  If usage read spans 184 days
  Data Aggregation loads from the trade date forward 183 days to support a 184 day read that begins on the trade date.
  And since ERCOT is required to use any reads within 365 days of the trade date, Data Aggregation must also load 365 + 184 days prior to the trade date (to support a read that spans 184 days and stops 365 days prior to the trade date). 365 +184 + 184 = 733
Notes: No comment.

## Slide 6: NIDR 867_03 Usage Loading
Number of NIDR kWh records where total days in read is between 60 and 184
Number of NIDR kWh records loaded in ERCOT systems by year
Notes: No comment.

## Slide 7: NIDR 867_03 Usage Loading
Number of NIDR kWh records where total days in read is between 60 and 184
Notes: No comment.

## Slide 8: Recommended Change
  Update the 867_03 usage data loading business logic
    867_03 NIDR usage data submitted by the TDSPs allows for a read that includes up to 60 days
    867_03 Activity Report - Error code 20 – ‘STOPTIME minus STARTTIME exceeds 60 days for data submitted.’
  If usage loading process capped the read period to 60 days, it would change the amount of data required for data aggregation from 733 days to 485.
  If capped at 60 days
  Data Aggregation would load from the trade date forward 59 days to support a 60 day read that begins on the trade date.
  And since ERCOT is required to use any reads within 365 days of the trade date, Data Aggregation must also load 365 + 60 days prior to the trade date (to support a read that spans 60 days and stops 365 days prior to the trade date). 365 +60 + 60 = 485
Notes: No comment.

## Slide 9: Recommended Change Benefits
  Data Aggregation
    Processing time improvements for both Zonal and Nodal
  Load Profiling
    Accuracy improvement for Annual Validation
      Meter reads longer than 45 days are excluded for Residential assignments
      Long meter reads are included for Business assignments, but tend to unduly skew the load factor calculation
    Requires 184 days of profiles to be created before the actual implementation date of a new profile
  Market
    CRs receive more timely reads
Notes: No comment.

## Slide 10: Next Steps
Presented to COPS on 11/6/2007
TDSPs have requested review of the NIDR kWh records to determine root cause for the number of days the reads include
ERCOT will file ERCOT Initiated MarkeTrak Issue to each of the TDSPs for their review
ERCOT will review the TDSP findings to determine the recommended threshold change
TDSP findings will be reported with the ERCOT recommendation at the next Subcommittee meetings:
  COPS – 12/3/2007
  RMS – 12/5/2007

## Slide 11
Questions?