# WMS proposed response to TAC and Board Questions

Background

- Following the April 17, 2006 Firm Load Shedding Event ERCOT implemented a formulaic discounting of spinning generation capacity, thus reducing the calculated adjusted responsive reserves (a.k.a. Physical Responsive Capability), and the PUCT approved a new special emergency service, Emergency Interruptible Load Service (EILS).

- Discounting reserves results in ERCOT taking command and control actions (OOMing Units) which forces price down in real-time (prices fall during periods of scarcity).  ERCOT is taking actions to restore reserve levels before market energy offers are exhausted, and depressing prices in the process.

- TAC directed the formation of a Long-Term Solutions Task Force to address an alternative for the EILS service to meet the objectives of PUCT Subst. R. 25.507(h)).  In October, TAC approved a resolution recommending to the Board that ERCOT immediately increase its purchases of Responsive Reserves by 500 MW for the hours ending 0600 through 2200, with the intention of reducing both the number of short-supply Alerts issued by ERCOT and the frequency of OOME and OOMC deployments.

- Many people see EILS as similar to LaaR’s and LaaR participation in RRS.  EILS participants and LaaR participants are not related and do not provide similar services.  LaaR’s which participate in RRS have auto activation Under Frequency Relay and provide automatic response to frequency disturbances.  EILS is a Demand Response Program, with deployment only as a last resort during EECP Step 3 and via verbal instruction.  RRS is a service required to maintain frequency on a continual basis.

- EILS and an increase in RRS were linked by the original work of the LTSTF.

- In November, the PUC adopted EILS rule changes eliminating the requirement for a Long Term Solution, thus breaking any tie between the increase in RRS and EILS.

- Since the last Board and TAC meetings, ERCOT, working with stakeholders has refined its practice for discounting reserve levels.  Additional work is underway to refine the practice further.

- In October the Board instructed TAC to answer questions 1 through 6 below and report on any other issue TAC believes should be considered by the Board at the December 2007 meeting in determining whether to approve the proposal to increase RRS.  TAC added one more question.  Those questions and the answers recommended by WMS follow:

- Whether (a) the proposed increase of RRS by 500 MWs (from 2,300MW to 2,800MW) during hours-ending 0600 to 2200 should be an increase to only the amount of RRS or should be a combination of RRS and NSRS as discussed in the LTSTF White Paper and (b) whether 500 MWs is the right amount for the increase in Ancillary Services;

  - RRS and NSRS are two different services with two different purposes.   NSRS cannot substitute for RRS.

  - The amount of additional RRS needed to correct the price formation problem  has a direct correlation to the amount of RRS discount . WMS recommends that the amount of RRS procured be increased, (above 2300 MW) in an amount equal to the discount.

- Whether the proposed increase of RRS (or combination of RRS and NSRS) by 500 MWs is consistent  with (a) Section 6.4.1(2) of the Protocols and (b) the Long Term Solution provision of the EILS Rule (PUCT Subst. R. 25.507(h));

a. 	 WMS supports the IMM and ERCOT staff position that all planned online capacity is not deliverable. WMS believes there is enough empirical evidence to support the “increase”.

b. 	On November 1, 2007, the PUC voted to delete the Long Term Solution provision from the Commission’s EILS Rule.  Consequently, the merit of the proposed RRS increase is no longer in part a function of whether the increase constitutes a long term substitute for EILS Service.)

- Whether LaaR can maintain the existing 1,150 MWs level of participation in all hours of the RRS market if the Board were to take action at the December 2007 Board Meeting to increase the amount of RRS (or combination of RRS and NSRS) at that meeting.  ERCOT staff shall immediately begin working on system changes necessary to ensure that LaaR can continue to participate in the RRS market at the current 1,150 MWs levels and ERCOT staff shall report to the Board whether the system changes have been completed at the December 2007 Board Meeting;

The software updates are underway and it is expected that LaaR will be able to maintain its existing 1,150 MW level of participation by December 2007 Board Meeting.

- Whether the level of LaaR participation should be increased above 1,150 MWs if RRS is increased above 2,300 MWs (with the understanding that the ERCOT study to determine whether this is viable is currently underway but may take up to six months to complete)

A 2002 study had concluded that if all load trips at one frequency (as is currently done), then 1150 MW is the limit. If load shed is tiered, then it would be possible to increase LaaR participation up to 1725 MW.  (Going to tiered frequency response is a significant market change, which would likely take more than 6 months to implement, and could have significant impact on contracts already in place between market participants).

- Whether an increase in the amount of RRS (or combination of RRS and NSRS) is needed for all hours between hours-ending 0600 and 2200 or on the weekends;

WMS recommends to TAC that additional Responsive Reserves should be procured for the hours ending 0600 through 2200 for all days, with the hourly amount procured tied to day-ahead forecasted temperatures.

- A cost/benefit analysis or other type of reasonable comparison of the benefits of EILS vs. RRS, including any broader benefits that increasing the amount of RRS (or combination of RRS and NSRS) may have (such as addressing the issues raised by the Independent Market Monitor);

  - EILS will not cost more than $50 million annually and offers the benefit that it may reduce or eliminate some occurrences of firm load shed.

  - Increasing RRS is likely to ____ Ancillary Services prices by $__ annually and ____ BES by $____ annually.

  - Increasing RRS should nearly eliminate ERCOT command and control actions and therefore effectively solve the price formation issues raised by the IMM.

- (Additional TAC added Question) If the board adopts the 500 MW increase in RRS (or other proposal) is there still a need for the Administrative Pricing Proposal.

It is not necessary to both increase RRS and impose one of the Administrative Pricing Proposals.   Increasing RRS will nearly eliminate ERCOT command and control actions and therefore effectively solve the price formation issues that the Administrative Pricing Proposal was intended to address.