## Slide 1: Resource Node Locations 01-16-08 WMS Meeting

## Slide 2: Agenda
Introduction
Discussion Points
Information and Answers to Questions
Example Diagram for discussion
Questions

## Slide 3: Introduction – ERCOT Actions To Date
The spreadsheet posted 01-04-08 ---- had most of the Resource Nodes designated to be the “low side” of the Generation Step Up (GSU) transformer.
Tests have been conducted by ABB using the low side.
ERCOT has identified pros and cons for assigning the Resource Node to the low side or to the high-side of the GSU transformer.

## Slide 4: Discussion Points
Pros:
Low-side approach has been tested by ABB.
Using the low-side is a more straight forward for Network Model management.
No problem with voltage support. Either way will use measured Vars from Pi.
Both ways result in the same LMP’s.
Cons:
Using the low side increases the instances in which the CRR’s are not included in the Deration Factor (DRF) calculation.
Pros:
No problem with voltage support. Either way will use measured Vars from Pi.
Both ways result in the same LMP’s.
Using the high side decreases the instances in which the CRR’s are not included in the DRF calculation.
Cons:
Resource Node on the high side introduces Network Model mapping complexity.
May require more clarity to protocol definition.
High side approach remains to be confirmed and tested.
LOW-SIDE
HIGH-SIDE

## Slide 5: With the Resource Nodes (on low side of the GSU Xfrmer)
The model will have the “Connectivity Node” of the generator to the ERCOT system. This info will be passed to MMS as the Resource Node.
The model will have the locations of the CT’s used by the EPS meters to provide Settlement Quality measurement of the injections and withdrawals. These EPS locations are where the 15 minute price will be calculated and used for “RT Energy” settlement.
The ratings of the GSU Xfrmers are provided by the Resource Entity through the RARF and are entered into the model. These “elements” will NOT limit the flow by the CRR system.
A 15 minute price will be calculated for the Resource Node in the event that the Resource is off-line.
A 15 minute price will be calculated for the Resource Node in the event that the GSU Xfrmer is de-energized for maintenance. (The15-minute price is calculated as the average of other prices in the substation).
A 15 minute price will be calculated for a Resource Node in the event that the part of the substation or the entire substation with the Resource Node is de-energized. (A separate calculation would be performed that essentially sets the price to be equal to the substation average or the system wide average.)

## Slide 6: With the Resource Nodes (mostly on the high side of the GSU Xfrmer)
The model will have the “Connectivity Node” of the generator which will indicate the generator’s connection to the ERCOT System. This info will be passed to MMS for power flow analysis.
The model will have the designated Resource Node for each Resource. This will be the point in which Offers are submitted, CRR’s are bought and sold, and Energy Only offers and bids can be made. DAM awards are settled at these Resource Nodes.
The model will have the locations of the CT’s used by the EPS meters to provide Settlement Quality measurement of the injections and withdrawals. These EPS locations are where the 15 minute price will be calculated and used for “ RT Energy” settlement.
The ratings of the GSU Xfrmers are provided by the Resource Entity through the RARF and are entered into the model. These “elements” will NOT limit the flow by the CRR system.
A 15 minute price will be calculated for the Resource Node in the event that the Resource is off-line.
A 15 minute price will be calculated for the Resource Node in the event that the GSU Xfrmer is de-energized for maintenance (without special sub-routine).
A 15 minute price will be calculated for a Resource Node in the event that the part of the substation or the entire substation with the Resource Node is de-energized. (A separate calculation would be performed that essentially sets the price to be equal to the substation average or the system wide average.)

## Slide 7: Current Definition of Resource Node
Resource Node (Current Definition)
The Electrical Bus defined in the Network Operations Model at which a Resource's measured output is settled.
For a Generation Resource that is connected to the ERCOT Transmission Grid only by one or more radial transmission lines that all originate at the Generation Resource and terminate in a single substation switchyard, the Resource Node is an Electrical Bus in that substation.
For all other Generation Resources, the Resource Node is the Generation Resource's side of the Electrical Bus at which the Generation Resource is connected to the ERCOT Transmission Grid.

## Slide 8: Diagram for Discussion

## Slide 9: Questions
Other concerns not addressed.
Timeline for performing analysis and finalizing direction.
Questions ?