## Slide 1: Alignment of CSC Shadow Price Caps with New System-wide Offer Caps
ERCOT WMS Meeting
January 16, 2008

## Slide 2: Background
CSC shadow price cap of $2,500/MW implemented via SCR 747 on 12/07/2006
The $2,500/MW shadow price cap was developed based on an offer cap of $1,000/MWh and an offer floor of ($1,000)/MWh
  Typical shift factor difference between most effective zones approximately 0.40
  $2,500 x 0.40 = $1,000

## Slide 3: Background
System-wide offer cap changed to $1,500/MWh on March 1, 2007
System-wide offer cap will change to $2,250/MWh on March 1, 2008
Offer floor remains at ($1,000)/MWh (Protocols Section 6.11.1)
When there is zonal congestion, with the current CSC Shadow Price cap of $2,500:
  Offers > ~$1,000/MWh will be ignored
  Zonal prices will be limited to approximately $1,000/MWh, even if all available energy is exhausted in the most effective zones

## Slide 4: Changes
Increase the CSC Shadow Price cap to $5,600/MW
  Offer cap increase from $1,000 to $2,250 (2.25x)
  Shadow price cap increase from $2,500 to $5,600 (~2.25x)
Apply price administration to limit any negative zonal price to a minimum of ($1,000)/MWh
  Automated and ex ante ultimately
  May be manual and ex post initially
  CSC shadow price will also be re-determined administratively and ex post if this price administration occurs