| NPRR Number |  | NPRR Title | Settlement of Power Imported via DC Ties (Back to Back Ties) and Block Load Transfer Under Emergency Conditions |
| --- | --- | --- | --- |
| Date Posted |  |
| Protocol Section(s) Requiring Revision (Include Section No. and Title) | 6.6.3.4, Payment for emergency import via a DC Tie 6.6.3.5, Real-Time Payment for a Block Load Transfer Point |
| Requested Resolution (Normal or Urgent, and justification for Urgent status) | Normal |
| Revision Description | During emergency conditions EROCT may order emergency energy imports over the DC Tie interconnects and/or the transfer of BLT Load from the ERCOT control Area to a Non-ERCOT control Area. These revisions add settlement formulas to pay a QSE for emergency energy imported over the DC Ties and for energy supplied to BLT Load moved from the ERCOT Control Area to a Non-ERCOT Control Area during emergency conditions. These payments may only be made for actions taken by the QSE in response to an ERCOT Dispatch Instruction. |
| Reason for Revision | In accordance with Section 6.5.9, Emergency Operations, ERCOT may order the import of emergency energy over the DC Tie Interconnections or the transfer of BLT Load from the ERCOT Control Area to a Non-ERCOT Control Area. The additions to the Settlement formulas included in this NPRR are intended to make the QSE responsible for responding to the ERCOT Dispatch Instructions issued during emergency conditions is assured a guaranteed cost recovery. Charges to cover the payments described in this NPRR are included in Section 6.6.10, Real-Time Revenue Neutrality Allocation. |
| Overall Market Benefit | Encourage availability of an alternative source of energy during EECP and thus Increase grid and system reliability |
| Overall Market Impact | Costs of Emergency power would be uplifted |
| Consumer Impact | None. |
| Credit Implications (Yes or No, and summary of impact) | None. |
| Reason for Revision (from Transition Plan Task Force (TPTF) Charter Scope) | (1) Revisions resulting from Commission orders; (2) Clarifications of Protocol language that do not change the intent or technical specifications of the Protocols; (3) Correction of technical errors or processes that are found to not be technically feasible; (4) Revisions to the Protocols necessary to implement the results of the value engineering analysis or to otherwise avoid severe cost impacts; or (5) Other (describe): To allow ERCOT to adequately settle import power during emergency conditions via the DC ties and transfer BLT load to Non-ERCOT Control Areas and to synchronize with zonal protocol PRR543, approved in 2006. |
| TPTF Review (Yes or No, and summary of conclusion) |  |

Quantitative Impacts and Benefits

Instructions:  To allow for comprehensive NPRR consideration and development of the Cost Benefit Analysis (CBA), please fill out each block below completely and provide as much detailed information as possible.  Wherever possible, please include reasons, explanations, and cost/benefit analyses pertaining to the PRR.

| Assumptions | 1 | e.g.: Key assumptions used in estimating market cost and/or benefit |
| --- | --- | --- |
|  | 2 | Dependencies on other projects or other timing requirements |
|  | 3 |  |
|  | 4 |  |
| Market Cost |  | Impact Area | Monetary Impact |
|  | 1 |  |  |
|  | 2 |  |  |
|  | 3 |  |  |
|  | 4 |  |  |
| Market Benefit |  | Impact Area | Monetary Impact |
|  | 1 | Grid Reliability |  |
|  | 2 | Additional tools that ERCOT can use to manage the grid |  |
|  | 3 |  |  |
|  | 4 |  |  |
| Additional Qualitative Information | 1 |  |
|  | 2 |  |
|  | 3 |  |
|  | 4 |  |
| Other Comments | 1 |  |
|  | 2 |  |
|  | 3 |  |
|  | 4 |  |

| Sponsor |
| --- |
| Name |  |
| E-mail Address |  |
| Company |  |
| Phone Number |  |
| Cell Number |  |
| Market Segment |  |

| Market Rules Staff Contact |
| --- |
| Name |  |
| E-Mail Address |  |
| Phone Number |  |

For TPTF Meeting and Review Consideration:

Throughout Section 6.5.9, Emergency Operations, a variety of different emergency conditions are described which may warrant ERCOT Operator directed actions. These events range from transmission emergencies –  described as “Market-based congestion management techniques embedded in SCED as specified in these Protocols will not be adequate to resolve transmission security violations” (6.5.9.3.3) – to ERCOT Actions to be taken in response to EECP events.

Note: Depending on TPTF action, the following may be included, subject to revision, in the NPRR form entry (i.e. Reason for Revision, etc):

The added payments for emergency energy imported over the DC Ties and for BLT Load transferred out of the ERCOT Control Area that are described in this NPRR are consistent with the current process as described in PRR 543, Schedules and Emergency Assistance Over CFE-ERCOT Ties, approved on 02/21/2006. The ability of ERCOT to import energy over the ties in emergency situations would continue in the Nodal market.  In the Zonal market, imports via the ties during emergency conditions and Block Load Transfers (BLTs) are settled based on a minimum price equal to the Fuel Index Price (FIP) times a Heat Rate of 18MMBtu/MWh (FIP*18).  However, in the Nodal market, these two services are settled at the Real Time Settlement Price per Settlement Point (RTSPPp), regardless of whether the RTSPPp falls below the FIP *18 price.  Allowing the RTSPPp to fall below the FIP *18 price would risk not having this capacity available in emergency situations.  This would be contrary to the original premise of PRR543.  Hence, ERCOT believes this was an omission and that the settlement price should be changed to include a floor price of FIP*18.

Proposed Protocol Language Revision

6.6.3.4	Real-Time Energy Payment for DC Tie Import

(1)	The payment to each QSE for energy imported into the ERCOT System through each DC Tie is calculated based on the Real-Time Settlement Point Price at the DC Tie Settlement Point.  The payment for a given 15-minute Settlement Interval is calculated as follows:

RTDCIMPAMT q, p	=	(-1) * RTSPP p * (RTDCIMP q, p * ¼)

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| RTDCIMPAMT q, p | $ | Real-Time DC Import Amount per QSE per Settlement Point—The payment to QSE q for DC Tie import through DC Tie p, for the 15-minute Settlement Interval. |
| RTSPP p | $/MWh | Real-Time Settlement Point Price per Settlement Point—The Real-Time Settlement Point Price at Settlement Point p, for the 15-minute Settlement Interval. |
| RTDCIMP q, p | MW | Real-Time DC Import per QSE per Settlement Point—The aggregated DC Tie Schedule submitted by QSE q as an importer into the ERCOT System through DC Tie p, for the 15-minute Settlement Interval. |
| Q | None | A QSE. |
| P | None | A DC Tie Settlement Point. |

(2)	ERCOT shall pay each QSE for energy imported into the ERCOT System during emergency conditions through each DC Tie in response to an ERCOT Dispatch Instruction.    The payment for a given 15-minute Settlement Interval is calculated as follows:

RTEDCIMPAMT q, p	=	(-1) * Max {RTSPP p, (FIP * 18 or VCOSTEMGENERGYq)}* (RTEDCIMP q, p * ¼)

Note: TPTF should select either the 18 HR or the verifiable cost option

The above variables are defined as follows:

| Variable | Unit | Description |
| --- | --- | --- |
| RTEDCIMPAMT q, p | $ | Real-Time Emergency DC Import Amount per QSE per Settlement Point—The payment to QSE q for emergency DC Tie import through DC Tie p, for the 15-minute Settlement Interval. |
| RTSPP p | $/MWh | Real-Time Settlement Point Price per Settlement Point—The Real-Time Settlement Point Price at Settlement Point p, for the 15-minute Settlement Interval. |
| FIP | $/MMBtu | Fuel Index Price – As defined in Section 2, Definitions and Acronyms. |
| RTEDCIMP q, p | MW | Real-Time emergency DC Import per QSE per Settlement Point—The aggregated DC Tie Schedule for emergency energy imported by QSE q into the ERCOT System during emergency conditions through DC Tie p, for the 15-minute Settlement Interval. |
| VCOSTEMGENERGYq | $/MWh | Verified Cost for Emergency Energy — The ERCOT verified cost plus 10% for the energy imported by QSE q into the ERCOT System during emergency conditions through a DC Tie p as instructed by an ERCOT dispatch instruction. |
| Q | None | A QSE. |
| P | None | A DC Tie Settlement Point. |

(3)	The total of the payments to each QSE for all energy imported into the ERCOT System through DC Ties for the 15-minute Settlement Interval is calculated as follows:

RTDCIMPAMTQSETOT q	=	(RTDCIMPAMT q, p + RTEDCIMPAMT q, p)

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| RTDCIMPAMTQSETOT q | $ | Real-Time DC Import Amount QSE Total per QSE(The total of the payments to QSE q for energy imported into the ERCOT System through DC Ties for the 15-minute Settlement Interval. |
| RTDCIMPAMT q, p | $ | Real-Time DC Import Amount per QSE per Settlement Point—The payment to QSE q for DC Tie import through DC Tie p, for the 15-minute Settlement Interval. |
| RTEDCIMPAMT q, p | $ | Real-Time Emergency DC Import Amount per QSE per Settlement Point—The payment to QSE q for emergency DC Tie import through DC Tie p, for the 15-minute Settlement Interval. |
| Q | none | A QSE. |
| P | none | A DC Tie Settlement Point. |

6.6.3.5	Real-Time Payment for a Block Load Transfer Point

(1)	The payment for the energy delivered to an ERCOT Load through a BLT Point is made to the QSE for that BLT Point for each 15-minute Settlement Interval, based on the Real-Time Settlement Point Price for the Load Zone Settlement Point where the ERCOT Load normally locates. The payment for a given 15-minute Settlement Interval is calculated as follows:

BLTRAMT q, bltp, p	=	(-1) * RTSPP p * BLTR q, bltp , p

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| BLTRAMT q, bltp , p | $ | Block Load Transfer Resource Amount per QSE per Settlement Point per BLT Point—The payment to QSE q for the BLT Resource that delivers energy to Load Zone p through BLT Point bltp, for the 15-minute Settlement Interval. |
| RTSPP p | $/MWh | Real-Time Settlement Point Price per Settlement Point—The Real-Time Settlement Point Price at Settlement Point p, for the 15-minute Settlement Interval. |
| BLTR q, p, bltp | MWh | Block Load Transfer Resource per QSE per Settlement Point per BLT Point—The energy delivered to an ERCOT Load in Load Zone p through BLT Point bltp represented by QSE q, for the 15-minute Settlement Interval. |
| Q | None | A QSE. |
| P | None | A Load Zone Settlement Point. |
| Bltp | None | A BLT Point. |

(2)	ERCOT shall pay each QSE for the energy delivered to an ERCOT Load through a BLT Point that is moved, in response to an ERCOT Dispatch Instruction during Emergency Conditions, from the ERCOT Control Area to a Non-ERCOT Control Area.  The payment for a given 15-minute Settlement Interval is calculated as follows:

BLETRAMTq, BLT  p = (-1) * MAX {RTSPPp ,  (FIP * 18 or VCOSTEMGENERGYq)} * BLTR q,BLT p

Note: TPTF should select either the 18 HR or the verifiable cost option

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| BLETRAMT q, bltp , p | $ | Block Load Emergency Transfer Resource Amount per QSE per Settlement Point per BLT Point—The payment to QSE q for the BLT Resource that delivers energy to Load Zone p through BLT Point bltp, for the 15-minute Settlement Interval. |
| RTSPP p | $/MWh | Real-Time Settlement Point Price per Settlement Point—The Real-Time Settlement Point Price at Settlement Point p, for the 15-minute Settlement Interval. |
| VCOSTEMGENERGYq | $/MWh | Verified Cost for Emergency Energy — The ERCOT verified cost plus 10% for the energy delivered to an ERCOT Load through BLT Point BLTp during emergency conditions in ERCOT as determined by an ERCOT Dispatch Instruction. |
| BLTR q, p, bltp | MWh | Block Load Transfer Resource per QSE per Settlement Point per BLT Point—The energy delivered to an ERCOT Load in Load Zone p through BLT Point bltp represented by QSE q, for the 15-minute Settlement Interval. |
| q | None | A QSE. |
| p | None | A Load Zone Settlement Point. |
| BLT p | None | A BLT Point. |

(3)	The total of the payments to each QSE for all energy delivered to ERCOT Loads through BLT Points for the 15-minute Settlement Interval is calculated as follows:

BLTRAMTQSETOT q	=	(BLTRAMT q, blt,p,  p +  BLETRAMT q, blt,p,  p)

The above variables are defined as follows:

| Variable | Unit | Definition |
| --- | --- | --- |
| BLTRAMTQSETOT q | $ | Block Load Transfer Resource Amount QSE Total per QSE(The total of the payments to QSE q for energy delivered into the ERCOT System through BLT Points for the 15-minute Settlement Interval. |
| BLTRAMT q, bltp , p | $ | Block Load Transfer Resource Amount per QSE per Settlement Point per BLT Point—The payment to QSE q for the BLT Resource at BLT Point bltp, which delivers energy to Load Zone p, for the 15-minute Settlement Interval. |
| BLETRAMT q, bltp , p | $ | Block Load Emergency Transfer Resource Amount per QSE per Settlement Point per BLT Point—The payment to QSE q for the BLT Resource that delivers energy to Load Zone p through BLT Point bltp, for the 15-minute Settlement Interval. |
| q | none | A QSE. |
| p | none | A Load Zone Settlement Point. |
| BLT p | none | A BLT Point. |