## Slide 1: Quantifying Demand Reduction for Load Control Measures
Kyle Hemmi
Frontier Associates LLC
February 2008

## Slide 2: Proposed Bridge Solution Programs
Program 1: Res, Single Family, AC, 33% cycling
Program 2: Res, Multifamily, AC, 33% cycling
Program 3: Res, Single Family, Pool Pump, 100% cycling
Program 4: Res, Single Family, Electric Water Heater, 100% cycling
Program 5: Commercial, Removed

## Slide 3: Demand Reduction: Program 1
Program 1: Res, Single Family, AC, 33% cycling
Utility | kW Savings 1
Austin Energy | 1.0
HL&P 2 | 1.32
ESPRE Simulation PSCO (Xcel Colorado) 3 | 1.0
ESPRE Load Control Simulation, Texas 4 | 1.0
1 All kW savings numbers presented for proposed programs account for diversity and assume control during summer system peak periods (Avg. of Hours ending 16 through 19).
2 +/- 0.14 kW; Based upon 50% cycling strategy
3 EPRI Simplified Energy Analysis for Residential Buildings (ESPRE) modeling calibrated to PSCO Metering data and Building Characteristics
4 Calibrated to Texas Metering data and Building Characteristics

## Slide 4: AC Load Curve: Peak Day PSCO (Xcel Energy)

## Slide 5: Demand Reduction: Program 2
Program 2: Res, Multifamily, AC, 33% cycling
Utility | kW Savings
ESPRE Load Control Simulation, Texas 5 | 0.65
5 Calibrated to Texas Metering data and Building Characteristics

## Slide 6: Demand Reduction: Program 3
Program 3: Res, Single Family, Pool Pump, 100% cycling
Utility | kW Savings*
2001 PG&E Pool Pump Program Evaluation by ADM | 0.33

## Slide 7: Pool Pump Load Curve: 2001 PG&E Study
1.718 is the average kW of pool pumps in PG&E service territory: Adjusted for Diversity

## Slide 8: Demand Reduction: Program 4
Program 4: Res, Single Family, Electric Water Heater, 100% cycling
Utility | kW Savings*
ESPRE Load Control Simulation, Texas 6 | 0.35
6 Calibrated to Texas Metering data and Building Characteristics

## Slide 9: Water Heater Curves by Month

## Slide 10: Summary of Deemed Savings
 | Deemed Savings
Program 1: Res, Single Family, AC, 33% cycling | 1.0
Program 2: Res, Multifamily, AC, 33% cycling | 0.65
Program 3: Res, Single Family, Pool Pump, 100% cycling | 0.33
Program 4: Res, Single Family, Electric Water Heater, 100% cycling | 0.35