## Slide 1: Resource Node Locations 02-20-08 WMS Meeting (version 02-20-08 11:11)

## Slide 2: How we got here……..
WMS Hi-Lo Subgroup established at 01-16-08 WMS meeting.
Subgroup met in Taylor on 01-28-08
Subgroup met in Austin on 02-15-08

## Slide 3: Agenda
Overview of the Revised Approach [Most Resource Nodes to be located “north” of the high side of the GST (as recommended by WMS).]
  Typical Configuration Description and Examples
  CCP Description and Examples
  PUN Description and Examples
Is a Protocol Revision Required?
Timeline for final review, release and use of updated Resource Node Names and Locations
Questions

## Slide 4: High Level Description of Locating the Resource Nodes #1
Use the “Principles” to place the Resource Nodes in the model for each unit. In many cases this is “north” of the high side of the GST and is the same electrical bus with the EPS meter. Approach follows WMS recommendation.
Also……. Connectivity Nodes for all units are in the model. These nodes indicate where the unit is physically connected to the system (low side of GST). This info is passed to EMS and MMS.
More than one unit can be mapped to a Resource Node. A unit cannot be mapped to more than one Resource Node.
See examples. (In many cases, there is a reduction in the number of Resource Nodes as compared to previous approach.) Need naming convention.

## Slide 5: Typical

## Slide 6: Typical Complex
SCED & 3PO
Mw Telm
HSL
LSL
AS etc
Resource Status
SCED & 3PO
Mw Telm
HSL
LSL
AS etc.
Resource Status
DAM
EOO
CRR
Bids

## Slide 7: High Level Description of Locating the Resource Nodes #2 CCP’s
For CCP’s use CCP Logical Resource Node approach. (approximately 56 Trains). This CCP Logical Resource Node is (essentially) the Resource Node for the train.
CCP Resource specific offers (3PO and AS) can be submitted at CCP Logical Resource Nodes
Also … CCU Resource Nodes are identified by the “Principles” for each unit. Most of these CCU Resource Nodes will be “north” of the GST of CCU.
In DAM, Resource Specific offers at the CCP Logical Resource Node will disaggregate to the units based on the max capacity of the units in selected configuration.
Settlement Point specific offers and bids, i.e. CRR bids/offers, DAM energy only offers and DAM energy bids can be submitted to the CCU Resource Nodes only.
See examples.

## Slide 8: Combined Cycle Plant Slide 1
SCED & 3PO
Mw Telm
HSL
LSL
AS etc.
Resource Status
DAM
EOO
CRR
Bids
SCADA Gross
Line
1
Line
5
Line
4
Line
3
Line
2
EPS
G
1
G
3
G
2
CCP Logical Resource
Node

## Slide 9: Combined Cycle Plant Slide 2
SCED & 3PO
Mw Telm
HSL
LSL
AS etc.
Resource Status
DAM
EOO
CRR
Bids
SCADA Gross
Line
1
Line
4
Line
3
Line
2
CCP Logical Resource
Node
EPS
EPS
G
1
G
2
G
3

## Slide 10: High Level Description of Locating the Resource Nodes #3 PUN’s
Use the “Principles” to place the Resource Nodes in the model for each unit. In most cases this is “north” of the high side of the GST. It is usually within the PUN and also NOT where the EPS meter is located.
Also …… place a “PUN” Resource Node (with no units mapped to it) at the ERCOT interconnection point (usually where the EPS meter is located). This “PUN” Resource Node is where DAM Energy Only Offers and CRR bids can be made.
Constraints within the Private Use Network are not enforced (only monitored).
See examples.

## Slide 11: PUN

## Slide 12: PUN Complicated

## Slide 13: PUN Very Complicated
Interconnection with ERCOT
E
P
S
E
P
S
Line
2
Line
1
load
Logical Resource
Node
Logical Resource
Node
PUN RN
PUN RN
G
1
G
2
G
3
G
4
G
5
G
6
G
7

## Slide 14
Activities  Settlement Point  | 3PO | AS Offer | DAM Energy Only | DAM Energy Bid | CRR Offers and Bids | Bilateral Trades
Generation RN |  |  |  |  |  | 
CCP RN |  |  |  |  |  | 
CCU RN |  |  |  |  |  | 
PUN RN |  |  |  |  |  | 

## Slide 15: Current Definition of Resource Node
Resource Node (Current Definition)
The Electrical Bus defined in the Network Operations Model at which a Resource's measured output is settled.
For a Generation Resource that is connected to the ERCOT Transmission Grid only by one or more radial transmission lines that all originate at the Generation Resource and terminate in a single substation switchyard, the Resource Node is an Electrical Bus in that substation.
For all other Generation Resources, the Resource Node is the Generation Resource's side of the Electrical Bus at which the Generation Resource is connected to the ERCOT Transmission Grid.

## Slide 16: Terms
First Fork Rule
Resource Node
CCP Logical Resource Node
CCU Resource Node
PUN Resource Node (PUN RN)

## Slide 17: Timeline
Send out spreadsheet with new Resource Node names and locations based on revised approach.
When do we release new names and start using them in EDS 4?

## Slide 18: Questions
Questions ?