## Slide 1: DAM Self-Commitment Issues & Solutions
Shams Siddiqi, Ph.D.
shams@crescentpower.net
(512) 263-0653
February 20, 2008
Notes: <number>

## Slide 2: Background
Current implementation does not allow Self-Committed Resources (SCRs) to offer Ancillary Services and co-optimize energy and AS offers from available capacity thus violating Protocols 4.4.7.2.1:
  (d) An Ancillary Service Offer linked to a Three-Part Supply Offer from a Resource designated to be Off-Line for the offer period in its COP may only be struck if the Three-Part Supply Offer is struck. The total capacity struck must be within limits as defined in item (4)(c)(iii) of Section 4.5.1, DAM Clearing Process.
  (e) An Ancillary Service Offer linked to other Ancillary Service offers or an Energy Offer Curve from a Resource designated to be On-Line for the offer period in its COP may only be struck if the total capacity struck is within limits as defined in item (4)(c)(iii) of Section 4.5.1.
February 20, 2008
<number>

## Slide 3: Background
TPTF guidance on payment of startup cost when a Three-Part Offer (TPO) is awarded in DAM was to pay the resource its startup cost regardless of what it has in its COP (i.e. ignore the COP for startup payment).
  That discussion probably led to the following statement in the Req. doc:“The DAM shall not assume any self-commitment due to COP”
Vendor extrapolation and assumptions (many of which are not documented in the Req. doc) from this statement created the problem – e.g.:
  Assuming 0 startup and min-energy offers for EOC-only offers
  Defining “DAM Commitment” as any award in DAM such that if AS-only offer is awarded, no EOC can be submitted
  Enforcing temporal constraints on AS-only and EOC-only offers
February 20, 2008
<number>

## Slide 4: Background
The other problem is not a SCR issue, but rather corrects co-optimization for all Resource offers –
linked (or “Inclusive”) AS and Energy offers may be struck in a way that does not account for the opportunity cost
February 20, 2008
<number>

## Slide 5: Principles
February 20, 2008
<number>
Implementation must comply with Protocols so that:
Self-Committed Resources have the same flexibility as today to offer and be awarded AS for any hour of its choosing.
Self-Committed Resources are able to take advantage of DAM co-optimization of their AS offers and Energy offers from capacity beyond that required to meet own obligations.
All Resources have certainty that their linked (or “Inclusive”) AS and Energy offers are struck in a way that maximizes their revenues (i.e. opportunity cost is considered whenever DAM awards AS and/or Energy).
Notes: <number>

## Slide 6: Solution Pieces to Correct Mistake
February 20, 2008
<number>
1. Ignore temporal constraints for Generation Resources with Online AS offers only for some or all hours of the DAM (i.e. no Three-Part Offer or Offline AS is submitted for the day). Such Resources will be allowed to enter an EOC in the adjustment period (no EOC was submitted in the DAM anyway) with a new reason code “DAM Self-Committed”.
  This allows SCRs to offer AS in DAM
2. Correct the co-optimization of “Inclusive” AS and Three-Part Offer to limit AS and/or energy award to the maximum quantity of the Energy Offer Curve.
  This is not an SCR issue but rather corrects co-optimization for all Resource offers.
Notes: <number>

## Slide 7: Solution Pieces to Correct Mistake
February 20, 2008
<number>
3. Ignore temporal constraints for Generation Resources with EOC-only and/or Online AS offers only for some or all hours of the DAM (i.e. no Three-Part Offer or Offline AS is submitted for the day). Such Resources will be allowed to enter an EOC in the adjustment period with the reason code “DAM Self-Committed”.
  This allows SCRs to take advantage of co-optimization in DAM as long as they are self-committed for the entire day.
4. Full implementation of co-optimization for all Resources including those that may be self-committed for only part of the day.
Notes: <number>

## Slide 8: Action Needed for Solution
February 20, 2008
<number>
May be possible to implement the relatively minor changes in items 1 and 2 (and possibly 3 – the group didn’t have enough time to redline the Req. doc for 3) prior to the 168-hour test.
Attached redline DAM Requirements document implements items 1 (highlighted) and 2.
Items 1, 2 and 3 likely impact only the DAM engine and have no impact on other systems (e.g. Settlements).
Your urgent action: instruct ERCOT to immediately start working on the issue (i.e. move it up on the priority list) so that these features are available preferably at market open so that implementation is in compliance with the Protocols.
Notes: <number>