## Slide 1: Calculation of Net Energy for Load COPS

## Slide 2: Outline
Definition of Net Energy for Load
How Net Energy for Load is calculated in ERCOT

## Slide 3: Net Energy for Load - Definition
Net Energy for Load (NEL)
  Net generation of an electric system plus energy received from other balancing authority areas less energy delivered to other balancing authority areas through an interchange
Net Generation
Plus Energy Received
Less Energy Delivered
ERCOT

## Slide 4: ERCOT Energy Received
Imports into ERCOT
  Imports to ERCOT are via DC Tie Imports and Block Load Transfer Imports.
Plus Imports
ERCOT

## Slide 5: Net Generation
Net Generation
  The sum of all ERCOT internal generation
Net Generation
ERCOT

## Slide 6: Adjusted Metered Load (AML)
Adjusted Metered Load (AML)
  In ERCOT, the net generation value plus imports is the same as the ERCOT total load value since load is required to match generation for each settlement interval.
  AML is load that has been adjusted for distribution losses, transmission losses and UFE. Summing all AML values for a given time period represents the total ERCOT load (also represents the total ERCOT net generation plus imports).
  Can use AML values to represent ERCOT’s net generation plus imports

## Slide 7: Adjusted Metered Load (AML)
Adjusted Metered Load (AML)
Equivalent to Net Generation plus imports into ERCOT
Net Generation +
Imports = AML
ERCOT

## Slide 8: ERCOT Energy Delivered
Exports from ERCOT
  Exports from ERCOT are via DC Tie Exports and Block Load Transfer Exports. These exports are treated as load.
  Exports from ERCOT (energy delivered to other balancing areas through an interchange) result in the creation of AML bill determinants/data cuts.

## Slide 9: ERCOT Energy Delivered
Exports from ERCOT
  The AML bill determinants for DC Tie exports are not associated to LSE’s but are directly associated to QSE’s. These AML bill determinants/data cuts are excluded from the calculation.
  The AML bill determinants for BLT exports are associated to LSE’s but these determinants/data cuts are excluded from the calculation.
AML
ERCOT
Less Exports

## Slide 10: Net Energy for Load
NEL calculation for ERCOT is performed by
  Summing all AML data cuts with the exception of:
    AML data cuts that are created as a result of DC Tie Exports or Block Load Transfer Exports

## Slide 11: Net Energy for Load
NEL calculation for ERCOT is performed by
AML
(Net Generation
plus imports)
Plus
DC Tie, Block Load Transfer Imports
Less
DC Tie, Block Load Transfer Exports
ERCOT

## Slide 12: Load Ratio Shares
Load Ratio Shares are calculated by
i
∑ LREPUFE_<REP>_<QSE>
________________________
i
∑ LTOTERCOT_4CP
  Where i = 15-minute settlement interval for the previous calendar year (most recent settlement run for each Operating Day)
  Calculation can be performed for REPs and QSEs

## Slide 13: Questions?
ON
OFF