## Slide 1: Congestion Management Work Group Update
Presented to WMS 3-19-08
Marguerite Wagner, Reliant Energy Inc.

## Slide 2: 2008 Activities
Competitiveness Constraint Test Support
Nodal Shadow Price Cap Development
CSCs for 2009

## Slide 3: Constraint Competitiveness Test (CCT)
Used to determine mitigation in RT SCED
All energy offers in SCED are subject to Offer Caps and Floors in PUCT Rule 25.505 and the Protocols
SCED Texas Two Step uses Energy Offers to dispatch energy to serve load and solve congestion
  Energy Offers used to solve congestion on competitive constraints are not mitigated through SCED
  Energy Offers used to solve congestion on non-competitive constraints are mitigated under Protocols 4.4.9.4.1
Notes: 25.505 (g) (6) The system-wide offer caps shall be as follows:
(A) The low system offer cap (LCAP) shall be set on a daily basis at the higher of:
(i) $500 per MWh and $500 per MW per hour; or
50 times the daily Houston Ship Channel gas price index of the previous business day, expressed in dollars per MWh and dollars per MW per hour.
(C) Beginning March 1, 2008, the HCAP shall be $2,250 per MWh and $2,250 per MW per hour.
(D) Beginning two months after the opening of the nodal market, the HCAP shall be $3,000 per MWh and $3,000 per MW per hour.

## Slide 4: Identification of Competitive Constraints
Section 3.19 of the Nodal Protocols describes process
Test evaluates capacity availability and concentration of control
  Constraint is competitive if there are sufficient Generation Resource MW to resolve constraint, controlled by a sufficient number of different QSEs

## Slide 5: CMWG will work with ERCOT to:
Understand process used to set up base case for CCT annual evaluation
Ensure that QSE - Resource mappings are up to date so that the Resource ‘control’ can be identified
Develop list of potential Competitive Constraints
Timeline Now-Summer

## Slide 6: Backstop for CCT
Backstop: CSCs are deemed to be competitive 3.19(1) need to determine CSCs for 2009
Timeline: late Summer 2008
Timing may require PRRs to amend timeline for CSC determination
Zonal Protocols (Section 7.2) require:
  ERCOT analysis complete: 8/1
  CSCs & CREs determined by 11/1 (means Oct TAC & BOD)
Likely will not have analysis done by 8/1, targeting 9/1 with CMWG consideration early Sept and Sept WMS

## Slide 7: Nodal Shadow Price Cap
Protocols 6.5.7.1.11 require ERCOT to “establish a maximum Shadow Price for each constraint…”
Each contingency used in SCED must have a max SP cap
CMWG will develop proposals for how to establish SP cap and bring to WMS for consideration and recommendation to TAC
Target completion of draft by start of 168 hr test
TAC approval by Oct  Sept WMS consideration