## Slide 1: TPTF Verifiable Cost Sub-group Summary
Final Report
3/xx/2008
Jim Galvin- TPTF VC Sub-group Chair

## Slide 2: Process
The VC Sub-group drafted a set of 9-principles to guide the discussions
Some principles identified multiple issues for which the group discussed resolving
Only issues that received consensus are brought forth from the group to identify as resolved
The group will report on items that did not receive consensus
Today’s report summarizes the group’s findings

## Slide 3: Start-up and Minimum Energy- (Principle 1)
Verifiable Start-up and Min Energy
  Capturing Costs from Breaker Close to LSL (resolved)
  Including Shut-down Costs in Start-up (resolved)
  Recovering Start Costs when RUC is cancelled (by ERCOT) and Cost recovery during SPS
    Rare occurrences will be noted in Protocols and cost recovery through dispute process
  Use of Auxiliary Equipment for Start-up (resolved)

## Slide 4: Incremental Heat Rate- (Principle 2)
Verifiable Incremental Heat Rate
  Creating monotonically non-decreasing Incremental Heat Rate Curve (resolved)
  Actual System design will change a decreasing curve in MMS, setting a segment of the curve that is less than the previous segment, equal to that previous segment
  For verification of the Incremental Heat Rate, the submitting entity may utilize data from a Heat Rate Test, or Historical Data

## Slide 5: Variable O&M (Principle 3)
Verifiable O&M Costs
  10-year requirement for data/evidence of costs
    For submitting entities who do not have 10-years worth of data, they may submit all the history they have
  Escalation rate will utilize the Handy-Whitman Index
  The Manual will reference types of Verifiable O&M; however, submitting entities will have the ability to submit O&M costs based on their formats and data sources (extremely difficult to create a O&M standard across the market)
  The VC Sub-group agrees with ERCOT in having a stakeholder group track O&M types and/or issues over the course of the Nodal Market

## Slide 6: Risk by Resource Owners- (Principle 4)
Actual Principle that was defined:
  “There is a level of risk that Resource owners take in the recovery of Start-up and Minimum Energy costs”
Some discussions centered around that there will be days when a Generator recovers costs and days when they may not
Some market participants requested that this Principle is not appropriate and is contrary to Principle 5
No systematic or procedural issues were brought up under this Principle

## Slide 7: Make Generators Whole at Min Cost to Load (Principle 5)
The Over-riding theme throughout all discussions
No issues were presented under this Principle

## Slide 8: Use of FIP and FOP (Principle 6)
Index pricing for fuel using Fuel Index Price and Fuel Oil Price was agreed upon by the group
Discussions around fuel costs during exceptional events, such as:
  Imbalance Fees
  Swing Costs
  Spot Gas (gas purchased at close of Day Ahead that diverges significantly from Index)
The VC Group agrees that cost recover mechanism will be needed for “Exceptional Events” that significantly harm a resource entity
Exceptional Events will also have to be defined

## Slide 9: Emissions Costs- (Principle 7)
Submitting entities may submit verifiable incremental emissions costs for Start-up and Minimum Energy
All emissions costs were included in discussions
Open items around emissions
  The applicable rate for emissions costs was discussed as using Index or historical costs to come up with a $/MWh rate
  Some concern expressed about discussing opportunity costs as they are more complex than incremental historical costs

## Slide 10: Prospective and Voluntary- (Principle 8)
The group agreed that the process was prospective and that only anomalous events would be considered under “Exceptional Events” for cost recovery
The current protocols reference a single RUC event as the trigger for a resource entity to be required to submit Verifiable Costs
  The VC group recommends that the trigger of the mandatory submittal for Verifiable Costs be 5 RUC events
  Recommendation relaxes the restriction for resources that are RUC’d infrequently and reduces the administrative burden on those entities and on ERCOT

## Slide 11: Other Issues- CCP’s and SGR’s
Combined Cycle Plants may submit Verifiable Costs by registered configuration
Entities must submit for any configuration that meets the RUC trigger
Split Generation Resources may submit individually or through a Management QSE
  SGR’s may submit by set percentages that may differ from percentage of ownership
  ERCOT may require all owners of SGR’s to submit costs if the assignment of cost to the unit cannot be verified

## Slide 12: Non-consensus Items
Power Purchase Agreements, arguments for and against included, but not limited to:
  Entities represented that PPA’s are a realized cost to the QSE to operate the resource in ERCOT and should be included in the VC Process
  Other Markets do include these elements as a form of Verifiable Costs
  Entities opposed indicated the difficulty in managing and verifying that these are true incremental costs
  Concerns expressed in having PPA’s set up to raise cost levels
No consensus from the Sub-group; however, we have encouraged the supporters of including PPA’s to continue discussions with WMS and/or TPTF

## Slide 13: Next Steps
Decision on Emissions rate using Index or Historical
Definition of “Exceptional Events” and defining a cost recovery process
Work with ERCOT Staff to develop an implementation plan
NPRR’s needed to clarify issues vetted and resolved in the VC Sub-group
Final Report to TPTF and WMS
Any additional “To Do’s” for the VC Sub-group

## Slide 14: Questions