## Slide 1: DRG Slides for PWG Update to COPS

## Slide 2
Highlights from the DGTF Recommendation - 3
Small DRG applies to generation less than 50 kW
  Profiling is applicable provided a readily available profile has been accepted and validated by ERCOT
  No consensus on specific methodology, but
    Excess generation should be profiled in a type-specific manner and
    The load profile should reflect solar output during daylight hours
  Recommended assigning solar profile development to PWG

## Slide 3
TAC Instructions to COPS/PWG
At the January 3,2008 COPS reviewed the DGTF recommendations
  TAC requested that PWG/COPs assess and further develop profiling options for consideration to address small distributed renewable generation
  TAC members indicated that PWG should take into consideration the generation characteristics specific to the renewable technology

## Slide 4
Settlement of Outflow Only
Some possibilities for allocating the PV-generated outflows:
1. Spread the energy evenly over daylight hours
2. Spread the energy evenly over the peak PV generating hours
3. Spread the energy using a PV model
4. Spread the energy using both a PV model and the existing settlement load profile
How can the outflow for residential photovoltaic (PV) arrays as measured at the point of interconnection be settled?

## Slide 5
DGTF Attachment A

## Slide 6
DGTF Attachment B

## Slide 7
DGTF Attachment C

## Slide 8
DGTF Attachment D

## Slide 9
Distributed Renewable Generation (DRG)
TDSPs responded to ERCOT’s request for information on premises that have DRG with a generation capacity < 50 kW.
What is out there?
Five of the ESI IDs included above have PV and wind generation. This means there are currently 87 unique ESI IDs known to have one or more type of DRG (< 50 kW).

## Slide 10
How much energy will a PV array produce?
Given the currently known average Residential PV generation capacity of 3.5 kW (AC), at 100% capacity factor there would be (3.5 * 24 =) 84 kWh generated per day.
If we utilize the Interstate Renewable Energy Council’s irradiance estimate of 20% from its presentation to the DGTF on 12/04/07, the estimated yield would be 16.8 kWh per day.
Applying the above to the average Business PV generation capacity of 8.9 kW (AC) yields an estimated 42.7 kWh per day.
For simplicity, the energy produced by a PV array is presented in most of the slides as a sine wave spanning 9:00 AM to 5:00 PM.

## Slide 11
  Represented using Sine function
  Begin/End Times for PV Generation are day of year & weather zone specific
    1 hour after sunrise
    1 hour before sunset
  Daily kWh Generation for Residential is based on 3.5 kW with a 20% capacity factor
    Average daily PV Generation is 16.8 kWh
    Average daily PV produces output for 10.2 hours (range: 7.9 – 12.4)
    Daily PV Generation is prorated based on hours of generation for the day compared to an average day
      Example day with 8 hours of Generation:
PV Generation Assumptions

## Slide 12
Residential PV Model assumptions
  Standard Profile multiplied by 1.1215 to adjust to average usage level for PV ESIIDs
  Subtract PV Generation from scaled up Profile
    if result in an interval is negative, set to zero
Business PV Model assumptions
  Standard Profile multiplied by 2.7633 to adjust to average usage level for PV ESIIDs
  Subtract PV Generation from scaled up Profile
    if result in an interval is negative, set to zero
Residential and Business Wind/Other Model assumption
  Standard Profile used – the interaction between wind generation and load is unpredictable
DRG - KWh Load Models

## Slide 13
PV Gen PV Profile Standard Profile
Residential HIWR North PV

## Slide 14
Excess generation is the energy flowing into ERCOT from the premise
PRR756 - Credit for excess generation handled as an adjustment to load in settlement process
  PV assumption: Flat line from 11am to 3pm
  Wind/Other assumption: Flat line for entire day
Settlement adjustment is triggered by a DRG Profile ID assignment
Profiling Excess Generation

## Slide 15
Residential PV – Applying the Profile

## Slide 16
Breakdown of Proposed DRG Models
8 Models per Profile Type to represent Weather Zones
BUSIDRRG and RESIDRRG are not generation type specific:
  Profile ID assignment is used to trigger settlement adjustment for excess generation
  KWh Load and kWh Gen are settled with actual interval data

## Slide 17
DRG Profile ID Assignment
TDSPs submit documentation to ERCOT to initiate a change to a DRG Profile ID assignment.
ERCOT validates requests within 5 Business Days and notifies to initiate the 814-20
Information required from TDSP
Affirmation of Interconnection Agreement with customer and effective date
Generation Type, and characteristics
Metering configuration
Inverter information if applicable (DC Generation)

## Slide 18
18.2.1 Guidelines for Development of Load Profiles
In developing Load Profiles, ERCOT shall strive to achieve an optimal combination of the following:
(1) Give no unfair advantage to any Entity;
(2) Maximize usability by minimizing the total number of Load Profiles without compromising accuracy and cost effectiveness;
(3) Minimize the Load Profiles’ contribution to UFE over all Settlement Intervals, paying particular attention to higher cost periods;
(4) Reflect reasonably homogenous groups, with respect to load shape and likely supply costs;
(5) Develop Load Profiles that are distinctly different;
(6) Develop Load Profiles for areas with incomplete load data utilizing data from other sources, taking into account similarities and differences in load;
(8) Use the most accurate load research data available; and
(9) Develop Load Profiles based on readily identifiable parameters that are not subject to frequent change.

## Slide 19
Distributed Renewable Generation Modifications LPGRR030
Pros:
Incorporates kWh load modifications resulting from PV Generation behind the meter
PV and Non-PV DRG Profile ID assignments results in specific settlement cuts, and supports the reporting of load by Profile ID
DRG Profile ID assignments trigger settlement for kWh Gen specific to the DRG type
Allows forecasting systems to track customers by their DRG Profile ID to better forecast the balancing market schedules
Shadow settlement systems perform the same basic evaluation as present
Cons:
Large (128) increase in the number of Profile IDs used in ERCOT and Market Participants settlement and forecast systems

## Slide 20
Alternatives for DRG - LPGRR030
Concerns were raised at the March 26, 2008 PWG meeting about the large number of new Profile IDs being introduced for DRG
Several alternatives were discussed and then narrowed to three options:
LPGRR030 as drafted - 128 new Profile IDs
DRG Profile IDs only for PV - 72 new Profile IDs
RESPV, BUSPV, RESWD, BUSWD, RESIDR, BUSIDR * 8 WZones – 48 new Profile IDs
PWG did not have consensus
on a single option

## Slide 21
DRG Profile IDs only for PV Option 2:
Pros:
72 Profile IDs instead of 128 – eliminated the requirement for Non-PV DRG Profile IDs
DRG Profile ID assignments trigger settlement for kWh Gen specific to PV
Cons:
No settlement cuts for Non-PV ESIIDs with DRG; increases the difficulty to report NonPV DRG metrics
No trigger for settlement for kWh Gen specific to Non-PV (requires an assumption that data in the meter-loop for ESIIDs with standard profiles are for Non-PV DRG)
Increases the difficulty to perform required quarterly and annual validations for Non-PV ESIIDs
Requires continuing manual validation of usage records with meter-loop information to confirm they are correctly associated with DRG ESIIDs and use of MarkeTrak to resolves discrepancies
Increases the difficulty for forecasting systems to track customers by their DRG Profile ID
Does not support Protocols Section 18
PRR756 will need to be amended

## Slide 22
RESPV, BUSPV, RESWD, BUSWD, RESIDR, BUSIDR Option 3:
Pros:
48 Profile IDs instead of 128
DRG Profile ID assignments trigger settlement for kWh Gen specific to DRG type
Settlement cuts with DRG Profile IDs will be created
Cons:
For some PV and Wind ESIIDs the Load shape will be inconsistent with the ESIIDs usage pattern (e.g. RESLOWR settled with RESHIPV)
Increases possibility of gaming (e.g. Adoption of DRG to obtain a more advantageous settlement shape)
Does not support Protocols Section 18
Creates disincentives for some categories of ESIIDs to adopt DRG (e.g. Adoption of DRG would result in a less advantageous settlement shape)