## Slide 1: ERCOT ERCOT 2007 Seminar DC Tie Scheduling Process

## Slide 2
Objectives
Review ERCOT Protocols
Discuss DC Tie Scheduling Requirements
Explain QSE Registration and Setup
Describe the roles and responsibilities of SPP and OATI
Discuss the DC Tie Automation Project
Summarize the DC Tie scheduling process

## Slide 3
ERCOT Protocols - 5.2 North American Electric Reliability Council/ERCOT Tagging Procedures
The QSE will follow all NERC guidelines for tagging of Control Area interchange transactions.
ERCOT will be operated as a single Control Area. Therefore, no internal ERCOT transactions require tagging. Only transactions across ERCOT interconnections to SPP, WSCC, or Mexico, will be tagged by the QSE as prescribed in the NERC tagging guidelines.

## Slide 4
ERCOT Protocols 4.4.18.1 Control Area Operations
Control Area schedules between the ERCOT Control Area and interconnected non-ERCOT Control Area(s), through the use of schedules over Direct Current Tie(s), will be implemented in accordance with these Protocols, North American Electric Reliability Council (NERC) scheduling protocols, and in compliance with NERC operating policies.
Scheduling must also be in accordance with any applicable Federal Energy Regulatory Commission tariffs.

## Slide 5
ERCOT Protocols 4.4.18.1 Control Area Operations
ERCOT will perform schedule confirmation with the applicable interconnected non-ERCOT Control Area(s) and will coordinate the approval process for the NERC tags as both the ERCOT Control Area and on behalf of ERCOT TSPs.

## Slide 6
ERCOT Protocols - 4.4.18.2 Linkage of Schedules with Interconnected Non-ERCOT Control Area Schedules
ERCOT will match the Supply and Obligation schedules submitted by the QSEs with interconnected non-ERCOT Control Area schedules obtained through the NERC Scheduling Process to confirm schedules and perform checkouts with adjacent interconnected non-ERCOT Control Areas.

## Slide 7
ERCOT Protocols - 4.4.18.2 Linkage of Schedules with Interconnected Non-ERCOT Control Area Schedules
If a match does not exist between the interconnected non-ERCOT Control Area schedule and the QSE schedule to or from the DC Tie, then ERCOT will deny the interconnected non-ERCOT Control Area schedule with the applicable interconnected non-ERCOT Control Area(s).

## Slide 8
ERCOT Protocols - 4.4.18.2 Linkage of Schedules with Interconnected Non-ERCOT Control Area Schedules
Any QSE’s Supply or Obligation schedule indicated as being received or delivered to or from a DC Tie that cannot be confirmed or linked by ERCOT, will be declared a mismatch and set to zero as described in Section 4.7.2, Schedule Validation Process.

## Slide 9
ERCOT Protocols 4.4.18.3 Operation of DC Ties
ERCOT will confirm interconnected non-ERCOT Control Area schedule profiles with the DC Tie operator, who will control the tie to the schedules agreed to by both the designated Security Coordinator for the interconnected non-ERCOT Control Area and ERCOT.

## Slide 10
ERCOT Protocols 4.4.18.4 Settlement
A QSE importing into ERCOT through a DC Tie import schedule will include that DC Tie import schedule as a Supply in its Balanced Schedule by using the identifier field indicating the appropriate DC Tie.
Imports into ERCOT via DC Ties will be treated as generation into the Congestion Zone in the settlement system.

## Slide 11
ERCOT Protocols 6.8.1.13 Resource Imbalance
Resource Imbalance ($) for each QSE for each interval for each zone will equal the Resource schedule (MWh) for Resources represented by that QSE minus the actual meter read (MWh) for the Resource multiplied by the Market Clearing Price for Energy ($/MWh).
Resource Imbalance does not exclude DC Ties.
Note: For DC Tie schedules the approved NERC eTag schedule (MWh) is substituted for “the actual meter read (MWh)”.

## Slide 12
ERCOT Protocols 4.4.18.4 Settlement
A QSE exporting from ERCOT through a DC Tie export schedule will include that DC Tie export schedule as an Obligation in its Balanced Schedule by using the identifier field indicating the appropriate DC Tie.
Exports from ERCOT via DC Ties will be treated as a Load connected at transmission voltage in the settlement system and are responsible for allocated Ancillary Services, Transmission Losses, UFE, ERCOT administrative fees, as described in Section 9, Settlement and Billing, and any other applicable ERCOT fees.

## Slide 13
ERCOT Protocols 6.9.5.2 Settlement for Balancing Energy for Load Imbalances
Each QSE’s Load Balancing Energy Obligation quantity for each Settlement Interval, for each Zone, shall be equal to the QSE’s Adjusted Metered Load consumption of all CR Loads represented by the QSE, minus the QSE’s scheduled Load Obligation.
Load Imbalance does include scheduled Exports from a DC Tie.
Note: For DC Tie schedules the approved NERC eTag schedule (MWh) is substituted for “Adjusted Metered Load consumption”.

## Slide 14: ERCOT DC Tie Scheduling

## Slide 15
ERCOT DC Tie Scheduling Requirements
Qualified Scheduling Entities (QSE) have to be qualified with ERCOT to schedule within ERCOT including to/from ERCOT across the North and East DC Ties
ERCOT will follow NERC guidelines for tagging and approval of DC Tie Schedules

## Slide 16
ERCOT DC Tie Scheduling Requirements
ERCOT QSEs must be registered with NERC TSIN to participate in NERC tagging and obtain a Purchasing/Sales Entity (PSE) Name to schedule across the DC Ties to/from Non-ERCOT control areas
Qualified ERCOT QSEs may schedule across the DC Ties after completion of NERC TSIN registration and completion of initial setup at ERCOT

## Slide 17: NERC Transmission Services Information Network (TSIN) Registration
Sign onto NERC web site for TSIN – http://reg.tsin.com/
Select new registration option and follow directions to register company information and select a PSE Name for use in filing for NERC eTags
Registration is for specific NERC scheduling regions and ERCOT must be selected to schedule across the DC Ties

## Slide 18: NERC Transmission Services Information Network (TSIN) Registration
The PSE name selected by the QSE cannot have any resemblance to ERCO or ERCOT in the name
ERCOT must approve the PSE name and complete an initial setup for a QSE before NERC eTags can be filed
A list of QSE and Sub-QSE currently registered with TSIN for DC Tie scheduling is posted on the ERCOT web site at:
  http://www.ercot.com/mktparticipants/docs/QSEs.xls

## Slide 19
ERCOT DC Tie Setup
QSE or Sub-QSE must inform ERCOT Client Rep of intention to schedule across the DC Tie and provide:
  List of QSE and Sub-QSE names
  Duns numbers
  PSE names
ERCOT has to complete an initial setup before an eTag schedule can be filed and approved
  Confirm the QSE is qualified in ERCOT
  Confirm TSIN registration for scheduling to/from the ERCOT Region
  Approve PSE names and add the QSE Names to the drop down list
QSE and Sub-QSE can use the same PSE name for more than one entity

## Slide 20: SPP - DC Tie Scheduling Functions
SPP performs the reservation and scheduling functions for the North and East DC Ties
SPP performs schedule confirmation with the interconnected Non-SPP Control Area(s) and will coordinate the approval process for the NERC tags as both the SPP Control Area and on behalf of SPP TSPs.

## Slide 21: SPP - DC Tie Scheduling Functions
SPP interfaces with the DC Tie operators to implement approved eTag schedules
QSEs (or their counterparties) must be registered with SPP to arrange for DC Tie capacity

## Slide 22: Open Access Technology International Inc. (OATI)
OATI is a registered Scheduling Agent with NERC and provider of software services
Both ERCOT and SPP use OATI software and services for managing DC Tie scheduling and approval functions
QSEs or their counterparties must file for NERC eTag schedules through a NERC registered Scheduling Agent
ERCOT QSEs can either contract with OATI to file eTag schedules or with other NERC registered Scheduling Agents that have established interfaces with OATI such as the Minneapolis Consulting Group
For a complete list of registered Scheduling Agents, go to http://reg.tsin.com/Tagging/e-tag/vendorlist.htm

## Slide 23
DC Tie ERCOT Daily Scheduling
QSE DC Tie market schedules are filed in the Day Ahead Market and during the Adjustment Period up until one hour prior to the hour that energy flows
QSE (or their counterparties) must also file and obtain approval of NERC eTag schedules in amounts equal to or less than the ERCOT DC Tie market schedules for power to flow

## Slide 24
DC Tie ERCOT Daily Scheduling
Approved eTags at the time of real time operating period will be equivalent to measured meter flow for settlement purposes
Difference between eTag Schedules and actual metered flow will be treated as inadvertent energy and settled between ERCOT, the adjacent control area and DC Tie operator

## Slide 25
DC Tie SPP Daily Scheduling
QSE (or their counterparties) must arrange for DC Tie capacity with SPP in the day ahead and the hour ahead market according to SPP business rules
QSE (or their counterparties) must file for NERC eTag schedules across the DC Ties with a NERC registered Scheduling Agent not less than 20 minutes prior to the hour that energy flows
eTag schedules must be approved by ERCOT, by SPP Control Area, and by others along the schedule path by 20 minutes prior to the hour that energy flows
DC Tie schedules can be curtailed due to constraints according to a set of SPP business rules

## Slide 26: ERCOT DC Tie Automation Project
Automated Services from OATI
Improvements in ERCOT
Internal Processes

## Slide 27: ERCOT DC Tie Automation Project with OATI - Objectives
Automate Comparison of eTags to QSE DC Tie Schedules
Eliminate Operator offsets for DC Tie eTag/Schedule mismatches
Monitor/compare eTag Net Scheduled Interchange to real time DC Tie SCADA
Automate Inadvertent Energy Accounting

## Slide 28: Automate Comparison of eTags to QSE DC Tie Schedules
Add a QSE drop down list in the ERCOT Market Info field on the eTag application to identify ERCOT QSEs
Upload ERCOT DC Tie schedules to OATI
Develop new OATI displays to sort and compare eTags to QSE DC Tie market schedules

## Slide 29: Automate Comparison of eTags to QSE DC Tie Schedules
Download eTag schedule data from OATI to MDB and Settlements
Provide internal ERCOT eTag/QSE Schedule reporting capability
Eliminated manual spreadsheets and many hours of record keeping

## Slide 30: Eliminate Operator offsets for DC Tie eTag/Schedule mismatches
Substitute eTag Schedules for QSE DC Tie Schedules in the operating period real time applications
Automatically provides correct DC Tie flow for congestion analysis and balancing
Manual operator offset for DC Tie mismatches no longer necessary

## Slide 31: Monitor/Compare eTag Net Scheduled Interchange to Real Time DC Tie SCADA
Sum of eTags for DC Tie equals Net Scheduled Interchange (NSI)
NSI downloaded from OATI and linked to a display next to DC Tie SCADA value
Alarm for Differences
Errors identified quickly

## Slide 32: Automate Inadvertent Energy Accounting
Perform Inadvertent Energy Accounting on OATI application
Eliminate internal manual spreadsheets
Upload EPS meter data for DC Ties for final meter reading corrections
Enhanced OATI reporting capabilities

## Slide 34: DC Tie Scheduling
What has changed?

## Slide 35: ERCOT
Protocols
  No Changes
Procedures
  Same approval criteria for mismatches between ERCOT market schedules and NERC eTags
  NEW - Formal setup process in OATI software to enable QSE/Sub-QSE ability to schedule

## Slide 36: NERC eTags
Initial Setup of - QSE / OATI User Interface
  Select Options from main menu buttons
  Select Tagging Options
  Check “Enable Display of ERCOT Market Information”
  Then click Apply

## Slide 38: NERC eTags
One NEW step on NERC eTag New Tag Form
  Select ERCOT QSE from list provided in ERCOT Market Info Field
  Must be the same QSE/Sub-QSE that submitted the ERCOT market schedule
  QSE Name is used to match eTag schedules to Market schedules and link eTag schedule to QSE for settlement

## Slide 39
PSE Name
Source
ERCOT QSE, PSE Name
Sink

## Slide 40
Schedule will be denied
if QSE not selected
Select Back

## Slide 41
East4 Denied
North3 Denied
North4 Okay after North3 Denied

## Slide 42
East4 Denied
North3 Denied
North4 Okay after North3 Denied

## Slide 43
QSE DC Tie Schedule Requirement Summary
QSE must be registered with NERC TSIN and setup with ERCOT for DC Ties
QSE (or counterparty) must be registered with SPP for capacity reservations
QSE (or counterparty) Arrangement with OATI or another NERC registered Scheduling Agent to file eTag schedules

## Slide 45
Steps in DC Tie Schedules - Summary (Not necessarily in Order)
QSE files DC Tie schedule in ERCOT market
QSE arranges for DC Tie capacity with SPP
QSE files for eTag schedule with OATI or another NERC registered Scheduling Agent
ERCOT, SPP, and others in path approve eTag Schedule

## Slide 47
DC Tie eTag Scheduling Rules Summary
The ERCOT QSE’s PSE Name must appear as the source or sink for the ERCOT control area within the eTag schedule application (Existing)
The QSE that submitted the ERCOT market schedule must be selected from the ERCOT Market Info drop down list within the eTag schedule application (New)
An eTag schedule will be denied if it exceeds the market schedule or does not show the same ERCOT QSE name in the eTag ERCOT Market Info field

## Slide 48: ERCOT DC Tie Scheduling Process
Questions?