## Slide 1
Texas Nodal: What TOs and QSEs will be doing different
The Structure Group
2/5/2007

## Slide 2
Introduction
This segment is intended to provide market participants with a better understanding of what they will be doing under a Nodal market paradigm…

## Slide 3
Objectives
At the completion of this course of instruction you will:
Understand how ERCOT’s design evolved
Be familiar with key Nodal concepts
Have knowledge of impacts to operations

## Slide 4
Agenda
Nodal Evolution
Fundamental Changes
Key Concepts
Impact to Operations
Summary

## Slide 5
1. Nodal Evolution
The Zonal Design
Reasons for Change
The Road to Nodal
Issues Along the Way

## Slide 6
1.1 The Zonal Design
The following attributes are often used to describe the current zonal market…
Portfolio Market
Model
Zonal boundaries change annually
Allows Qualified Scheduling Entities (QSEs) to optimize their fleet
ERCOT has the ability to deploy resource specific
Retail Choice
Ability to choose your retail provider
Operating under price to beat construct (ends in 1/1/2007)
Centralized data aggregation
Ancillary Service
Markets
Capacity products are bought primarily in Day Ahead (DA)
ERCOT-wide, hourly & have separate clearing prices per product
Replacement capacity is primarily Day Ahead
Balanced
Bilateral Market
ERCOT only manages the residual energy, less than 5% of the energy
Predominant product is sellers choice
Relaxed balanced schedules was implemented Nov 1, 2002

## Slide 7
1.2 Reasons for Change
Portfolio-level Bidding, Scheduling, & Dispatch
Insufficient Price Transparency
No Direct Assignment of Local Congestion
Local congestion is congestion that cannot be resolved with balancing energy
ERCOT uses Out-of-Merit replacement Capacity (OOMC) and Replacement Reserves (RPRS) to solve local congestion
These costs are uplifted to participants on a load-ratio share (LRS) basis
Qualified Scheduling Entities (QSE) submit balanced schedules for a specific zone
ERCOT issues portfolio-level balancing energy dispatch instructions
ERCOT operators have limited tools to resolve congestion
This results in a less efficient dispatch of units
Less efficient power plant dispatch
Less-efficient congestion management
Muted or distorted signals for transmission & generation siting

## Slide 8
1.3 The Road to Nodal
Jul-31-2001
Single Control Area Operations in ERCOT
Jan-1-2002
Retail Market in Portions of ERCOT
Sep-2002 – Jul-2003
Project #26376
Rulemaking Proceeding on Wholesale
Market Design Issues in ERCOT
Aug-21-2003
Substantive Rule §25.501 issued
Sep-2003 – Mar-2004
Stakeholders develop & file nodal protocols
Dec-2008
Nodal Go-Live Scheduled
Mar 2006
Texas Public Utilities Commission (PUCT) approves nodal protocols

## Slide 9
1.4 Issues Along the Way
484 Protocol Revision Requests (PRRs) by end of December 2003
Over $450 million in local congestion collected since market open
Concerns over stable load zones
Need for transparency and improved dispatch
Desire for direct assignment (cost causation)
Sep-2002 – Jul-2003
Project #26376
Rulemaking Proceeding on Wholesale
Market Design Issues in ERCOT
Aug-21-2003
Substantive Rule §25.501 issued
Sep-2003 – Mar-2004
Stakeholders develop & file nodal protocols

## Slide 10
2. Fundamental Changes
Eleven Key Attributes
Change Matrix
Unique Features
Change Summary

## Slide 11
2.1 Market Framework
Network Model
Bidding &
Scheduling
Forward
Markets
Pricing
Ancillary
Services
Bilateral
Trades
Commitment
Reliability Unit
Commitment
Transmission
Rights
Dual
Settlements
Market
Mitigation

## Slide 12
Attribute
Zonal Model
Nodal Model
Network Model
Zonal
  Out of merit energy (OOME) and out of merit capacity (OOMC) needed for local constraints
Full nodal
  All local constraints enforced
Bidding &
Scheduling
Portfolio Based
  QSE bids portfolio, manages resources in Real-Time (RT)
Resource Based
  Requires selection of resources in Day-Ahead (DA) time frame
Forward
Markets
Bilateral only
  Offers DA certainty for fuel planning
Bilateral + Centralized Day-Ahead Market
  Self-commitment still an option
Pricing
Zonal
  Plus OOME for local deployments
  Local congestion uplifted
Resources
  Nodal Pricing
Load
  Average zonal
2.2 Change Matrix (1)

## Slide 13
Attribute
Zonal Model
Nodal Model
Ancillary
Services (A/S)
A/S Clearing is independent of energy scheduling and congestion redispatch
A/S/Energy co-optimized in DA
  Offers ability for lower cost A/S
  May result in lower clearing prices to sellers
Bilateral
Trades
Trades are only zonal (e.g. South, North, Houston)
  No congestion if traded within zone
Trades at a variety of pricing points
  Generation Node (e.g. Ferguson)
  Hub (e.g. Houston, South)
  Load Zone (e.g. South)
  Congestion risk if not at DE’s generation or Load Zone
Commitment
Self commitment is only option
  Provides full discretion to participants
  Allows stable fuel forecasting
  At risk for cost recovery
ERCOT Centralized to meet Day Ahead Load
  In addition to self-commitment option
  Offers some start-up cost recovery
2.2 Change Matrix (2)

## Slide 14
Transmission
Rights
Auctioned Transmission Congestion Rights (TCRs)
  Flowgate approach – more simplistic selection & valuation
Auctioned Congestion Revenue Rights (CRRs)
  PTP approach - More complex selection, valuation, and bidding
Dual
Settlements
Single Settlement
  No forward energy clearing other than congestion management
  Imbalance energy cleared in Real-Time (RT)
Dual settlement
  Energy and A/S Capacity cleared in DA
  RUC and RT energy deviations from DA settled in RT
Market
Mitigation
Resource Category Generic Costs (RCGC)
  Bid Premiums <= RCGC
Day-Ahead
  No mitigated offer caps or must offer requirements
Real-Time
  Mitigated offer caps and TX 2-Step
Attribute
Zonal Model
Nodal Model
Reliability Unit
Commitment
None other than indirectly Out-of-Merit Capacity (OOMC) and RPRS
Additional commitment/ decommitment based on forecast
  May use generic prices
  Subject to additional restrictions on cost recovery
2.2 Change Matrix (3)

## Slide 15
2.3 Unique Features
Ability to take CRRs to Real-Time
5-minute Granularity of Output Schedules
Non-Componentized Nodal Prices
Separation of COP and Offers
SCED Algorithm does not use STLF
Mitigation using Texas Two-Step

## Slide 16
Zonal Market | Nodal Market
Day-ahead market for A/S capacity No Day-ahead Energy market | Co-optimized DA market for A/S, certain CRRs, and forward energy transactions
Day-Ahead & Hour-Ahead Studies | DA & HA Reliability Unit Commitment
Auctioned Transmission Congestion Rights | Auctioned Congestion Revenue Rights
Portfolio-based Offers by Zone | Resource-specific Offers
Balancing Energy services every 15 minutes Zonal congestion management by portfolio for CSCs Resource specific for local congestion | Dispatch every 5 minutes All deployments and congestion management will be resource-specific Enhanced Load Frequency Control
Zonal market clearing prices for balancing energy for generation and loads | Nodal locational marginal pricing (LMP) for generation Zonal weighted LMP for loads
2.4 Change Summary

## Slide 17
3. Key Concepts
Nodal Pricing
Co-Optimization
Unit Commitment
Simultaneous Feasibility Test (SFT)
Dual Settlements

## Slide 18
3.1 Nodal Pricing
What is it?
A market-based pricing approach
Specialized algorithm is used to generate nodal prices (SCED)
Values energy & congestion at settlement points, including:
  Resource buses (generators)
  Load zones (similar to CZs)
  Trading hubs (liquid trading locations)
  DC Ties
Nodal prices will have two components: energy and congestion
Algorithm maximizes revenues from submitted bids while respecting security limits
  Security limits (aka constraints) include line limits, ramp rates, etc.
What does it mean to me?
New price signals for bilateral market
Possible revenue impacts
Potential for reduced uplift
Sharing of congestion costs
Load settled by zone using ’03 definitions
Infrastructure updates due to data volumes

## Slide 19
3.2 Co-Optimization
Zonal
Nodal
What is it?
The DAM will co-optimize energy , ancillary services, and CRRs to obtain the lowest TOTAL cost solution
Current ERCOT zonal market:
  Operates a sequential market, where A/S are cleared in the DA & Energy is cleared in RT
  Does not evaluate the trade-offs between providing energy vs. A/S
Allows ERCOT to procure ancillary services available at least cost by reserving generation to provide reserves versus energy (or vice versa)
Co-optimization produces the lowest overall power (theoretical) costs for the day, so it is possible that LMPs will not be minimized for every hour
A/S clearing prices include consideration of the opportunity cost of, and lost revenues associated with, providing A/S instead of energy
What does it mean to me?
Participants should be indifferent to providing energy or ancillary services

## Slide 20
3.3 Unit Commitment
Energy Offers
Forecasted Demand
Bid-In Demand
DAM
RUC
50 MW
75 MW
In this example, an additional 25 MW of generation would be RUC’d
What is it?
Ensures sufficient generation is on-line in the right location
Any generator committed by ERCOT are eligible to recover their costs
ERCOT will perform several centralized unit commitments
  DAM commitment, DA RUC, HA RUC
Each process leverages the same algorithm: security constrained unit commitment
  Ensures constraints are not violated: line limits, ramp rates, etc.
Commitment costs are recovered similar to today’s RPRS: 1st uplifted to cap short resources, then to market
What does it mean to me?
Participants can self-commit their units or leave the decision to ERCOT
Financial incentives for allowing ERCOT to commit your units

## Slide 21
3.4 Simultaneous Feasibility Test
What is it?
To ensure revenue adequacy and reliability, ERCOT will run a simultaneous feasibility test
The Simultaneous Feasibility Test (SFT) uses a DC power-flow model
The SFT models the effect of CRR Auction bids and offers on the expected system network topology during the auction term
Not a system reliability test and is not intended to model actual system operating conditions
Run during the determination of the winning bids and offers for the CRR Auction
What does it mean to me?
May determine there are some oversold quantities
If oversold quantities exist, participants CRRs may be derated
Auction /
Network
Model
Auction
Awards &
Allocations
CRR Bids
& Offers
Simultaneous Feasibility Test

## Slide 22
3.5 Dual Settlement
What is it?
ERCOT will operate a dual settlement system for Day-Ahead and Real-Time
Settlement will occur at settlement points, including nodes, load zones, and hubs
New charge types/billing determinants will be created for each of the new markets/functions
Participants will continue to receive settlement statements and invoices
Participants will not receive a separate settlement for CRRs
Resources will be settled on a nodal basis every 15 minutes
Loads will continued to be settled on a zonal basis using load-weighted average of calculated LMP prices within pre-determined zones
What does it mean to me?
Separate settlement for DA and RT
New settlement and invoicing calendar
New settlement locations (zones, hubs, nodes)
New charge types & bill determinants
Increased credit monitoring

## Slide 23
Submit Parameters
Maintain Model
Retrieve Information
Plan for Operations
Commit Units
Submit Schedules
Submit Bids/Offers
Maintain Outages
Dispatch Units
Provide Telemetry
Control Frequency
Respond to Emergencies
Validate Settlement
Analyze Transactions
4. Impacts to Operations

## Slide 24
4.1 Submit Parameters
QSEs submit resource parameters to ERCOT
Examples include:
  General: HSL, LSL, Type, QF Status, Normal Ramp
  Seasonal: Seasonal MW Rating, Max Weekly Starts
Special parameters for:
  Load Resources, Controllable Load
ERCOT uses parameters in DAM & RUC
Parameters typically do not change
Market Monitor may require documentation

## Slide 25
4.2 Maintain Model
ERCOT implementing a Network Model Management System (NMMS)
Ensures consistency between:
  Annual Planning Models,
  CRR Models, and
  Network Operations Model.
MPs maintain modeling data w/ ERCOT
SPSs/RAPs defined in the Model
Model published on ERCOT MIS in CIM format

## Slide 26
4.3 Retrieve Information
ERCOT upgrading Market Information System
Extensive information available to MPs
  System Conditions (A/S, Forecast, etc.)
  Market Information (DAM, CRR, etc.)
  Clearing Results (Nodal Prices, MCPC, etc.)
Information can be retrieved several ways:
  Online, File Download, Programmatic Interface
Nodal Sandbox environment available

## Slide 27
4.4 Plan for Operations
Resource Plan eliminated
Replaced by Current Operating Plan
Similar time horizon (next 7 operating days)
COP contains additional information
  HSL, LSL, HEL, LEL, A/S Capacity, etc.
QSE must update COP throughout the day
  Cleared awards
  Changes in Resource availability

## Slide 28
4.5 Commit Units
QSEs can still self-commit units
QSEs can also have ERCOT commit units
ERCOT performs commitments during:
  Day-Ahead Market, DRUC/HRUC
ERCOT requires more information
  Startup Costs, Minimum Energy Costs
Incentives exist to allow ERCOT to commit
  Make-whole, Clawback

## Slide 29
4.6 Submit Schedules
Bilateral energy market remains
Scheduling process being replaced
  No more balanced schedules
  No more mismatched schedules
Penalties exist for coming in “capacity short”
ERCOT tracks capacity available through
  Net Capacity Trades
  Net Bilateral Energy Trades
  Net A/S Trades
  Net Energy Purchases

## Slide 30
4.7 Submit Bids/Offers
Important change in jargon:
  In Zonal: You “Bid” to Buy and Sell
  In Nodal: You “Bid to Buy” and “Offer to Sell”
In DA, QSEs can submit bids/offers for:
  Ancillary Services
  Day-Ahead Energy
  Congestion Revenue Rights
In RT, QSE can submit offers for:
  Real-Time Energy
New data structure for all bids and offers

## Slide 31
4.8 Maintain Outages
Outage process largely unchanged
ERCOT serves as coordinator of outages
Leverages Outage Scheduling tool
TSPs & Resource Entities provide ERCOT w/ 12-month outage plan
  Must be updated monthly
ERCOT can reject requests under certain circumstances
Outages must be reflected in COPs

## Slide 32
4.9 Dispatch Units
ERCOT centrally dispatches all resources using new SCED algorithm
Dispatch generates resource base points
Dispatch levels determined by either:
  Energy Offer Curve
  Output Schedule
QSEs must provide new RT telemetry data to ERCOT

## Slide 33
4.10 Provide Telemetry
QSEs/TOs will provide telemetry to ERCOT
Telemetry includes:
  Status of Transmission elements
  Status of Resources, and
  Resource Outputs
Telemetry used in RT Network Security Analysis
Must be updated at a 10s or less scan rate
Need condition detection capability
Must be fully redundant

## Slide 34
4.11 Control Frequency
Enhanced LFC used to maintain frequency
Does not use a cost-optimization function
Executes every four seconds
Provides control signals to each QSE providing Reg & RRS using the ICCP data link or SCADA
QSE provides ERCOT with participation factor every 4s for each resource
RT telemetry used to gather Resource output & actual system frequency
Deployments settled using RT prices

## Slide 35
4.12 Respond to Emergencies
Several conditions may trigger Emergency Condition
  Example: SCED failure
Emergency conditions communicated using:
  Operating Condition Notice, Advisory, Alert, Emergency Notice
During Emergencies, ERCOT may issue a Emergency Base Point
  Resource operating parameters will be honored
EECP Protocol is unchanged*
* Some NPRRs impact EECP

## Slide 36
4.13 Validate Settlements
New set of settlement charges/credits
DAM does not rely on meter data
  Allows for a separate DAM settlement stream
Results in:
  Separate statements
    DA on accelerated timeline; RT on same timeline
  Separate invoices
    DA has daily invoices; RT has weekly
  Separate payment processes
  Separate dispute timelines

## Slide 37
4.14 Analyze Transactions
Important aspect of operations is P&L analysis
  New sources of revenue (DAM Energy Credit, etc.)
  New sources of cost (DAM Make-Whole Charge, etc.)
New cost allocation requirements

## Slide 38
5. Summary
QSE Impacts
Submit Parameters
Maintain Model
Retrieve Information
Plan for Operations
Commit Units
Submit Schedules
Submit Bids/Offers
Maintain Outages
Dispatch Units
Provide Telemetry
Control Frequency
Respond to Emergencies
Validate Settlement
Analyze Transactions
TO Impacts
Maintain Model
Maintain Outages
Provide Telemetry

## Slide 39
Questions
?
?