## Slide 1
Generation Dispatch in a De-Regulated Market
Presented by
Larry Gurley, P.E.

## Slide 2
Introduction
This section on Economic Dispatch is intended to provide the student with a basic understanding of classical economic dispatch theory and how generating units will be dispatched in both the existing ERCOT zonal market and the new ERCOT nodal market.

## Slide 3
Objectives
At the completion of this course of instruction you will:
Summarize economic dispatch principles
Explain how units are dispatched in the current ERCOT zonal market
Explain how units are dispatched in the new ERCOT nodal market
Describe the basis of performance monitoring of generating units in the zonal and nodal market designs.

## Slide 4
Background
Economic dispatch has been around for over 70 years
Theory has not changed; only the way it is applied
Yesterday: done by slide rule
Today: done by high-speed computers
Results are still the same

## Slide 5
Definitions
Unit Commitment – Deciding which units to run
Unit Dispatch – Deciding what MW level to move operating units to

## Slide 6
Definitions
Average Heat Rate – the average amount of fuel used to generate a unit of energy
Incremental Heat Rate – the amount of fuel necessary to generate one additional unit of energy

## Slide 7
Definitions
Average Cost – the average cost to generate a unit of energy
Incremental Cost – the cost necessary to generate one additional unit of energy

## Slide 8
Economic Dispatch
Based only on incremental cost or incremental heat rate (i.e., the cost to produce the next MW of capacity)

## Slide 9
Economic Dispatch - Example
Assumptions:
  Fuel Cost = $1/MMBtu
  Unit A = 100 MW
  Average Cost of Unit A = $11/MW/hour
  Unit B = 100 MW
  Average Cost of Unit B = $10/MW/hour
  Both units currently operating at 50 MW output
Q: Which unit would you dispatch to serve the next MW of load?
A: You don’t know! You need to know the incremental cost of each unit

## Slide 10
Economic Dispatch - Example
Now assume that you know the incremental costs of each unit:
Unit A – Incremental Cost = $9/MW/Hour
Unit B – Incremental Cost = $10/MW/Hour
Q: Which unit would you dispatch to serve the next MW of load?
A: Unit A, because it’s incremental cost is the lowest.

## Slide 11
Unit A
Unit B
Which unit should be dispatched?

## Slide 13
Incremental Heat Rate
Change in MW
Change in
Fuel Burn

## Slide 14
Incremental Heat Rate (or Cost) Curves
Unit A
Unit B
65
83

## Slide 15
The Good Old Days
Utilities operated as “control areas”.
Dispatched units economically within the control area.
Re-calculated economics every 5 minutes.
Re-Dispatched units every 4 seconds using participation factors until new calculation was available.
Manually modified dispatch as necessary to deal with transmission congestion.

## Slide 16
Today’s Zonal Market
QSEs dispatch their resources economically based on their estimate of market prices.
QSEs will buy from the market if prices are lower than their costs or will sell to the market if prices are higher than their costs.
ERCOT operates Balancing Market using economic dispatch theory.
ERCOT manages transmission congestion through Balancing Market and unit-specific OOM deployments.

## Slide 17
Tomorrow’s Nodal Market
Back to the Future!
Dispatch all units economically within ERCOT.
Re-calculate economics every 5 minutes and establish new generator set points.
Re-Dispatch units every 4 seconds.
Automatically (and more precisely) modify dispatch as necessary to deal with transmission congestion.

## Slide 18
Performance Measurement
Uninstructed Deviation
In the Zonal Market: by QSE (i.e., portfolio)
In the Nodal Market: unit-specific

## Slide 19
Summary
Economic dispatch is based on incremental heat rate (or cost), not average heat rate (or cost).
Zonal market dispatch is optimized by QSE portfolio using incremental cost. ERCOT optimizes the balancing market.
Nodal market dispatch is optimized system wide by ERCOT using incremental cost of each unit.
Unit performance changes from portfolio in the zonal market to unit-specific in the nodal market.

## Slide 20
Questions?