## Slide 1: Compliance Registration and Certification
Jeffrey Whitmer
ERCOT Compliance

## Slide 2: Objectives
Correlate NERC functional model to ERCOT market participants.
Identify & register ERCOT market participants.
Describe which entity must obtain NERC organizational certification.
Understand the meaning of responsibility for a NERC function.
State the obligation that comes with registration.

## Slide 3: NERC Reliability Functional Model
The model is a guideline and not a standard.
Framework for the development and enforcement of NERC’s Reliability Standards.
Defines the Functions that must be performed to ensure the reliability.
Defining the Responsible Entities.
Provide for consistency and compatibility among different Reliability Standards.

## Slide 4: NERC Reliability Functional Model (con’t)

## Slide 5: Entity Registration
FERC requires all bulk power system owners, operators, and users to:
  Comply with reliability standards.
  Register with NERC.
  Provide requested information to ERCOT and NERC.
Non-binding Registration List:
  First draft complete and under review.
  Registration finalized once FERC approves NERC standards and rules.
  ERCOT provided notices will be provided to entities being registered.

## Slide 6: Registration Candidates
NERC and the Regional Entity (ERCOT) will:
Identify candidates for registration.
Assign to the compliance registry.
Principles utilize to develop the compliance registry:
NERC/ERCOT must identify the owners, operators, and users who have a material impact on the bulk power system.
Registered Organizations are responsible and will be monitored for compliance with reliability standards.
They will be subject to NERC's and the Regional Entities' compliance and enforcement programs.
Entities can be removed or added depending on the entities material reliability impact.

## Slide 7: Registration Criteria
Determining registration candidates:
Section I determines bulk power system owner, operator, or user.
Section II uses NERC’s current functional type definitions to provide an initial determination of the functional types for which the entities identified in Section I should be considered for registration.
Section III lists the criteria regarding smaller entities.
Section IV lists additional criteria for joint registration.

## Slide 8: Section I – Identify Entities
Entities that use, own or operate elements of the bulk electric system as established by NERC’s approved definition of bulk electric system below are (i) owners, operators, and users of the bulk power system and (ii) candidates for registration:
“As defined by the Regional Reliability Organization, the electrical generation resources, transmission lines, interconnections with neighboring systems, and associated equipment, generally operated at voltages of 100 kV or higher. Radial transmission facilities serving only load with one transmission source are generally not included in this definition.”

## Slide 9: Section II – Assigning Functions
Entities identified in Section I:
Will be categorized as registration candidates.
May be subject to registration under one or more function type based on a comparison of the functions the entity normally performs against the following function:

## Slide 10: Section II – Assigning Functions (con’t)
Function Type | NERC | ERCOT | Definition/Discussion
Balancing Authority | BA | ERCOT | Integrates resource plans ahead of time, maintains load-interchange-generation balance within a BA area, and supports Interconnection frequency in real-time.
Transmission Operator | TOP | ERCOT | Responsible for the reliability of its local transmission system and operates or directs the operations of the transmission facilities.
Reliability Coordinator | RC | ERCOT | The highest level of authority who is responsible for the reliable operation of the bulk power system, has the wide area view of the bulk power system, and has the operating tools, processes and procedures, including the authority to prevent or mitigate emergency operating situations in both next-day analysis and real-time operations. The RC has the purview that is broad enough to enable the calculation of interconnection reliability operating limits, which may be based on the operating parameters of transmission systems beyond any Transmission Operator’s vision.

## Slide 11: Section II – Assigning Functions (con’t)
Function Type | NERC | ERCOT | Definition/Discussion
Transmission Planner | TP | TDSP | Develops a long-term (generally one year and beyond) plan for the reliability (adequacy) of the interconnected bulk electric transmission systems within its portion of the PA area.
Transmission Owner | TO | TDSP | Owns and maintains transmission facilities.
Transmission Service Provider | TSP | ERCOT | The entity that administers the transmission tariff and provides transmission service to transmission customers under applicable transmission service agreements.
Distribution Provider | DP | TDSP | Provides and operates the “wires” between the transmission system and the end-use customer. For those end-use customers who are served at transmission voltages, the Transmission Owner also serves as the DP. Thus, the DP is not defined by a specific voltage, but rather as performing the Distribution function at any voltage.

## Slide 12: Section II – Assigning Functions (con’t)
Function Type | NERC | ERCOT | Definition/Discussion
Load-Serving Entity | LSE | ? | Secures energy and transmission service (and related interconnected operations services) to serve the electrical demand and energy requirements of its end-use customers.
Planning Authority | PA | ERCOT | Coordinates and integrates transmission facility and service plans, resource plans, and protection systems.
Purchasing-Selling Entity | PSE | ? | Purchases or sells and takes title to energy, capacity, and interconnected operations services. PSE may be affiliated or unaffiliated merchants and may or may not own generating facilities.
Resource Planner | RP | ERCOT | Develops a long-term (generally one year and beyond) plan for the resource adequacy of specific loads (customer demand and energy requirements) within a PA area.

## Slide 13: Section II – Assigning Functions (con’t)
Function Type | NERC | ERCOT | Definition/Discussion
Reserve Sharing Group | RSG | NA | A group whose members consist of two or more Balancing Authorities that collectively maintain, allocate, and supply operating reserves required for each BA’s use in recovering from contingencies within the group. Scheduling energy from an adjacent BA to aid recovery need not constitute reserve sharing provided the transaction is ramped in over a period the supplying party could reasonably be expected to load generation in (e.g., ten minutes). If the transaction is ramped in quicker, (e.g., between zero and ten minutes) then, for the purposes of disturbance control performance, the areas become a RSG.
Generator Operator | GOP | QSE Level III - IV | Operates generating unit(s) and performs the functions of supplying energy and interconnected operations services.
Generator Owner | GO | RE | Owns and maintains generating units.

## Slide 14: Section III – Registering Smaller Entities
GO, GOP, DP, TO, TOP or LSE should be registered if they meet any of the criteria listed below:
Generator Owner/Operator:
Individual generating unit > 20 MVA and is directly connected to the bulk power system.
Generating plant/facility > 75 MVA.
A blackstart unit.
Any generator that is material to the reliability of the bulk power system.

## Slide 15: Section III – Registering Smaller Entities (con’t)
Distribution Provider:
System serving >25 MW of peak load
Registered entity that owns, controls, or operates facilities that are part of any of the following protection systems or programs designed, installed, and operated for the protection of the bulk power system:
- a required UFLS program.
- a required UVLS program.
- a required special protection system.
- a required transmission protection system.

## Slide 16: Section III – Registering Smaller Entities (con’t)
Transmission Owner:
Owns an integrated transmission element associated with the bulk power system 100 kV and above.
An entity that owns a transmission element below 100 kV associated with a facility that is included on a critical facilities list that is defined by the ERCOT.

## Slide 17: Section III – Registering Smaller Entities (con’t)
Joint Registration Organization and
Member Registration:
NERC provided for the ability to register Joint Action Agencies and Generation and Transmission Cooperatives on behalf of their members.

## Slide 18: Section III – Registering Smaller Entities (con’t)
Load-serving Entity:
Peak load is > 25 MW
Connected to the bulk power (>100 kV) system.
Required for underfrequency load shedding (UFLS) program.
Required for undervoltage load shedding (UVLS) program.

## Slide 19: ERO Organization Registration
Registration process:
  Entities may request specific registration function type.
  ERCOT or NERC may add to the registration list.
  Others may nominate those with material impact for registration.
Entity may challenge compliance registry:
  Demonstrate why it is not a bulk power system owner, operator, or user.

## Slide 20: Entity Registration
The ERCOT ISO is registered for the following NERC functions:
  Reliability Coordinator (RC)
  Transmission Operator (TOP)
  Balancing Authority (BA)
  Planning Authority (PA)
  Transmission Service Provider (TSP)
  Resource Planner (RP)
Some of the Standards Requirements for the above functions will be delegated by the ERCOT ISO to other ERCOT entities such as QSEs and TDSPs

## Slide 21: Entity Registration
Other ERCOT Entities have been registered as:
  Transmission Owner (TO) (+100kV)
  Transmission Planner (TP) (+100kV)
  Generator Owner (GO)
  Generator Operator (GOP) (QSEs with Resources)
  Distribution Provider (DP) (DP with primary responsibility of under-frequency and/or under-voltage load shedding)
The Texas RE Compliance Draft Registry is posted on the ERCOT Compliance Web Site at…
http:/www.ercot.com/mktrules/compliance/nerc/index.html

## Slide 22: Who is Registered?
Solid Red = ERCOT
Dotted Yellow = Market Participants

## Slide 23: Entity Certification
NERC shall provide for certification of all entities with primary reliability responsibilities established in the NERC Reliability Standards.
The NERC Program shall:
  Evaluate and certify the competency of entities performing reliability functions.
  Certify each entity’s ability to meet the minimum requirements established by the NERC Reliability Standards for each function.
  Maintain documentation and records of currently certified entities.

## Slide 24: Entity Certification
Entities currently expected to be certified:
Reliability Coordinators.
Transmission Operators.
Balancing Authorities.
Other entities may be added as required by approved Standards.

## Slide 25: What’s Next?
ERCOT continue efforts to complete preliminary registration.
Transitional Process:
  Use the Existing Control Area Certification Procedures.
  Existing Control Areas.
    Can receive initial certification as control area.
      Control area recertification procedures.
      Readiness audits.
    Focus on responsibilities identified in reliability standards.

## Slide 26: Continuing Programs
Reliability assessments.
Reliability readiness.
Training and education.
System personnel certification.
Situation awareness and infrastructure security.
Event analysis and information exchange.

## Slide 27: Compliance Registration Timeline
March 2007
ERCOT submits final draft regional registration lists to NERC (March 2).
NERC reviews and assembles proposed registration list and provides to ERCOT.
ERCOT Compliance and NERC staff meet to confirm proposed registration list.
NERC posts proposed registration list.
April 2007
Registered entities are notified of proposed registration.
Registered entities have 21 days to appeal.

## Slide 28: Compliance Registration Timeline (con’t)
April 2007
NERC meets with industry trade associations and stakeholders to discuss the proposed registration list.
NERC Director of Compliance rules on objections.
Registered entity has 21 days to file appeal.
May 2007
NERC Compliance Committee decides appeals.
Registered entity may seek review by applicable governmental authority.
Reliability Standards Approval (Future)
NERC provides registration list for applicable entities to FERC.

## Slide 29
Questions
Jeff Whitmer
Reliability Engineer
ERCOT Compliance
7620 Metro Center Dr
Austin, TX 78744
(512) 225-7030
Email: jwhitmer@ercot.com