## Slide 1: Congestion Management Work Group Update
Presented to WMS 5-21-08
Isabel Flores, ERCOT
Marguerite Wagner, PSEG

## Slide 2: April/May Work Summary
Progress Report
Met 4/28, 5/9, 5/19
Discussed
  Process for CCT
  Development of Maximum SP Cap
  Outage Evaluation Process

## Slide 3: Process for CCT
ERCOT received CCT as part of 4/22 MMS “code drop” from ABB—are evaluating tool
On 5/19, CMWG group agreed that CRR models should be used as basis for CCT
Goal that CCT be done prior to CRR auctions so that CRR purchasers know which constraints will be deemed as competitive
Tentative Timeline for January CRR auction
  Competitive Constraints determined by 10/30/08 so that they can be emailed out to tAC
  Approved at TAC Nov 6
  CCT and Network model ERCOT will use in CRR allocation to be posted on 11/7
  PCRR requests submitted on 11/12
  ERCOT posts PCRR allocations and McFRIs on 11/20
  CRR auction submissions 12/8-10
  CRR Auction Results posted on 12/15
ERCOT working on more definitive calendar

## Slide 4: How Competitive Constraints are used in SCED
Step 1: execute the SCED process to determine Reference LMPs. In this step ERCOT executes SCED using the full Network Operations Model while only observing limits of Competitive Constraints. Energy Offer Curves for all On-Line Generation Resources, whether submitted by QSEs or created by ERCOT under this section are used in the SCED to determine “Reference LMPs.”
Step 2: execute SCED to produce Base Points, Shadow Prices, and LMPs, subject to Competitive and Non-Competitive Constraints and other Resource constraints. The second step must:
  Use Energy Offer Curves for all On-Line Generation Resources, whether submitted by QSEs or created by ERCOT. Each Energy Offer Curve must be capped at the greater of the Reference LMP (from Step 1) at the Resource Node or the appropriate Mitigated Offer Cap and bounded at the lesser of the Reference LMP (from Step 1) at the Resource Node or the appropriate Mitigated Offer Floor; and
  Observe all Competitive and Non-Competitive Constraints.

## Slide 5: Development of Maximum SP Cap
Discussed:
  Constrain SCED solution based on shift factor impact and amount market is willing to spend to solve the constraint
  SP Caps based on constraint type and Generic Offer Caps
  ERCOT evaluating tiered process where degree of violation determines the SP cap

## Slide 6: Timeline/Upcoming
For CCT: clarifying language in Go-Live document to capture the fact that since there is no annual CRR auction at go live, TAC approved Competitive Constraints are not required for December 2008
For SP Cap: Striving to have proposal to WMS in June so that can go to July PRS and August TAC and be used in 168 hour test

## Slide 7: Outage Evaluation
Presentation from ERCOT about outage evaluation processes in ISO-NE, & PJM
Discussion
  ERCOT has more outages than other ISOs and controls to lower kV level
  Limited coordination role and limited communications between TOs, Resource Entities
  Is there a way to improve what we have—discussion tentatively to occur 6/13

## Slide 8: Upcoming Meetings
6/10 Continue SP discussions
6/13 Outage Timing/Notification (possible agenda change to SP discussions depending on 6/10 outcome)
6/19 Finalize SP discussions