## Slide 1: PROPOSAL FOR ACHIEVING ZONAL PRICES THAT DO NOT EXCEED THE OFFER CAP
By
Dr. Shmuel Oren
June 13, 2008

## Slide 2: The Objective
Keeping the MCPE from exceeding the Offer Cap when single line congestion or simultaneous congestion on multiple zonal constraints occurs
Under the proposed Two-Step procedure: Offers that raise the zonal MCPE above that offer cap are identified and cannot set the price

## Slide 3: Two-Step Procedure : Step One
In each zone, add a resource (a virtual load response) at the offer cap + $1 per MWh, currently $2,251.
The virtual resource has unlimited capacity.
Run SPD and solve the optimal dispatch LP.

## Slide 4: Step One Result
Any offer that would result in raising the zonal MCPEs above the offer cap will be rejected, as it will be dominated by the local virtual load response offer.
This first run sets the MCPE in each zone, based on,
  The highest offer accepted, or
  The virtual load response offer ($2,251)

## Slide 5: Step Two
A second run solves without the virtual load response offers.
Resources procured in Step Two (but that were rejected in Step One) are paid as bid and do not participate in the zonal price setting.
This approach will produce the same results as the shadow price cap when only one CSC is congested (assuming the correct shift factor is used)
This approach will also work whenever there is simultaneous congestion on multiple constraints with no need for ex post adjustment.

## Slide 6: EXAMPLE OF SECURITY CONSTRAINED ECONOMIC DISPATCH
Zone
1
Zone
2
Zone
3
Load = 1000MW
No Generation
$/MWh
200
MW
1000
Gen Offers
$/MWh
500
500
Gen Offers
150
MW
All lines
same impedance
600MW flow limit
2000
200
800
16.7
50
533.3
16,3
50
267.3
267.3
100
33.3
LINE 2 to 1 IS CONGESTED
Total Flow = 600MW
Serving 1 more MW at Zone 1 without overloading line 2 to 1 requires
DEC of 1 MW from Zone 2 and INC of 2MW from Zone 3 at total net cost
2X2000 – 1X200 = $3800 = > Zone 1 MCPE = $3800
By same rational Zone 2 MCPE = $200 and Zone 3 MCPE = $2000.

## Slide 7: EXAMPLE OF SECURITY CONSTRAINED ECONOMIC DISPATCH WITH VIRTUAL LOAD RESPONSE (VLR)
Zone
1
Zone
2
Zone
3
Load = 1000MW
No Generation
$/MWh
200
MW
1000
Gen Offers
$/MWh
500
500
Offers
150
MW
All lines
same impedance
600MW flow limit
2000
825
50
550
50
275
275
100
LINE 2 to 1 IS CONGESTED
The Economic dispatch algorithm will reject the $2000 offer from Zone 3
and instead dispatch another 25MW from Zone 2 at $200 and make up
the difference of $25 MW with VLR at $2251 from zone 1. The resulting
MCPEs for Zone 1 = $2251, Zone 2 = $200, Zone 3 = $500.
In step 2, the rejected 50 MW at $2000 are procured and paid as bid.
Offers
25
MW
2251
2251
VLR
VLR
2251
VLR

## Slide 8: Question No 1
Can the virtual resource offer set the price at $2251 if there is no zonal congestion?
Yes, if there is no zonal congestion but all dispatchable offers are deployed (i.e. there is systemwide shortage), the virtual resource could still set the MCPE in all zones.
Solution: when there is no congestion, and MCPE in all zones is $2251 we can set the MCPE in Step Two to the marginal offer.

## Slide 9: Question No. 2
Does the proposal eliminate the shadow price cap?
Answer: Under the proposal, a shadow price is no longer needed since we assume unlimited demand response at $2251.
A shadow price cap assumes instead unlimited counterflow at the cap, which is equivalent to our method if only one line is congested but does not generalize to multiple congested lines.