## Slide 1: WMS Report To TAC
September 2008

## Slide 2: In Brief
Four Working Group Reports
One Task Force Report
Three Staff reports

## Slide 3: Working Group Reports DSWG
Price Responsive load and RUC
Energy Efficiency Project #27647
NPRR with Zero Floor on RRS
Notes: DSWG has taken up the subject of Price Responsive Loads and RUC. The underlying theory is that if prices are high at times of scarcity, Price Responsive Loads won’t be there. This project is still underway and no action was requested from WMS however, members of WMS were interested and asked in particular that the final product address concerns about how DA RUC produces costs and how those should be addressed.
The Commission formed a subcommittee for their Energy Efficient Project #27647
Subcommittee Mission Statement: Encourage the collaborative development and deployment of cost effective Load Management programs in order to meet the needs of Texas’ energy consumers, within the guidelines of Texas’ energy efficiency rule.
One of the companies active in the DSWG is making a report to the subcommittee and asked for and received input from the DSWG as part of the collaborative effort.
The issue of negative bids by LaaRs for RRS has been the topic of much discussion. Two potential long term solutions have been vetted and brought to TAC only to be rejected here. The advocates for both solutions agree that a Zero Floor, as we have now, is the only solution that can be in place for Nodal go live and thus, at the request of the WMS chair, an NPRR to that effect has been prepared and is now in the pipeline.

## Slide 4: Working Group Reports QSEWG
NERC audit of ERCOT scheduled for September 8-11, 2008
NERC EOP and its Sub-requirements
WGRPP Forecast issues
WGR only QSE Performance Metrics
Notes: NERC audit of ERCOT scheduled for September 8-11, 2008
Balancing Authority tasks delegated to QSE’s
Three NERC Standards provided by ERCOT (see three Rs Below)
QSEWG determined current procedures have us covered and no further action was required
R3.4. - Develop, maintain, and implement a set of plans for system restoration.
R7.3. - The Transmission Operator and Balancing Authority shall coordinate transmission and generator maintenance schedules to maximize capacity or conserve the fuel in short supply. (This includes water for hydro generators.)
R7.4. - The Transmission Operator and Balancing Authority shall arrange deliveries of electrical energy or fuel from remote systems through normal operating channels.
WGRPP
There was concern expressed about the use of e-mail which is a non-secure system, for operational purposes. The only other option is the nodal xml systems, which are in test mode and also not production quality. At least one member stated that there support for PRR763 was based on the assumption that e-mail was a first step and NOT to be the end product.
WGR only QSE Performance Metrics
There was concern expressed at the WMS that the formulation of metrics was ahead of the formulation of procedures. It was asked that ERCOT be more clear about what it wants before participates are graded on how well they are doing it. No action was taken by WMS.

## Slide 5: Working Group Reports VCWG
VC Manual and white paper
Emissions credits
Implementation Plan
NPRRs 144 (5 RUC) and 145(PPAs)
FIP analysis
Notes: The VCWG has been working very hard and has met several times working through the VC manual and white paper which have been approved by WMS, but are probably still changing and will have more approvals as they do.
There is a consensus that Emissions credits have value and more work is being done on that
ERCOT staff reports that it will take 5 to 7 months to grind through submissions and is concerned with how to manage that body of work. After an initial effort to get WMS action on the Implementation Plan it was decided that it was more in the purview of TPTF than WMS and has been turned over. TPTF decided not to decide until more is known about the schedule.
NPRRs have been produced and are now in the pipeline. Comments have been received on NPRR 145 and PRS has asked for a resolution from the working group.
Work is continuing on the FIP analysis and WMS input will be requested at our next meeting.

## Slide 6: ERCOT Staff Reports
Market Credit Risk Standard – Update
Procedures for Identifying Resource Nodes
OOMC/OOME Deployments and Costs
Notes: Market Credit Risk Standard – Update
Cheryl Yager presented on the need for a Market Credit Risk Standard
The document is out for comment and will be considered at our next meeting.
The document is just a requirement to report credit risk on quarterly basis.
phase 2 Will provide teeth.
Nodal: Procedures for Identifying Resource Nodes
There is little guidance in the Nodal Protocols on how to define the Resource Nodes. ERCOT needs some written direction. The document Kenneth put forth started with the work of the Hi/Low task force with some gaps filled in. It has been reviewed and approved by TPTF, and WMS approved it as well.
OOMC/OOME Deployments and Costs
A question was raised regarding the amount of ERCOT deployment and its impact on market prices. Staff’s ability to anticipate questions and respond was limited due to staff limitations and work going into CSC determination. Input was received from WMS and we will continue to review.

## Slide 7: CCR Credit Policy TF
NPRR140 Revision to CRR Obligation Margin Adder
Other Market Concerns
Notes: CCR Credit Policy TF – NPRR 140Greer – Clayton deferred presentation to next month on the Obligation adder. The draft is proposing that our current $10 value be changed to 3 X NYISO which comes out to about $2.5
Randa discussed some Market Concerns and a desire to further efine:
Daily Credit Calculations
The Low Risk Market Player
The High Risk Market Player
Near Term Credit Solutions
Long Term Credit Solutions
No WMS action was taken and an NPRR is anticipated soon.

## Slide 8: Working Group Reports CMWG
SP Cap recommendation status
Outage Evaluation
Competitive Constraint Test
CSC discussion and action
Notes: Wagner summarized status of SP Cap recommendation
Outage Evaluation
Competitive Constraint Test
IMM – “didn’t pass the test” rather than
Wagner – agreed
Greer – do we need a different test?
IMM – not really determined that is wasn’t competitive, but how used in the market. “Didn’t pass the test to be a Competitive Constraint” not that it wasn’t competitive.
Belk – would we allow it to roll forward to nodal?
IMM – you could approve something that didn’t pass.
Belk – may have been competitive in zonal, but not nodal.
Greer – is the bar too high?
IMM – we know the bar is not right, but a good effort at a test, and there are exceptions, not proposing a mechanical change.
Belk – we are about to over-write this with 2009 CSCs
Greer – this was to get list beyond CSCs, hopefully hundreds of lines.
Wagner – look forward to ERCOT update.

## Slide 9: SP Cap Progress & Recommendation
CMWG Recommendation: Proceed to Implement Existing System Capabilities
3/08 Directed by WMS to look at SP issue
4/08 ERCOT proposal, SP cap by kV level
5-6/08 Alternate proposal for penalties based on degree of constraint violation
5-6/08 Comments on ERCOT Proposal & Discussion of Alternate Proposal
7/08 CMWG: Implement Existing Sys Capabilities
7/08 Clarification on MMS Capabilities
8/27 CMWG: Discuss SP Cap Number

## Slide 10: Working Group Reports CMWG
SP Cap recommendation status
Outage Evaluation
Competitive Constraint Test
CSC discussion and action
Notes: Outage Evaluation
This topic came up as a result of a great deal of congestion in the West and was labeled a “wind” issue. ERCOT staff put in a lot of work and developed a concept paper that expanded the topic to all outages. WMS discussion confirmed the working group conclusion that the full potential of the concept was simply not achievable with our current resources at this stage of the nodal development and that partial or flawed implementation posed sever risk to individual market participants. It is disappointing to many as there is clearly a very large amount of money that could be saved with an improved coordination system and the CMWG was asked again to review the narrower scope of the “wind” issue, however, we were reminded that there is other generation in the west and that clearly that label and limit was not appropriate. The CMWG was asked to narrow the scope to Low Hanging Fruit and see if there was something simple and low risk that could be done that might help avoid the big screw ups.
Competitive Constraint Test
Evaluated 2008 CSCs and found some that did not pass the test
  CSCs that failed have not yet been presented to CMWG
  ERCOT following up to identify the various definitions of "decision-making entity,” operator, etc. to compare and contrast the use so that MPs can clarify how ERCOT is to interpret “decision-making entity” for purposes of CCT evaluation

## Slide 11: 2009 CSCs
What’s not changing?
  General the geographic regions are stable: West, North, South, Houston
What is changing?
  CSC definitions
For N_H, Singleton is not scheduled to be in-service until May 2009

## Slide 12: 2009 CSCs
CSC | Scenario 3b | Scenario 3g | Scenario 3h
N_H* | Singleton-Obrien/ Singleton-TH Wharton 345-kV double circuit | Singleton-Obrien/ Singleton-TH Wharton 345-kV double circuit | Singleton-Obrien/ Singleton-TH Wharton 345-kV double circuit
N_S & S_N | Lake Creek-Temple/ Tradinghouse-Temple Pecan Creek 345-kV double circuit | Lake Creek-Temple/ Tradinghouse-Temple Pecan Creek 345-kV double circuit | Lake Creek-Temple/ Tradinghouse-Temple Pecan Creek 345-kV double circuit
W_N & N_W | Graham-Benbrook/ Graham-Parker 345-kV double circuit | Graham-Long Creek/ Graham-Cook Field Road 345-kV double circuit | Sweetwater-Long Creek/ Abilene Mulberry Creek-Long Creek 345-kV double circuit
Notes: Talk about N-H and the midyear name change
Talk about the N-S and S-N moving north to better control N-S congestion
Note that the difference in the three scenarios is the W-N and N-W choice of CSCs.
All three choices are in a line running east west on which there is ongoing new construction of wind and changes in configuration last June.
The Scenarios unfortunately named 3b, 3g, and 3h represent different sections of the line with
3b being the most eastern and unchanged from 2008.
3g is the center section and results in some load and generation moving from West to North
3h is the western section and results in more generation moving from West to North
Presentations were made on the merits of all three and three motions were made at WMS
the first for 3b, which failed by a narrow margin. (43% to 57%)
The second motion was for 3g and it failed to get a second.
The third motion was 3h and it passed by a narrow margin. (61% to 69%)

## Slide 13: Two kinds of constraints
It is generally understood that the western most CSC (3h) will probably result in easier operations for thermal constraints.
It is generally understood that the eastern most CSC (3b) will probably result in easier operations for stability constraints.
ERCOT can reliably manage either option, but has indicated they are less comfortable with the amount of generation that option 3h moves from West to North.
Notes: WMS was clearly divided between the Eastern most option, 3b and the Western most option 3h.
I will talk a little more about them.

## Slide 14: Benefits of Scenario 3b
Provides Market Stability:
CSC for W-N and N-W has been 345kV double circuit Graham-Parker/Graham-Benbrook since inception of ERCOT Zonal Market
Changing the CSC will re-cluster 785MW (20% of total) West zone load into North zone, BUT this load will move back to the West upon Nodal Market implementation per nodal protocols 4.1-4.2.

## Slide 15: Benefits of Scenario 3b
Ensures Robust Competitive Solution for Resolution of N-W Congestion
Scenario 3h moves 33% of scheduled (non-wind) resources from the West to the North:
  Oklaunion 649 MW
  Graham 611 MW
  North DC Tie 220 MW
  Wichita Falls 77 MW
  Morris Sheppard 24 MW
Of the remaining scheduled West zone resources, Luminant will own 54% of the capacity.

## Slide 16: Benefits of Scenario 3h
W-N transmission topology for 2009 was reconfigured on June 3, 2008 with the completion of the Long Creek substation, significantly changing flows on both the east side & west side of Long Creek.
As a result of this topology change, thermal congestion since June 3 has been primarily on Abilene Mulberry Creek – Long Creek.

## Slide 17
On June 3 W-N transmission topology significantly changes
Configuration before June 3
Configuration after June 3
Note increase after June 3
Note flows equalize after June 3
Long Creek Substation was looped into Sweetwater Cogen - Graham 345 kV line on June 3, 2008. This change 1) equalized flows on Graham – Long Creek circuits #1 and #2, 2) increased the flow on the Mulberry Creek – Long Creek, and 3) exacerbated the congestion on the Mulberry Creek – Long Creek.

## Slide 18
Historical cost is highest along Mulberry Creek – Long Creek
Source: Congestion charges from ERCOT website
Proposal 3h accounts for 75% of all congestion since June 3.
Notes: The transmission configuration changed on June 3rd and the pattern of thermal problems changed.
After June 3rd, there were 23 days of congestion.
13 of those days the line chosen as the CSC in option 3h was binding.
6 of those days the line chosen as the CSC in option 3b was binding.
And
3 of those days there was a stability limit.

## Slide 19: WMS Report To TAC